## Slide 1: Sterilization methods and equipment
PHT 434

## Slide 2: Sterilization concept
Sterilization is essential concept in the preparation of sterile pharmaceutical products .
Its aim is to provide a product that is safe and eliminates the possibility of introducing

## Slide 3: Sterilization
Sterilization –a process that by which all viable M.O are removed or destroyed , based on a probability function .

## Slide 4: Method of inactivating M.O may be classified as either :
1.Physical
A. moist heat
b. dry heat
c. irradiation
d. sterile filtration is another process , but it only removes , not inactivates M.O

## Slide 5: Method of inactivating M.O may be classified as either :
2. Chemical
a. Gaseous
b. Liquid sterilants

## Slide 6: Sterilization methods

## Slide 7
Method | Equipment
Thermal | 
Moist heat sterilization | Saturated steam autoclaves Superheated water autoclaves Air over steam autoclaves
Dry heat sterilization | Batch sterilizers Continuous tunnel sterilizers
Non- thermal | 
Chemical cold sterilization | Ethylene oxide Vaporized hydrogen peroxide Hydrogen peroxide/steam Other gases
Radiation sterilization | Electromagnetic Particulate
Filtration | Membranes

## Slide 8: Thermal sterilization
Involves the use of either moist or dry heat.
Moist –heat sterilization is the most widely used and reliable sterilization method.
Dry – heat sterilization is appropriate for materials that cannot withstand moist – heat sterilization

## Slide 9: 1-Moist –heat sterilization
  Microorganism are destroyed by cellular protein coagulation .
  The objects to be sterilized are exposed to saturated steam under 1 atmosphere pressure at a minimum temperature of 121°C for at least 20-60 minutes.
  An autoclave is commonly used for moist – heat sterilization .
  Because it does not require as high a temperature, moist – heat sterilization cause less product and equipment damage compared to dry – heat sterilization .

## Slide 10: Autoclaves
Is a device to sterilize equipment and supplies by subjecting them to high pressure saturated steam at 121 °C or more, typically for 15-20 minutes

## Slide 11: Autoclaves types
Portable autoclave (bench autoclave)
Stationary autoclave (large steriliser)
      For porous loads e.g., dressing
      For bottled fluids

## Slide 12: Portable autoclave (bench autoclave)

## Slide 13: Stationary autoclave (large sterilizer)

## Slide 14: Main features of autoclave ( * )
Lid(door) fitted with clamps and asbestos jacket , stationary autoclave may be double doors at both ends one for loading and one for unloading.
Pressure gauge
Thermocouple for measurement of temp. usually located within the discharge channel in dummy article .
Air vent to remove air before sterilization .

## Slide 15: Main features of autoclave
5. Safety valve to permit escape of excess steam to prevent explosion .
6. Modern autoclaves are recording (record pressure, temp during the whole process ) supplied with timer and are automatically controlled .

## Slide 16: Advantage of jacket autoclave
Rapid in operation as steam is stored in the jacket .
More economic as steam is trapped in the jacket and not allowed to escape into the atmosphere.
Load comes out dry as the inner surface is always warm.

## Slide 17: Operation of the autoclave
Articles to be sterilized are placed in baskets or cylinders.
Door is closed and clamped
Heating is started and steam is generated
Air vent is closed after complete removal of air (noticed by continues and vigorous flow of steam from the air vent .
When pressure reached that required 1 atm , 121 C , sterilization period is timed .

## Slide 18: Operation of the autoclave
6. At the end of the period , heat is disconnected .
7. Autoclave should be not opened before pressure is fallen down.

## Slide 19: Air must be removed from autoclave
Because :
It reduces the penetration of steam especially with decreasing .
It cause superheating in stationary autoclaves.
In temp. controlled autoclaves explosion may occur.

## Slide 20: 2-Dry – heat sterilization
Is appropriate for materials that cannot withstand moist – heat sterilization (e.g., oily materials and powders) .
Objects are subjected to a temperature of at least 160 °C for 120 minutes ( if higher temperatures can be used , less exposure time is required).

## Slide 21
Non- Thermal method

## Slide 22
Method | Equipment
Non- thermal | 
Chemical cold sterilization | Ethylene oxide Vaporized hydrogen peroxide Hydrogen peroxide/steam Other gases
Radiation sterilization | Electromagnetic Particulate
Filtration | Membranes

## Slide 23: 1-Chemical ( gas ) sterilization
  Is used to sterilize surfaces and porous materials ( e.g., surgical dressings ) that other sterilization methods may damage .
        In this method , ethylene oxide is used generally in combination with heat and moisture .
        Residual gas must be allowed to dissipate after sterilization and before use of the sterile product .

## Slide 24: 2-Radioactive sterilization
Is suitable for the industrial sterilization of contents in sealed packages that cannot be exposed to heat ( e.g., prepackaged surgical components , some ophthalmic ointments ) .
    This technique involves either electromagnetic or particulate radiation .
    Accelerated drug decomposition sometimes results.

## Slide 25: 2-Radioactive sterilization
Principles :
  Accelerated electrons ( particulate radiation ).
  Gamma – rays and ultraviolet (UV) light (both electromagnetic radiations).
Target :
      Microbial DNA

## Slide 26: A- electromagnetic radiations
Ultraviolet (UV) light
  Less damaging and less lethal to M.O
  Not efficient method
  Less use due to , poor penetration
Gamma – rays ( ionising radiations )
  Ionizing – radiations cause both excitation and ionization of atoms of different molecules in M.O
    Diredct action (Target theory )
    Indirect action
  Decrease M.O resistance
  Efficient method

## Slide 27: B- particulate radiation
Two types of electron accelerator machine :
  Electrostatic accelerator .
  Microwave linear accelerator.

## Slide 28: 3-Mechanical sterilization (filtration)
Removes but does not destroy microorganisms and clarifies solutions by eliminating particulate matter.
For solutions rendered unstable by thermal, chemical, or radiation sterilization, filtration is the preferred method .
A depth filter or screen filter may be used .

## Slide 29: Mechanical sterilization (filtration) cont
Depth filter usually consist of fritted glass or unglazed porcelain (i.e., substances that trap particles in channels ).
Screen (membrane) filters are films measuring 1-200 mm thick made of cellulose esters, microfilament, polycarbonate , synthetics polymers, silver, or stainless steel.

## Slide 30: Mechanical sterilization (filtration) cont
  Screen (membrane) filters
    A mesh of millions of microcapillary pores of identical size filter the solution by a process of physical sieving .
    Flow rate .because pores make up 70 % to 85% of the surface , screen filters have a higher flow rate than depth filters.

## Slide 31: Mechanical sterilization (filtration) cont
  Types of screen filters
    Particulate filters
    Microbial filters
    Final filter

## Slide 32: 1-Particulate filters
Remove particles of glass, plastic, rubber, and other contaminants .
              Other uses . these filter also are used to reduce the risk of phlebitis associated with administration of reconstituted powders. filtration removes any undissolved powder particles that may cause venous inflammation.

## Slide 33: 1- Particulate filters (cont)
The pore size of standard particulate filters ranges from 0.45-5mm .
Special particulate filters are required to filter blood, emulsion (e.g., fat emulsion), or colloidal dispersions or suspensions because these preparation have a larger particle size.

## Slide 34: 2- Microbial filters
    With a pore size of 0.22 mm or smaller, ensure complete microbial removal and sterilization .
    This is referred to as cold sterilization .

## Slide 35: 3- Final filter
    Which may be either particulate or microbial , are often included as part of the tubing used in drug administration .
    They are referred to as in – line filters and are used to remove particulates or microorganisms from an intravenous (IV) solution during infusion .