## Slide 1
BCH 312 [PRACTICAL]
Identification of the common laboratory glassware, pipettes and Equipment .

## Slide 2
Objective:
-To be familiar with most used tools in biochemistry labs.

## Slide 3
(1)Identification of the common laboratory glassware :
A- Conical flasks and beakers:
They are used for mixing, transporting and reacting, but not for accurate volume measurements.
Conical flasks
Beaker
[Ehrlenmeyer]

## Slide 4
B- Graduated cylinders [measuring cylinder ]:
-Used to measure the volume of a liquid. Graduated cylinders are generally more accurate and precise than laboratory flasks and beakers.
-If greater accuracy is needed, use a pipet or volumetric flask.
Graduated cylinders

## Slide 5
C- Volumetric flasks:
It is used to make up a solution of fixed volume very accurately.
Volumetric flasks

## Slide 6
D- Burettes :
A burette delivers measured volumes of liquid. Burettes are used primarily for titration.
Burette

## Slide 7
Are Tools commonly used to transport a measured volume of liquid. Pipettes come in several designs for various purposes with differing levels of accuracy and precision.
E- Pipettes:
There are two main type of pipettes are used in biochemical laboratory:
(a)Volumetric or transfer pipettes.
(b)Graduated or measuring pipettes.

## Slide 8
Pipettes

## Slide 9
There are two main type of pipettes are used in biochemical laboratory:
(a)Volumetric pipettes. [transfer ]
(b)Graduated pipettes. [measuring]
• Are designed to deliver accurately a fixed volume of liquid.
• More accurate than measuring pipettes.
• Not graduated.
• consists of a cyclindrical bulb joined at both ends to narrowed glass tubing.
•Graduated.
•Some are blown out.
•There are two types: Mohr and serological
•Non-blown out.

## Slide 10
(a)Volumetric pipettes. [transfer ]
(b)Graduated pipettes. [measuring]
Mohr pipette
Serological pipette

## Slide 11
Smallest division of graduated pipette:
1ml
10
= 0.1 ml
1 ml
2
= 0.5 ml

## Slide 12
Steps of the Use of the pipettes:
-The pipette is first washed with water ,then rinsed several times with a little of the solution to be used and finally filled to just above the mark , the liquid is allowed to fall to the mark .
The solution is allowed to drain into the appropriate vessel with the jet of the pipette touching the wall of the vessel .
After the flow of the liquid has stopped, the jet is held against the wall for some times and then removed . A certain amount of liquid will remain at the tip and this must not be "blown out".

## Slide 13
(2) Identification of the common laboratory Equipment:
(A)Balance.
(B) pH meter.
(C) Spectrophotometer.
pH meter

## Slide 14
•Hydrogen ion concentration of many solution is low and difficult to measure accurately.
•So, the term pH introduced as a way of expressing hydrogen ion concentration .
•PH define as the negative logarithm of the hydrogen ion concentration .
•PH = - log10 [H+]
•Since the PH determines many important aspects of the structure and activity of biological macromolecules and thus of the behavior of the cell and organisms .
• Note: PH range value (0 - 14) ,, the higher PH number , the lower the hydrogen ion concentration and vice versa..
pH meter:
• A pH meter is an electronic device used for measuring the pH (acidity or alkalinity) of a liquid.

## Slide 15
•There are many ways in biochemical laboratory to measure PH value such as ; and
•litmus s paper,
• a field kit
• PH meter. The most accurate and reliable method is
Note: before use it needs to be calibrated
The glass electrode

## Slide 16
Using a pH Meter
https://www.youtube.com/watch?v=vwY-xWMam7o

## Slide 17
• Spectrophotometer is instrument used to measure the intensity of light at a given wavelength that is transmitted or absorbed by a sample.
Spectrophotometer
-Invisible range(ultraviolet) from 100 to 360 nm [Quartz cuvette are used]
-Visible range (above 360 nm -700 nm) [Glass or plastic cuvette are used]
• Blank : contain everything except the compound to be measure.
• Wavelength in this instrument divided into:

## Slide 18
The spectrophotometer: it can be used to measure the amount of light absorbed by a solution.
-By using the spectrophotometer, we can quantitatively measure absorbance, and this information can be used to determine the concentration of the absorbing molecule.
-More concentrated solution will absorb more light and transmits less.
So, the more concentrated solution  high absorbance value.
And Less concentrated solution  less absorbance value.

## Slide 19
How a spectrophotometer works

## Slide 20
How a spectrophotometer works

## Slide 21
http://www.youtube.com/watch?v=pxC6F7bK8CU
How does a spectrophotometer work?