## Slide 1: Scanning spectrophotometry and spectrophotometric determination of concentration
BCH 333 [practical]

## Slide 2: Objectives:
1. What is absorption spectrum and determination of λmax.
2. standard curve and determination of concentration of an unknown solution.

## Slide 3
How a spectrophotometer works

## Slide 4
The spectrophotometer: it can be used to measure the amount of light absorbed by a solution. How?
-Using the spectrophotometer, we can quantitatively measure absorbance, and this information can be used to determine the concentration of the absorbing molecule.
-A more concentrated solution will absorb more light and transmits less .[why?]
So, the more concentrated solution  high absorbance value.
And Less concentrated solution  less absorbance value.

## Slide 5
Absorption spectrum:
The curve that display the action or behavior of absorption of molecule[solute] at different weave lengths. Every molecule has its own Absorption spectrum, So it’s act as fingerprint for each molecule.
λmax: it is the weave length at which the molecule has the maximum absorbance at this weave length.[best absorbance]
[the wavelength of maximum absorption (λmax)]

## Slide 6
Absorption spectrum curve and determination of λmax.

## Slide 8
What is the benefit of studying the Absorption spectrum :
λmax.
used to identify substances.
It also can be used to know if there is any contamination with another molecule.

## Slide 9
http://www.youtube.com/watch?v=pxC6F7bK8CU
How does a spectrophotometer work?

## Slide 10
Beer-Lambert law:
Principle:
The absorption of light by a solution is described by the Beer-Lambert law:
The law implies that there is linear relationship between absorbance and concentration of an absorbing species.
A = εlc
A= is the absorbance.
ε = extinction(absorption) coefficient.
l = length of the light path through the solution.
c = concentration of the absorbing substance.
So, what does standard curve mean?

## Slide 11
A standard curve:
- It is a graph that shows the relationship between different known concentrations of a substance and the absorbance at a specific wave length.
-Standard curve are most commonly used to determine the concentration of a substance, using serial dilution of solutions of known concentrations.
-So, what is the principle of a standard curve???
So, what is standard solutions???
standard solution:
is a solution containing a precisely known concentration of an element or a substance.

## Slide 12
How to determine unknown concentration,
of a solution with known absorbance value?

## Slide 13
Chart: BSA standard curve
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Absorbance of the
” unknown solution”
Concentration of the
” unknown solution”
If the unknown solution has absorbance value =0.45,
the conc. From the curve will be ......

## Slide 14
To determine the concentration of an unknown solution:
From standard curve:
-Measure the absorbance of the “unknown solution” in order to determine the concentration.
- …
Beer-Lambert law:
Using available information of any standard solution to determine the “ε”,
then using these information to get the unknown concentration. Using:A = εlc
Note: “ε” will changed when the weave length changed.

## Slide 15
A-Absorption spectrum of bromophenol blue:
Draw absorption spectrum curve[absorbance against wavelength] of bromophenol blue then determine λmax.
Wave length [n.m] | Absorbance
320 | 0.105
340 | 0.110
360 | 0.120
380 | 0.167
400 | 0.251
420 | 0.334
440 | 0.357
460 | 0.306
480 | 0.203
500 | 0.113
520 | 0.056
540 | 0.037
560 | 0.038
580 | 0.051
600 | 0.055
620 | 0.019

## Slide 16
λmax
λmax for bromophenol blue =440nm

## Slide 17
2. Standard curve
a) Set up 8 test tubes as follows:
Tube No. | 7.5x10 - 5M bromophenol blue (ml) [std.] | 95% ethanol (ml) | 0.1 M citrate buffer [pH 2.4] (ml) | Sample With unknown concentration (ml)
1 | 0.1 | 0 . 9 | 9 . 0 | -
2 | 0.2 | 0.8 | 9 . 0 | -
3 | 0.4 | 0.6 | 9 . 0 | -
4 | 0.6 | 0.4 | 9 . 0 | -
5 | 0.8 | 0.2 | 9 . 0 | -
6 | 1.0 | - | 9 . 0 | -
7 [unknown] | - | - | 9 . 0 | 1.0
b) Mix and measure the absorbance of all the tubes at 430 nm against a water blank.

## Slide 18
Tube No. | Molar concentration of bromophenol blue x 10 - 6 | Absorbance at 430 nm
1 | 0.75 | 0.171
2 | 1.5 | 0.391
3 | 3 | 0.806
4 | 4.5 | 1.243
5 | 6 | 1.639
6 | 7.5 | 1.996
7[unknown] | ................... | 1.505
Results:
b-Plot a standard curve of absorbance against Molar concentration of bromophenol blue x10 – 6.
c-From the curve determine the molar concentration of the unknown sample (tube 7).

## Slide 19
- Molar concentration of bromophenol blue in unknown sample (tube 7).=……… x 10 – 6

## Slide 20
Standard curve animation:
http://www.wellesley.edu/Biology/Concepts/Html/standardcurve.html
Spectrophotometry Introduction:
http://www.youtube.com/watch?v=qbCZbP6_j48
Spectrophotometry Example
http://www.youtube.com/watch?v=VqAa_cmZ7OY&feature=relmfu