## Slide 1: Scanning spectrophotometry and spectrophotometric determination of concentration
BCH 333 [practical]
Lab# 1

## Slide 2
Objectives:
1. What is absorption spectrum and determination of λmax.
2. Standard curve of known concentration and determine the concentration for a solution “with unknown concentration”.

## Slide 3
How a spectrophotometer works.
(spectrophotometer components)

## Slide 4
Spectrophotometer: it can be used to measure the amount of light absorbed by a solution. How?
-By using the spectrophotometer, we can quantitatively measure the absorbance, and this information can be used to determine the concentration of the absorbing molecule.
-More concentrated solution will absorb more light and transmits less.[why?]
So, the more concentrated solution  high absorbance value.
And Less concentrated solution  less absorbance value.
Notes: المذكور كمثال هو احد التطبيقات

## Slide 5
Absorption spectrum

## Slide 6
Absorption spectrum:
The curve that display the action or behaviour of absorption of molecule [solute] at different weave lengths, Known as Absorption spectrum curve.
-Every molecule has its own Absorption spectrum, So it’s considered as fingerprint for each molecule.
λmax: it is the weave length, at which the molecule has the maximum absorbance at this weave length.[best absorbance]. It can be determined from absorption spectrum curve.
[The wavelength of maximum absorption (λmax)]

## Slide 7
Absorption spectrum curve and determination of λmax.

## Slide 8
Absorption spectrum curve for different molecules.

## Slide 9
What is the benefit of studying the Absorption spectrum :
Determine λmax.
Used to identify substances.
It also can be used to know if there is any contamination with another molecule.

## Slide 10
http://www.youtube.com/watch?v=pxC6F7bK8CU
How does a spectrophotometer work?

## Slide 11
Standard curve of Concentrations

## Slide 12
Principle Standard curve of Concentrations:
Beer-Lambert law:
The absorption of light by a solution is described by the Beer-Lambert law as:
There is linear relationship between absorbance and concentration of an absorbing species.
A = εlc
A= is the absorbance.
ε = extinction(absorption) coefficient.
l = length of the light path through the solution.
c = concentration of the absorbing substance.
So, what does standard curve of concentrations mean?

## Slide 13
A standard curve for concentrations:
- It is a graph that shows the relationship between different known concentrations of a substance and the absorbance at a specific wave length.
-Standard curve are most commonly used to determine the concentration of a substance, using serial dilution of solutions of known concentrations.
-So, what is the principle of a standard curve concentrations???
Wait….. what is standard solutions???
Standard Solution:
is a solution containing a precisely known concentration of an element or a substance.

## Slide 14
How to determine unknown concentration
of a solution with known absorbance value?

## Slide 15
Chart: BSA standard curve of concentration
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Absorbance of the
” solution with unknown concentration”
Concentration of the
” solution with unknown concentration”
If the unknown concentration of a solution has absorbance value =0.45,
the conc. From the curve will be ......??

## Slide 16
To determine the concentration of a solution with
“an unknown concentration”:
From standard curve of concentration:
-Measure the absorbance of the “solution with unknown concentration” in order to determine the concentration, from the curve.
Beer-Lambert law:
Using available information of any standard solution to determine the “ε”,
then using these information to get the unknown concentration. Using:A = εlc
Note: “ε” will changed when the weave length changed.

## Slide 18
Spectrophotometry Introduction:
http://www.youtube.com/watch?v=qbCZbP6_j48
Spectrophotometry Example
http://www.youtube.com/watch?v=VqAa_cmZ7OY&feature=relmfu