## Slide 3: 11001 / 101 , 110000/011

## Slide 5
1.18) Perform subtraction on the given unsigned binary numbers using the 2's complement of the subtrahend.
Where the result should be negative, find its 2‘s complement and affix: a minus sign.
1 0 0 1 1 – 1 0 0 0 1 | 1 0 0 1 – 1 0 1 0 0 0

## Slide 6
Find the 5-bit signed magnitude, 1’s and two’s complement representation of the
decimal number. (-5)

## Slide 7
Overflow
40+30 ( 7 bit signed number )
0 _ 1 0 1 0 0 0
0 _ 0 1 1 1 1 0

## Slide 8
Perform the addition of following 8-bit two’s complement binary numbers. Indicate
if there is an overflow or not.
11100100 + 10011100

## Slide 9
+49: 0 _ 1 1 0 0 0 1
-49: 1 _ 0 0 1 1 1 1
+29: 0 _ 0 1 1 1 0 1
-29: 1 _ 1 0 0 0 1 1

## Slide 11
86 + 48

## Slide 13
0101 0001 0011 0111

## Slide 14
Complement bit 6
A: 100 0001
a: 110 0001

## Slide 15: Other Codes

## Slide 16: ASCII Code
American Standard Code for Information Interchange (ASCII)

## Slide 17: ASCII Properties
  Digits 0 to 9 span Hexadecimal values 3016 to 3916
  Upper case A-Z span 4116 to 5A16
  Lower case a-z span 6116 to 7A16
  Lower to upper case translation (and vice versa) occurs by flipping bit 6.