## Slide 1: Lab1: Microscopy & Cellular structure
Lama AlAbdi

## Slide 2: Applications of compound microscope
Investigation of cells and cellular structures.
Study of tissues and microorganisms.
Monitoring embryos development.
And much more...

## Slide 3: Structure & Systems
The compound microscope is made of 3 systems:
  The mounting and movement System.
  The magnification System.
  The illumination System.

## Slide 4: The Mounting and Movement System
The nose piece:
Carries the objective lenses and move them accordingly above the stage
The stage:
Horizontal platform upon which the slide of interest rest
The base:
Supports the microscope
The arm:
Supports and connects the upper part of the microscope
The body tube:
carries the ocular lenses
The coarse focusing knob:
for stage movement
The fine focusing knob:
for image sharpness

## Slide 5: The Magnification System
How to calculate the magnification power?
Magnification power = ocular lens * objective lens.
(e.g.) 10X * 40X = 400X hint: Don’t forget the unit
The objective lenses:
Scanning lens: 3.5X or 4X or 5X
Low power lens: 10X
High power lens: 40X
Oil immersion lens: 100X
The ocular lenses:
5X, 10X, and 15X

## Slide 6: The Illumination System
The illuminator:
light source
The condenser:
collects and concentrate the light
The iris diaphragm:
controls the amount of light reaching the slide

## Slide 7: The cell
It is the functional and structural unit in organisms.
Different cell structures depending on their location and function in the body.
3 major cell components:
  Genetic material.
  Cytoplasm.
  Cell membrane.

## Slide 8: cell types
Two major cell types depending on the arrangement of the genetic material inside the cell:
  Eukaryotic cells (True nucleated cells):
    Nucleus is present. DNA is associated with protein making chromatin.
  Prokaryotic cells (pro = before; Karyone = nucleus):
    Nucleus is absent. The region where the DNA is located in the cytoplasm is called nucleoid.

## Slide 9: Prokaryotes: bacteria
Bacillus:
  Rod shape and occur in strands.
Coccus:
  Rounded and occur in colonies or strands.

## Slide 10: Eukaryotes
Plant cells:
  Have cell wall.
  example: onion cells.
    Rectangular with eccentric nucleus.
Animal cells:
Does NOT have cell wall.

## Slide 11: Under the Microscope

## Slide 12: Plant cell: onion cell
1. Nucleus. 2. Cell wall. 3. Cytoplasm
4. Cell membrane.

## Slide 13: Animal cell: simple squamous epithelium- mouth mucosa (Top view)
1. Cell membrane. 2. Cytoplasm.
3. Nucleus.
1
2
3

## Slide 14
THANK YOU