## Slide 1: A Closer Look at Instruction Set Architectures

## Slide 2: Lecture Overview
Introduction
Instruction formats
  Introduction
  Design Decisions for Instruction Sets
  Little VS Big Endian
  Internal Storage in the CPU
  Number of operands and Instruction Length

## Slide 3: Introduction (1/1)
Introduction
We look at different instruction formats, operand types, and memory access methods.
We will see the interrelation between machine organization and instruction formats.
This leads to a deeper understanding of computer architecture and organization in general.

## Slide 4: Instruction formats – Introduction (1/2)
Instruction formats
In Chapter (MARIE) we saw that MARIE have an instruction length of 16 bits and could have, at most, 1 operand
In another architecture, those could be different
So, computer architectures generally differs by their Instructions Set format.
An Instruction Set can be described by its features.

## Slide 5: Instruction formats – Introduction (2/2)
Instruction formats
The Instruction set’s features are:
  Number of bits per instruction: 12, 32 and 64 are the most common
  Type of the CPU elementary memory: Stack-based or register-based (this will affect the instruction format)
  Number of operands per instruction: Zero, one, two, and three being the most common.
  Operand location: register-to-register, register to-memory or memory-to-memory instructions.
  Types of operations: not only types of operations but also which instructions can access memory and which cannot.
  Type and size of operands: operands can be addresses, numbers, or even characters.

## Slide 6: Design Decisions for Instruction Sets (1/4)
Instruction formats
During the design phase of a computer architecture, the Instruction set must be optimized.
  The instruction set must match the architecture.
  It must also maximize the efficiency of the computer architecture.
The first thing to define during the design phase is the instruction set format.
  To understand how this choice is made, we should know first, how we measure the efficiency of an ISA.

## Slide 7: Design Decisions for Instruction Sets (2/4)
Instruction formats
Instruction set architectures are measured according to:
  Main memory space occupied by a program.
  Instruction complexity: amount of decoding necessary to execute an instruction (number of clock cycles per instruction)
  Instruction length (in bits).
  Total number of instructions in the instruction set.

## Slide 8: Design Decisions for Instruction Sets (3/4)
Instruction formats
So, things to consider when designing an instruction set include:
  Instruction length
    Short Vs long instructions:
      shorter instructions take up less space in memory 
      shorter instructions can be fetched quickly 
      shorter instructions limit the number of instructions 
      shorter instructions limit the number of operands 
    Variable length VS fixed length instructions:
      Fixed length instructions are easier to decode 
      but Fixed length instructions waste space 

## Slide 9: Design Decisions for Instruction Sets (4/4)
Instruction formats
Things to consider when designing an instruction set include:
  Number of operands
    Fixed number : Zero, one, two, and three being the most common
    Variable number of operands (even if we have a fixed length instructions): Expanding opcode (to be explained in this lecture!)
  Addressable registers
    How many? (number of registers)
    How are they stored in the CPU?
  Memory organization
    Word addressable or byte addressable?
    A byte addressable architecture uses little or big endian concept? (to be explained in this lecture!)
  Addressing modes
    Direct, indirect, immediate, indexed, etc. (to be explained in this lecture!)

## Slide 10: Lecture Overview
Introduction
Instruction formats
  Introduction
  Design Decisions for Instruction Sets
  Little VS Big Endian
  Internal Storage in the CPU
  Number of operands and Instruction Length

## Slide 11: Little VS Big Endian (1/5)
Instruction formats
If we have a 32 bit data word, how we store this word in a byte addressable memory? The Least significant byte first? Of the most significant byte first?
Byte ordering, or endianness, is a major architectural consideration
We distinguish two concepts for byte ordering:
  Little Endian: A byte with a lower significance is stored in a lower address
  Big Endian: A byte with a higher significance is stored in a lower address

## Slide 12: Little VS Big Endian (2/5)
Instruction formats
Example 1: consider an integer requiring 4 bytes:
  On a little endian machine, this is arranged in memory as follows:
  Base Address + 0 → Byte0
  Base Address + 1 → Byte1
  Base Address + 2 → Byte2
  Base Address + 3 → Byte3
Byte 3 | Byte 2 | Byte 1 | Byte 0

## Slide 13: Little VS Big Endian (3/5)
Instruction formats
Example 2: consider an integer requiring 4 bytes:
  On a big endian machine, this long integer would then be stored as:
  Base Address + 0 → Byte3
  Base Address + 1 → Byte2
  Base Address + 2 → Byte1
  Base Address + 3 → Byte0
Byte 3 | Byte 2 | Byte 1 | Byte 0

## Slide 14: Little VS Big Endian (4/5)
Instruction formats
Example 3: On a byte-addressable machine, the 32-bit (8 numbers*4 each hex. Decimal number in binary) hex value 12345678 is stored at address 0. How is this value stored in memory if the machine uses a Big Endian concept? A little Endian concept?
  Answer:
Here in memory the data is stored in HEX. Based, means the following: 1 and 2 for example will 0001 and 0010, here the some of number -8. when calculate 8* 4 (locations)=32 bit

## Slide 15: Little VS Big Endian (5/5)
Instruction formats
Advantages of Big Endian:
  Is more natural: The most significant byte comes first (lower address).
  The sign of the number can be determined by looking at the byte at address offset 0.
  Strings and integers are stored in the same order.
Advantages of Little Endian:
  Makes it easier to place values on non-word boundaries.
  High-precision arithmetic is fast and easy.

## Slide 16: Lecture Overview
Introduction
Instruction formats
  Introduction
  Design Decisions for Instruction Sets
  Little VS Big Endian
  Internal Storage in the CPU
  Number of operands and Instruction Length

## Slide 17: Internal Storage in the CPU: Stacks VS Registers (1/5)
Instruction formats
Another consideration for architecture design concerns how the CPU will store data.
We have three choices:
  A stack architecture.
  An accumulator architecture.
  A general purpose register architecture.
Designers choosing an ISA must decide which will work best in a particular environment and examine the tradeoffs carefully

## Slide 18: Internal Storage in the CPU: Stacks VS Registers (2/5)
Instruction formats
Stack Architecture
  A stack is used to execute instructions
  Instructions and operands are implicitly taken from the stack
  Advantages
    Good code density
    Simple model for evaluation of expressions
  Disadvantages
    A stack cannot be accessed randomly
    Difficult to generate efficient code

## Slide 19: Internal Storage in the CPU: Stacks VS Registers (3/5)
Instruction formats
Accumulator architectures
  One operand of a binary operation is implicitly in the accumulator
    Example: MARIE
  Advantages
    Reduce the internal complexity of the machine
    Allow very short instructions
  Disadvantages
    Memory traffic is very high (since one operand is in memory)

## Slide 20: Internal Storage in the CPU: Stacks VS Registers (4/5)
Instruction formats
General purpose register architectures (GPR)
  General purpose registers can be used instead of memory
  Advantages
    Registers are faster than memory
    Easy for compilers to deal with
    Can be used very effectively and efficiently
  Disadvantages
    Long Instructions, long fetch and decode times

## Slide 21: Internal Storage in the CPU: Stacks VS Registers (5/5)
Instruction formats
General purpose register architectures (GPR)
  GPR are the most widely accepted models for machine architectures today
  There are three types of GPR
    Memory-memory architectures: may have two or three operands in memory, allowing an instruction to perform an operation without requiring any operand to be in a register.
    Register-memory architectures: require a mix, where at least one operand is in a register and one is in memory.
    Load-store architectures: require data to be moved into registers before any operations on that data are performed.

## Slide 22: Lecture Overview
Introduction
Instruction formats
  Introduction
  Design Decisions for Instruction Sets
  Little VS Big Endian
  Internal Storage in the CPU
  Number of operands and Instruction Length

## Slide 23: Number of operands and Instruction Length (1/6)
Instruction formats
On current architectures, instructions can be formatted in two ways:
  Fixed length: Wastes space but is relatively fast.
  Variable length: Complex to decode but saves storage space.
In this course, we will be interested in Fixed length instructions.
In such instructions, we define the maximum number of operands (this number has a direct impact on the length of the instruction itself)

## Slide 24: Number of operands and Instruction Length (2/6)
Instruction formats
Example:
  MARIE uses a fixed-length instruction with a 4-bit opcode and 12-bit operand.
  In MARIE the maximum number of operands is one. Though, some instructions for MARIE have no operand (for instance: halt).

## Slide 25: Number of operands and Instruction Length (3/6)
Instruction formats
The most common instruction formats include zero, one, two, or three operands:
  Zero operand
    OPCODE only
  One operand (usually a memory address)
    OPCODE + 1 Address
  Two operands (usually registers, or one register and one memory address)
    OPCODE + 2 Addresses
  Three operands (usually registers, or combinations of registers and memory)
    OPCODE + 3 Addresses

## Slide 26: Number of operands and Instruction Length (4/6)
Instruction formats
Machine instructions that have no operands must use a stack
In architectures based on stacks, most instructions consist of opcodes only; however, there are special instructions that have just one operand:
  Push X places the data value found at memory location X onto the stack
  Pop X removes the top element in the stack and stores it at location X

## Slide 27: Number of operands and Instruction Length (5/6)
Instruction formats
Example: Suppose we wish to evaluate the following expression: Z = (X x Y) + (W x U)
The assembly code would be:
For a Three operand ISA | For a Two operand ISA | For a one operand ISA (such as MARIE!)
Mult R1, X, Y Mult R2, W, U Add Z, R2, R1 | Load R1, X Mult R1, Y Load R2, W Mult R2, U Add R1, R2 Store Z, R1 | Load X Mult Y Store Temp Load W Mult U Add Temp Store Z

## Slide 28: Number of operands and Instruction Length (6/6)
Instruction formats
Example: Suppose we wish to evaluate the following expression: Z = (X x Y) + (W x U)
  In a stack architecture the assembly code would be :
For a zero operand ISA
Push X Push Y Mult Push W Push U Mult Add Store Z
X
Y
X
X x Y
Push Y
Mult
Push W;
Push U
U
W
W x U
Mult
W x U
X x Y
Add
X x Y + W x U
Stack
Stack
Stack
Stack
Stack
Stack