## Slide 1: Sterilization and Disinfections

## Slide 2: Sterilization
Freeing of an environment from all living microorganisms includes bacteria and their spores, fungi, parasites and viruses.
Sterilization means germ free objects.
Sterilization occurs by:
  Physical methods.
  Chemical methods.

## Slide 3
Sterilization
by
Physical
methods
Heat
Radiation
Filteration

## Slide 4: Physical methods
Heat:
  Exposure of the objects to heat will kills microbes by coagulation of protein, denaturation of enzymes and oxidation.
Filtration:
  Sterilization through removing of microbes from fluids by exposing to small size filter. Used for heat sensitive fluids like serum, antibiotic, suger, and urea.
Radiation:
  Exposure to irradiation causes denaturation of proteins and enzymes.

## Slide 5: sterilization by heat
Heat
Dry heat
Moist heat

## Slide 6: Dry heat
Dry heat
Red hot
Flaming
Hot air
oven
Incineration

## Slide 8: Red hot
Exposure of wires and forceps to the Bunsen flame until it becomes red hot, then cool down and use.
Used for loop, forceps, and metal rods.

## Slide 9: Flaming
Slowly passing of an objects to the Bunsen flame will reduce the number of microorganisms.
Used for sterilization of the mouth of bottle, flasks, containers and test tubes, smear slides etc,,,.

## Slide 10: Flaming

## Slide 11: Hot air oven
Instruments consist of heater, oven.
Used for sand, powder, metal, glass.
Thermal death point and Thermal death time:
  160C for 60 min.
  180C for 30 min.

## Slide 12: Incineration
Is treating of an objects to heating over 250 until become black.
Done for used equipment.

## Slide 13: Moist heat
Moist heat
Less than 100C
At 100C
Above 100C

## Slide 14: Less than 100C
Pasteurization of milk:
  Holding method (65C for 30 min)
  Flash method (72C for 20 sec)
Preparation of vaccine:
  By heating at 56C for 30-60 min.

## Slide 15: At 100 C
Steaming:
  Single exposure of the microbe to steam at 100C for 90 min.
Boiling:
  Boiling water is the most common form of application of moist heat but is not capable of killing endospores or killing all viruses
  At 100º C for 30 min.

## Slide 16: Boiling plate test
  A pure culture of a single microorganism is grown in a broth.
Divide the plate into 6 parts 0,5,15,30,45,60 min.
Culture the org. on 0 part.
Incubate the culture tube in water bath 100º C.
After 5 min culture org. in 5 part, and so on, until you complete 1 hr.
Incubate 24 hr.
0
60
45
30
15
5

## Slide 17: Above 100C (Autoclaving)
Depends on steam and pressure.
  Steam is a hot air able to penetrate through things.
  Pressure will rise the temperature from 100C to 121C.
Moist heat is more effective than dry heat at a given temperature or length of exposure. also more penetrating than dry heat
Make complete killing of bacteria, their spores, fungi and their spores, parasites and viruses including Envelop and non Envelop virus.
Thermal death point and thermal death time:
  121C for 15 - 20 min.
  Flash autoclaving at 134C for 4-5min.

## Slide 18: Autoclave indicator
Chemical indicator:
Autoclave tape.
Brown’s tube (diack tube).
Biological indicator: Spore strip (thermophilic organism).

## Slide 19: Radiation
  Sterilization by radiation kills microbes by causing mutation to the cellular protein and disrupting cellular elements.
  Types of radiation:
1) UV ( not a good sterilizing method).
2) Ionizing , most medical disposables ( syringes, needles).

## Slide 20: Filtration
Sterilization by mechanical removal of pathogenic microorganism by passing through membrane filter. Unable to filter viruses according to their small size.
The pore size is less than 0.45 µm(bacteria size 100-1 µm).
Used for sterilization of heat sensitive fluids like serum, glucose, urea, and Amino acids.

## Slide 21: Disinfection
Chemical methods of sterilization

## Slide 22
Disinfection:
  Is removing of pathogenic microorganism or reducing their number on the exposed area.
  Unable to destroy spores and some could not kill non envelop viruses.
  Antiseptic:
  is a chemical agent that is applied to living tissue to kill microbes.

## Slide 23: Factors affects disinfection action:
  Type of disinfection.
  Concentration of disinfectant.
  Type of microorganism.
  Number of microorganism.
  Time of exposure.
  Temperature.

## Slide 24: Phenolic group of disinfectant:
E.g.: Phenol crystal, Dittol, Lysol, Cresol.
Remain active, stable and persist for long period of time.
Active against G+ve, G-ve, Mycobacterium & viruses.

## Slide 25: Alcohols:
E.g.: Anti-bacterial, sanitizer.
They able to act and Evaporate, short period of time..

## Slide 26: Dyes:
Crystal violet and Eosine are very effective antiseptic.

## Slide 27: Surface active agents:
Soap and other detergent make mechanical remove of microbe by scrubbing of dead tissue so reduce their number.

## Slide 28: MIC test
  A pure culture of a single microorganism is grown in a broth.
  The antimicrobial agent is diluted in a number of times, 1:1, through a sterile diluent (usually Mueller-Hinton broth).
  Add 2 drops of the organism onto the antimicrobial dilution.

## Slide 29
  Incubate 24 hr in the incubator.
  After incubation, the dilution observe growth, The last tube in the dilution series that does not demonstrate growth corresponds with the minimum inhibitory concentration (MIC) of the antimicrobial agent.