## Slide 1
11. In SITU STRESSES

## Slide 2
We Will Consider this in the Next Chapter
INTRODUCTION

## Slide 3
Soils are multiphase systems. They consists of solid particles enclosing continuous voids which contain water and/or air.
INTRODUCTION
Solid
Solid
Air
When an external load is applied to soil it will be carried jointly by the three systems, solid, water, air.

## Slide 4
However, it is difficult, if not impossible to analyze such multiphase system.
When the soil is fully saturated, then only water is presented in the voids and the problem becomes relatively simple.
When an external load is applied to saturated soil it will be carried jointly by the two systems, solid grains and water in the pores.
F
The increase in pressure within the pore water causes drainage (flow out of the soil), and the load is transferred to the solid grains. The rate of drainage depends on the permeability of the soil.

## Slide 5
If by any mean we can find the part of the load carried by the water for a given external load, then we can find the part carried by the solids.
This is the theme of the Principle of Effective Stress. In other word the principle of effective stress determines the effect of a pore pressure on the behavior of a soil with a given TOTAL STRESS.
It is probably the single most important concept in soil mechanics and geotechnical engineering.
The compressibility and shearing resistance of a soil depend to a great extent on the effective stress.

## Slide 6
The concept of effective stress is significant in solving geotechnical engineering problems, such as:
Bearing capacity and settlement of foundations
Lateral earth pressure on retaining structures
Stability of earth slopes

## Slide 7
THE PRINCIPLE OF EFFECTIVE STRESS (P.E.S.)
This principle was based on some experimental data with some intuition. It states that:
Where
Eq. 1 is more of a working hypothesis than being a physical law.
Actually Terzaghi (1925, 1936) arrived at Eq. 1 from the results of laboratory experiments.
Many attempts have been exercised in examining the validity of the concept but no one is conclusive.

## Slide 8
Important Remarks (Facts) about P.E.S.
The behavior of soils is solely controlled by the value of , therefore in engineering is what matter because all measurable effects of a change of stress, such as:
are exclusively due to changes in the effective stress.
COMPRESSIBILITY
DISTRORION
SHEAR STRENGTH
If there are two soils with the same structure and mineralogy, there behavior will be the same if they are subjected to the same effective stress. (The following example will demonstrate this).
Cannot be measured, it can only be calculated.

## Slide 9
Example
Consider two sediments of the same soil, (a) an estuarine sediment and (b) a deep-sea sediment. The unit weight is 17 kN/m3. Calculate the vertical effective stress:
1 m
1 m
104 m
The two sediments have the same value of effective stress. Hence if they have the same structure and mineralogy, they will have the same engineering properties.
(a)
(b)

## Slide 10
Theoretical Basis for the Effective Stress Principle
F = Total applied force
Fs = Portion of force carried by solid
Fw = Portion of force carried by water
Fa = Portion of force carried by air
Area
A = Total Area
As = Area of solid
Aw = Area of water
Aa = Area of air
Force
F

## Slide 11
Substituting Eq. (5) into Eq. (4)
Substituting Eq. (7) into Eq. (6) yields
The term asps is called intergranular stress. It is not precisely equal to the effective stress.
Sometimes, in granular material effective stress is taken to be equal to the intergranular stress.
However, this is not true, because the grain-to-grain contact area may be very small and intergranular stress will be extremely high and hence greater than the effective stress.
Refer to Eq. 2

## Slide 12
Taking asps to be effective stress we have
For dry soil u = 0, and
Instead of pw we use u as it is conventional in soil mechanics.
Effective stress is approximately the force per unit area carried by soil skeleton.

## Slide 13
EVALUATION OF EFFECTIVE STRESS
We now know the importance of effective stress and that it is responsible for soil behavior and the dilemma that we cannot measure it.
However, as can be seen in Eq. 1, if we can find  and u, then
Therefore, our job now is to find  and u.
I. Determination of total stress, 
a. No external load is applied
Where
g = Unit weight of the soil, the unit weight of the soil may be, wet, saturated, dry. (This depends on the degree of saturation of soil).

## Slide 14
z = The vertical distance from the surface to the point at which  is evaluated.
 in Eq. 14 is called the BODY STRESS because it is generated by the mass located upon by gravity in the body. Also it is usually refereed to as OVERBURDEN.
b. If an external load is applied
In this case the total stress at depth z is given by
Where
is the stress due to the external load at depth z excluding the weight of soil i.e. z. We will discuss in the following chapter different ways for evaluating .

## Slide 15
II. Determination of p.w.p, u
a. No external load is applied
Where
w = Unit weight of water
Therefore, by substituting Eq. 15 and Eq.16 into Eq.14, we get
b. No external load is applied, but there is steady state seepage
From Bernoulli's equation
We find h from Laplace’s equation
We use the flow net

## Slide 16
c. External load is applied
i. Fully Undrained Condition
We find Skempton’s p.w.p parameters A and B in the laboratory and to use them in evaluating u in the field. A and B are discussed in Geotechnical Engineering II.
ii. Consolidation Condition
If we have partially drained condition in (Transient flow). Then it is the Theory of Consolidation which enables us to keep trace of u and hence . This theory will be discussed in details in Geotechnical Engineering II.
As can be seen case (a) is very simple and (c) is treated in CE 481. Since by now we have a background in seepage, we will next discuss case (b).
This will be covered in Geotechnical Engineering II such that:

## Slide 17
1. Stresses in Saturated Soil in the Static Case
The rate of water supply is kept constant.
at Point B
at Point C
at Point A
At point A,
Total Stress: sA = H1 gw
Pore water pressure: uA = H1 gw
Effective stress: s’A= 0
At point B,
Total Stress: sB = H1 gw + H2 gsat
Pore water pressure: uB = (H1 + H2) gw
Effective stress: s’B= H2(gsat – gw) = H2 g’
At point C,
Total Stress: sC = H1 gw + z gsat
Pore water pressure: uC = (H1 + z) gw
Effective stress: s’C= z(gsat – gw) = z g’

## Slide 18
Example 1
Calculate the total, neutral, and effective stresses at elevation A when:
The water table is at elevation A.
The water table rises to elevation B.
Solution
a.
b.
The saturated unit weight is 19.62 kN/m3

## Slide 19
Example 2
Plot the variation of total, effective vertical stresses, and pore water pressure with depth for the soil profile shown below.

## Slide 20
Within a soil layer, the unit weight is constant, and therefore the stresses vary linearly. Therefore, it is adequate if we compute the values at the layer interfaces and water table location, and join them by straight lines.
Solution

## Slide 22: s Diagram
s

## Slide 23
Example 3
Plot the variation of total and effective vertical stresses, and pore water pressure with depth for the soil profile shown below.

## Slide 24
2. Stresses in Saturated Soil with Upward Seepage
In case of seepage the effective stress at any point in a soil mass will differ from that in the static case.
Therefore the effective stress decreases when there is upward seepage. It decreases by exactly the increase in p.w.p.
Note: For illustration we consider simple 1D case
z

## Slide 25
Quick Condition (Boiling)
For the case of upward seepage, what happen if the hydraulic gradient gradually increased. At a certain value of hydraulic gradient the effective stress will be zero (Note that cannot be less than zero).
ic is called the CRITICAL HYDRAULIC GRADIENT. It is the value of I when a quick condition occurs.
Recall that
Note: fully saturated soil

## Slide 26
Remarks
The approach we just used to obtain ic is based on the premise that quick conditions occur when at the BOTTOM of the soil column is zero.
Each point of the soil column has its own ic. However ic for the point at the bottom will be the first one to occur since it has the largest gradient all times.
For most soils 0.9 < ic < 1.1 with an average of 1.0.

## Slide 27
3. Stresses in Saturated Soil with Downward Seepage
At B,
Total Stress: sB = H1 gw + H2 gsat
Pore water pressure: uB = (H1 + H2 - h) gw
Effective stress: s’B= H2(gsat – gw) + h gw
At C,
Total Stress: sC = H1 gw + z gsat
Pore water pressure: uC = (H1 + z – h/H2 z) gw
          = (H1 + z – i z) gw
Effective stress: s’C= z(gsat – gw) + iz gw
        = zg’ + iz gw
At A,
Total Stress: sA = H1 gw
Pore water pressure: uA = H1 gw
Effective stress: s’A= sA - uA = 0

## Slide 28
s’C = z g’
s’C
Static Case
Downward Seepage
Upward Seepage

## Slide 29
Example 4
A section through a dam is shown across. Determine:
The p.w.p. at points 1,3, and 4
The effective stress at point 2 if the saturated unit weight for the soil is 18 kN/m3.
h = 6.3 m , Nd = 10,
h =6.3/10 = 0.63 m
A.
B.
Datum
6.3
17.2
9.4
1.6

## Slide 30
A section through a sheet-pile wall which we have considered in the previous chapter is shown below. Determine:-
Example 5
The effective stress at points (a and b) if the soil has a unit weight of 18 kN/m3.
What depth of water behind the sheet-pile wall (i.e. above the upstream ground surface) will cause a quick condition at point (a).
Datum

## Slide 31
H = 11 m, Nd = 8 ,
h =11/8 = 1.375 m
Point (a)
Point (b)
Solution:
A.
B.
For quick condition at point (a) we have
Datum

## Slide 32
SEEPAGE FORCE
We have seen in the preceding sections that the effective stress at a point in a soil layer would increase or decrease due to seepage.
For the static case the effective stress at depth z measured from the surface of the soil layer is given by
Therefore, the effective force on an area A is
If there is an upward seepage of water in the vertical direction through the same soil layer, the effective force on an area A at a depth z is given by,

## Slide 33
Hence, the decrease in the total force because of seepage is
It is often convenient to express the seepage force per unit volume. Hence the seepage force per unit volume of soil is
Flow nets can be used to find i at any point and, thus, seepage force per unit volume of soil. This is important in analyzing the stability of structures where heave is of a problem.
Remarks
In an isotropic soils, the force acts in the same direction as the direction of flow.

## Slide 34
Static (Hydrostatic)
Upward Seepage
Downward Seepage
SEEPAGE FORCE
s’C = z g’
s’C