## Slide 1: A Closer Look at Instruction Set Architectures: Expanding Opcodes

## Slide 2: Lecture Overview
Instruction formats
  Expanding Opcodes
Instruction types
Addressing

## Slide 3: Expanding Opcodes
Instruction formats
We have seen how instruction length is affected by the number of operands supported by the ISA.
In any instruction set, not all instructions require the same number of operands.
Operations that require no operands, such as HALT, necessarily waste some space when fixed-length instructions are used.
One way to recover some of this space is to use expanding opcodes.

## Slide 4: Expanding Opcodes
Instruction formats
The idea of expanding opcodes is to make some opcodes short, but have a means to provide longer ones when needed.
When the opcode is short, a lot of bits are left to hold operands
  So, we could have two or three operands per instruction
If an instruction has no operands (such as Halt), all the bits can be used for the opcode
  Many unique instructions are hence available
In between, there are longer opcodes with fewer operands as well as shorter opcodes with more operands.

## Slide 5: Expanding Opcodes
Instruction formats
Example 1: Consider a machine with 16-bit instructions and 16 registers.
  The instruction format can have several structures:
    Opcode + Memory address (such as MARIE):
      If we have 4KB byte addressable memory we need 12 bits to specify an address location
      The remaining 4 bits are used for the opcode: 16 instruction are hence available
    Opcode + Registers Addresses
      we need 4 bits to select one of the 16 available registers
      Suppose we have 4 bits opcode, we could encode 16 different instructions with three operands each (3 x 4 bits = 12 bits).

## Slide 6: Expanding Opcodes
Instruction formats
Example 2: Consider a machine with 16-bit instructions and 16 registers. And we wish to encode the following instructions:
    15 instructions with 3 addresses
    14 instructions with 2 addresses
    31 instructions with 1 address
    16 instructions with 0 addresses
  Can we encode this instruction set in 16 bits?
  Answer: Yes if we use expanding opcodes

## Slide 7: Expanding Opcodes
Instruction formats
One possible encoding is as follows:
Is there something missing from this instruction set?

## Slide 8: Expanding Opcodes
Instruction formats
How do we know if the instruction set we want is possible when using expanding opcodes?
  We must determine if we have enough bits to create the desired number of bits patterns

## Slide 9: Expanding Opcodes
Instruction formats
Going back to Example 2 (Slide 6):
  The first 15 instructions account for:
    15x24x24x24 = 15 x 212 = 61440 bit patterns
  The next 14 instructions account for:
    14 x 24 x 24 = 15 x 28 = 3584 bit patterns
  The next 31 instructions account for:
    31 x 24 = 496 bit patterns
  The last 16 instructions account for 16 bit patterns
  In total we need 61440 + 3584 + 496 + 16 = 65536 different bit patterns
  Having a total of 16 bits we can create 216 = 65536 bit patterns
  We have an exact match with no wasted patterns.
  So our instruction set is possible.

## Slide 10: Expanding Opcodes
Instruction formats
Example 3: Is it possible to design an expanding opcode to allow the following to be encoded with a 12-bit instruction? Assume a register operand requires 3 bits.
  4 instructions with 3 registers
  255 instructions with 1 register
  16 instructions with 0 register

## Slide 11: Expanding Opcodes
Instruction formats
Solution:
  The first 4 instructions account for:
    4x23x23x23 = 4 x 29 = 2048 bit patterns
  The next 255 instructions account for:
    255 x 23= 2040 bit patterns
  The last 16 instructions account for 16 bit patterns
  In total we need 2048 + 2040 + 16 = 4104 bit patterns
  With 12 bit instruction we can only have 212 = 4096 bit patterns
  Required bit patterns (4104) is more than what we have (4096), so this instruction set is not possible with only 12 bits.

## Slide 12: Lecture Overview
Instruction formats
    Expanding Opcodes
Instruction types
Addressing

## Slide 13: Instruction types
Instruction types
Instructions fall into several broad categories:
  Data movement instructions
    The most frequently used instructions
    Data is moved from memory into registers, from registers to registers, and from registers to memory
    Examples: Load, Store, Move, Push, Pop, etc.
  Arithmetic instructions
    Include those instructions that use integers and floating point numbers.
    As with the data movement instructions, there are sometimes different instructions for providing various combinations of register and memory accesses in different addressing modes.
    Examples: Add, Subtract, Multiply, Increment, Decrement, etc.

## Slide 14: Instruction types
Instruction types
Instructions fall into several broad categories:
  Boolean Instructions
    Perform Boolean expressions.
    Commonly used to control I/O devices.
    Examples: Not, Or, Xor, Test, compare, etc.
  Bit manipulation instructions
    Used for setting and resetting individual bits (or sometimes groups of bits) within a given data word.
    Examples: Shift left, shift right, rotate left, rotate right

## Slide 15: Instruction types
Instruction types
Instructions fall into several broad categories:
  I/O instructions
    Used to communicate with input/output devices
    Examples: Input, Output.
  Control transfer Instructions
    Include branches, skips and procedure calls.
    Examples: For MARIE we have Jump, skipcond and JnS.
  Special purpose Instructions
    Include those used for string processing, high-level language support, protection, flag control, and cache management.

## Slide 16: Instruction types
Instruction types
When designing an instruction set for a given architecture, we must respect the following:
  Create a complete instruction set.
  Be carful not to add redundant instructions
  We should respect instructions orthogonality
    Each instruction should perform a unique function without duplicating any other instruction

## Slide 17: Lecture Overview
Instruction formats
    Expanding Opcodes
Addressing
  Introduction
  Addressing Modes

## Slide 18: Addressing - Introduction
Addressing
Addressing modes specify where an operand is located.
They can specify a constant, a register, or a memory location.
The actual location of an operand is its effective address.
Certain addressing modes allow us to determine the address of an operand dynamically.

## Slide 19: Addressing Modes
Addressing
Immediate addressing
  The data is part of the instruction.
  Example: Load 008
    The numeric value 8 is loaded into the AC
Direct addressing
  The address of the data is given in the instruction.
  Example: Load 008
    The data value found at memory address 008 is loaded into the AC
Register addressing
  The data is located in a register.
  Example: Load R1.
    The contents of R1 register is used as the operand.

## Slide 20: Addressing Modes
Addressing
Indirect addressing
  Gives the address of the address of the data in the instruction.
  Example Load 008
    The data value found at memory address 008 is actually the effective address of the desired operand.
      Suppose we find the value 2A0 stored in location 008.
      2A0 is the “real” address of he value we want.
      The value found at location 2A0 is then loaded into the AC

## Slide 21: Addressing Modes
Addressing
Register indirect addressing
  Uses a register to store the effective address of the data.
  Works exactly the same way as indirect addressing mode, except it uses a register instead of a memory address to point to the data.
  Example: Load R1
    The effective address of the desired operand is found in R1.

## Slide 22: Addressing Modes
Addressing
Indexed addressing
  uses a register (implicitly or explicitly) as an offset, which is added to the address in the operand to determine the effective address of the data.
  Example: Load X, where the index register holds the value 1.
    The effective address of the operand in actually X + 1

## Slide 23: Addressing Modes
Addressing
Based addressing
  Similar to indexed addressing except that a base register is used instead of an index register.
  An index register holds an offset relative to the address given in the instruction, but a base register holds a base address where the address field represents a displacement from this base.
  Example: Load 3, where the base register holds the address value X.
    The effective address of the operand is actually X +3
Stack addressing
  The operand is assumed to be on top of the stack.

## Slide 24: Addressing Modes
Addressing
Example: For the instruction shown, what value is loaded into the accumulator for each addressing mode?
800

## Slide 25: Addressing Modes
Addressing
Example: For the instruction shown, what value is loaded into the accumulator for each addressing mode?
900
800

## Slide 26: Addressing Modes
Addressing
Example: For the instruction shown, what value is loaded into the accumulator for each addressing mode?
1000
800
900

## Slide 27: Addressing Modes
Addressing
Example: For the instruction shown, what value is loaded into the accumulator for each addressing mode?
1000
800
900
700
800 + 800 = 1600