## Slide 1
Sterilization
<number>
2015
<number>
King Saud University
Dept. of Bot. & Microbiology
Notes: <number>

## Slide 2: Sterilization:
It is the process which makes things free of microbes .
<number>
Notes: <number>

## Slide 3: Things that can be sterilized :
Flasks
Beakers
Pipettes
Petri dishes
<number>
Tubes
Notes: <number>

## Slide 4
Petri dish
A petri dish is a flat dish made of plastic (disposable) or glass (autoclavable) with a cover that is used to grow
Microorgansim.
<number>

## Slide 5: Things that can be sterilized :
Apparatus
Clothes
Media
Needles
<number>
Notes: <number>

## Slide 6: There are 3 basic sterilization principles:
  1- Heat sterilization
  2- Chemical sterilization
  3-Radiation sterilization
<number>
Notes: <number>

## Slide 7
There are 3 procedures depending on the tolerance of the material used:
Advantages: It is the simplest, most effective and inexpensive method.
  1- Heat sterilization
  3- Steam or wet sterilization (Autoclaving).
  2-Dry heat sterilization
  (hot air oven).
<number>
  1- Incineration (Direct heat).
Notes: <number>

## Slide 8
Bunsen burner produces gas flame which used for heating, sterilization (inoculating loop and needled) .
Bunsen burners , flames
<number>
  1- Incineration
  (Direct heat):
Notes: <number>

## Slide 10
This kind of dry heat sterilization is recommended when it is undesirable that steam make contact with the material to be sterilized.
This is true for glassware's – glass petri plates, Pipettes as well as for substances like oil, powder, etc.
After sterilization wrap them in aluminum foil to avoid recontamination.
  2-Dry heat sterilization
  (hot air oven) :
<number>
Notes: <number>

## Slide 11
It includes autoclaves.
Used to sterilize culture media, glassware etc.
Usually it operates at 15 lb./sq. inch steam pressure at 121.5⁰C for 15 min.
The advantage of using an autoclave is that it can reach temperatures higher than boiling water alone, so it can kill not only bacteria but also bacterial spores, which tend to be resistant.
  3- Steam sterilization (Autoclaving) or wet :
<number>
Notes: <number>

## Slide 12: There are 3 different sterilization principles:
  1- Heat sterilization
  2- Chemical sterilization
  3-Radiation sterilization
<number>
Notes: <number>

## Slide 13
  2- Chemical sterilization
50% Dettol
Ethylene oxide and formalin
Benches /tables
For sterilizing disposable materials (that can not tolerate high temperatures).
<number>
Notes: <number>

## Slide 14: There are 3 different sterilization principles:
  1- Heat sterilization
  2- Chemical sterilization
  3-Radiation sterilization
<number>
Notes: <number>

## Slide 15
Gamma rays,U.V Rays.
  3-Radiation sterilization
<number>
Notes: <number>

## Slide 16
Other sterilization techniques:
Filtration
Boiling
Cold temperature
<number>
Notes: <number>

## Slide 17: Thanks…
Shroog Al-Shahrani
<number>
Notes: <number>