## Slide 2: Overview
Digital Systems and Computer Systems
Information Representation
Number Systems [binary, octal and hexadecimal]
Arithmetic Operations
Base Conversion

## Slide 3: Course description
Course name
  COMP 3508 - Computer organization and Assembly language
Course level
  Level 5
  Equivalent to 3 CH (Credit Hours)

## Slide 4: Course description
Reference Book
  The Essentials of Computer Organization and Architecture, 3rd edition – Author: Linda Null and Julia Lobur.

## Slide 5: Digital System
Takes a set of discrete information inputs and discrete internal information (system state) and generates a set of discrete information outputs.
System State
Discrete
Information
Processing
System
Discrete
Inputs
Discrete
Outputs

## Slide 6: Signal
An information variable represented by physical quantity.
For digital systems, the variable takes on discrete values.
Two level, or binary values are the most prevalent values in digital systems.
Binary values are represented abstractly by:
  digits 0 and 1
  words (symbols) False (F) and True (T)
  words (symbols) Low (L) and High (H)
  and words On and Off.
Binary values are represented by values or ranges of values of physical quantities

## Slide 7: Number Systems – Representation
Positive radix, positional number systems
A number with radix r is represented by a string of digits: An - 1An - 2 … A1A0 . A- 1 A- 2 … A- m + 1 A- m in which 0 £ Ai < r and . is the radix point.
The string of digits represents the power series:
(
)
(
)
(Number)r
=
å
å
+
j = - m
j
j
i
i = 0
i
r
A
r
A
(Integer Portion)
+
(Fraction Portion)
i = n - 1
j = - 1

## Slide 8: Number Systems – Examples
 | General | Decimal | Binary
Radix (Base) | r | 10 | 2
Digits | 0 => r - 1 | 0 => 9 | 0 => 1
0 1 2 3 Powers of 4 Radix 5 -1 -2 -3 -4 -5 | r0 r1 r2 r3 r4 r5 r -1 r -2 r -3 r -4 r -5 | 1 10 100 1000 10,000 100,000 0.1 0.01 0.001 0.0001 0.00001 | 1 2 4 8 16 32 0.5 0.25 0.125 0.0625 0.03125

## Slide 9: Special Powers of 2
210 (1024) is Kilo, denoted "K"
220 (1,048,576) is Mega, denoted "M"
230 (1,073, 741,824)is Giga, denoted "G"

## Slide 10: Positive Powers of 2
Useful for Base Conversion
Exponent
Value
Exponent
Value
0
1
11
2,048
1
2
12
4,096
2
4
13
8,192
3
8
14
16,384
4
16
15
32,768
5
32
16
65,536
6
64
17
131,072
7
128
18
262,144
19
524,288
20
1,048,576
21
2,097,152
8
256
9
512
10
1024

## Slide 11: Converting Binary to Decimal
To convert to decimal, use decimal arithmetic to form S (digit × respective power of 2).
Example:Convert 110102 to N10:
Notes: Powers of 2: 43210
110102 =>
1 X 24 = 16
+ 1 X 23 = 8
+ 0 X 22 = 0
+ 1 X 21 = 2
+ 0 X 20 = 0
2610

## Slide 12: Converting Decimal to Binary
Method 1
  Subtract the largest power of 2 (see slide 14) that gives a positive remainder and record the power.
  Repeat, subtracting from the prior remainder and recording the power, until the remainder is zero.
  Place 1’s in the positions in the binary result corresponding to the powers recorded; in all other positions place 0’s.
Example: Convert 62510 to N2
Notes: 625 – 512 = 113 => 9
113 – 64 = 49 => 6
49 – 32 = 17 => 5
17 – 16 = 1 => 4
1 – 1 = 0 => 0
Placing 1’s in the result for the positions recorded and 0’s elsewhere,
9 8 7 6 5 4 3 2 1 0
1 0 0 1 1 1 0 0 0 1

## Slide 13: Commonly Occurring Bases
Name
Radix
Digits
Binary
2
0,1
Octal
8
0,1,2,3,4,5,6,7
Decimal
10
0,1,2,3,4,5,6,7,8,9
Hexadecimal
16
0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F
The six letters (in addition to the 10
integers) in hexadecimal represent:
Notes: Answer: The six letters A, B, C, D, E, and F represent the digits for values
10, 11, 12, 13, 14, 15 (given in decimal), respectively, in hexadecimal.
Alternatively, a, b, c, d, e, f are used.

## Slide 14: Numbers in Different Bases
Decimal
(Base 10)
Binary
(Base 2)
Octal
(Base 8)
Hexa
decimal
(Base 16)
00
00000
00
00
01
00001
01
01
02
00010
02
02
03
00011
03
03
04
00100
04
04
05
00101
05
05
06
00110
06
06
07
00111
07
07
08
01000
10
08
09
01001
11
09
10
01010
12
0A
11
0101
1
13
0B
12
01100
14
0C
13
01101
15
0D
14
01110
16
0E
15
01111
17
0F
16
10000
20
10
Good idea to memorize!

## Slide 15: Conversion Between Bases
Method 2
To convert from one base to another:
1) Convert the Integer Part
2) Convert the Fraction Part
3) Join the two results with a radix point

## Slide 16: Conversion Details
To Convert the Integral Part:
  Repeatedly divide the number by the new radix and save the remainders. The digits for the new radix are the remainders in reverse order of their computation. If the new radix is > 10, then convert all remainders > 10 to digits A, B, …
To Convert the Fractional Part:
  Repeatedly multiply the fraction by the new radix and save the integer digits that result. The digits for the new radix are the integer digits in order of their computation. If the new radix is > 10, then convert all integers > 10 to digits A, B, …

## Slide 17: Example: Convert 46.687510 To Base 2
Convert 46 to Base 2
Convert 0.6875 to Base 2:
Join the results together with the radix point:
Notes: Answer 1: Converting 46 as integral part: Answer 2: Converting 0.6875 as fractional part:
46/2 = 23 rem = 0 0.6875 * 2 = 1.3750 int = 1
23/2 = 11 rem = 1 0.3750 * 2 = 0.7500 int = 0
11/2 = 5 remainder = 1 0.7500 * 2 = 1.5000 int = 1
5/2 = 2 remainder = 1 0.5000 * 2 = 1.0000 int = 1
2/2 = 1 remainder = 0 0.0000
1/2 = 0 remainder = 1 Reading off in the forward direction: 0.10112
Reading off in the reverse direction: 1011102
Answer 3: Combining Integral and Fractional Parts:
101110. 10112

## Slide 18: Additional Issue - Fractional Part
Note that in this conversion, the fractional part became 0 as a result of the repeated multiplications.
In general, it may take many bits to get this to happen or it may never happen.
Example: Convert 0.6510 to N2
  0.65 = 0.1010011001001 …
  The fractional part begins repeating every 4 steps yielding repeating 1001 forever!
Solution: Specify number of bits to right of radix point and round or truncate to this number.

## Slide 19: Checking the Conversion
To convert back, sum the digits times their respective powers of r.
From the prior conversion of 46.687510
1011102 = 1·32 + 0·16 +1·8 +1·4 + 1·2 +0·1
= 32 + 8 + 4 + 2
= 46
0.10112 = 1/2 + 1/8 + 1/16
= 0.5000 + 0.1250 + 0.0625
= 0.6875

## Slide 20: Octal (Hexadecimal) to Binary and Back
Octal (Hexadecimal) to Binary:
  Restate the octal (hexadecimal) as three (four) binary digits starting at the radix point and going both ways.
Binary to Octal (Hexadecimal):
  Group the binary digits into three (four) bit groups starting at the radix point and going both ways, padding with zeros as needed in the fractional part.
  Convert each group of three bits to an octal (hexadecimal) digit.

## Slide 21: Octal to Hexadecimal via Binary
Convert octal to binary.
Use groups of four bits and convert as above to hexadecimal digits.
Example: Octal to Binary to Hexadecimal
6 3 5 . 1 7 7 8
Why do these conversions work?
Notes: Answer 1:
6 3 5 . 1 7 7 8
110|011|101 . 001|111|111 2
Regroup:
1|1001|1101 . 0011|1111|1(000)2
Convert:
1 9 D . 3 F 816
Answer 2: Marking off in groups of three (four) bits corresponds to dividing or multiplying by 23 = 8 (24 = 16) in the binary system.

## Slide 22: A Final Conversion Note
You can use arithmetic in other bases if you are careful:
Example: Convert 1011102 to Base 10 using binary arithmetic:
  Step 1 101110 / 1010 = 100 r 0110
  Step 2 100 / 1010 = 0 r 0100
  Converted Digits are 01002 | 01102
  or 4 6 10

## Slide 23: Binary Numbers and Binary Coding
Flexibility of representation
  Within constraints below, can assign any binary combination (called a code word) to any data as long as data is uniquely encoded.
Information Types
  Numeric
    Must represent range of data needed
    Very desirable to represent data such that simple, straightforward computation for common arithmetic operations permitted
    Tight relation to binary numbers
  Non-numeric
    Greater flexibility since arithmetic operations not applied.
    Not tied to binary numbers

## Slide 24: Binary Arithmetic
Single Bit Addition with Carry
Multiple Bit Addition
Single Bit Subtraction with Borrow
Multiple Bit Subtraction
Multiplication
BCD Addition

## Slide 25: Single Bit Binary Addition with Carry

## Slide 26: Multiple Bit Binary Addition
Extending this to two multiple bit examples:
Carries 0 0
Augend 01100 10110
Addend +10001 +10111
Sum
Note: The 0 is the default Carry-In to the least significant bit.
Notes: Carries 00000 01100
Augend 01100 10110
Addend +10001 +10111
Sum 11101 101101

## Slide 27: Single Bit Binary Subtraction with Borrow
Given two binary digits (X,Y), a borrow in (Z) we get the following difference (S) and borrow (B):
Borrow in (Z) of 0:
Borrow in (Z) of 1:
Z
1
1
1
1
X
0
0
1
1
- Y
-0
-1
-0
-1
BS
11
1 0
0 0
1 1
Z
0
0
0
0
X
0
0
1
1
- Y
-0
-1
-0
-1
BS
0 0
1 1
0 1
0 0

## Slide 28: Multiple Bit Binary Subtraction
Extending this to two multiple bit examples:
Borrows 0 0
Minuend 10110 10110
Subtrahend - 10010 - 10011
Difference
Notes: The 0 is a Borrow-In to the least significant bit. If the Subtrahend > the Minuend, interchange and append a – to the result.
Notes: Borrows 00000 00110
Minuend 10110 10110
Subtrahend –10010 –10011
Difference 00100 00011