## Slide 1: King Saud University College of Engineering IE – 341: “Human Factors Engineering” Fall – 2015 (1st Semester 1436-7H)
Chapter 1. Introduction
Prepared by: Ahmed M. El-Sherbeeny, PhD

## Slide 2: Human Factors: Overview
Successful design entails what man:
  Needs
  Wants (desires)
  Can use
Human factors investigated by designers:
  Anthropometry (Human physical size, limitations)
  Physiology: human body,
    Reactions (hearing, seeing, touching, etc.)
    Functions
    Limitations
    Capabilities
  Ergonomics (“doing” vs. anthropometry: “being”)
    dynamic interaction of operator and machine
  Psychology: influence of mental conditions
  Others: social, climate, religion, etc.

## Slide 3: Cont. Human Factors: Overview
Objectives of Human Factors (HF):
  Increase work efficiency
    Increase effectiveness of work
    Increase convenience and ease of use of machines
    Increase productivity
    Decrease errors
  Study influence of design on people
  Change designs to suit human needs, limitations
  Increase human values:
    Increase safety
    Increase comfort
    Increase job satisfaction
    Decrease fatigue and stress
    Increase quality of life

## Slide 4: Human factors, definitions
Definition 1:
  Systematic application of information about human:
    Capabilities, limitations, and characteristics to the design of:
    objects and procedures that people use,
    and the environment in which they use them
Definition 2:
  HF discovers and applies information about human:
    Behavior, abilities, limitations, other characteristics to the design of:
    tools, machines, systems, jobs, tasks, environments for:
    productive, safe, comfortable, effective human use

## Slide 5: Human Factors: Characteristics
HF involves study of:
  Human response to environment
  Response as a basis for design, improvements
Characteristics of HF:
  Machines must be built to serve humans (not opp.)
  Design must take human differences into account
  Designs influence humans
  Design process must include data and calculations
  Human data must be tested scientifically
  Humans and machines are related
  NOT just check lists and guidelines
  NOT: using oneself as model for design
  NOT just common sense

## Slide 6: Human Factors: History (US)
Early 1900’s: Frank and Lilian Gilbreth:
  Design of workstations for disabled (e.g. surgery)
After WWII (1945): HF profession was born
1949: HF books, publications, conferences, e.g.:
  HF in Engineering Design, 1949
  HF Society (largest HF professional group), 1957
1960-80: emphasis moved from military to industry:
  Pharmaceuticals, computers, cars, etc.
1980-90: HF in PC revolution
  “ergonomically-designed” equipment, software
  HF in the office
  Disasters caused due to HF considerations
    e.g. Chernobyl, Soviet Union, 1986
  HF in forensics (injury litigations, defective designs)
>1990’s:
  Medical devices, devices for elderly
  OSHA ergonomic regulations

## Slide 7: Human Factors: Profession
HF Society members:
  Psychology: 45.1%
  Engineering: 19.1%
People performing HF work (in general)
  Business (private): 74%
  Government: 15%
  Academia: 10%

## Slide 8: Human-Machine Systems
System (Defn):
  “Entity that exists to carry out some purpose”
  Components: humans, machines, other entities
  Components must integrate to achieve purpose (i.e. not possible by independent components):
    Find, understand, and analyze purpose
    Design system parts
    System must meet purpose
Machine (Defn):
  Physical object, device, equipment, or facility
  used to perform an activity
Human-Machine system (Defn):
  ≥1 Human + ≥1 physical component
  Interaction using given input/command
  Result: desired output
  e.g. man + nail + hammer to hang picture on wall
  See Figure 1-1, pp. 15 (Sanders and McCormick)

## Slide 9: Cont. Human-Machine Systems
Types of HM systems:
  Manual systems:
    operator + hand tools + physical energy
  Mechanical systems (AKA semiautomatic systems):
    operator (control) + integrated physical parts e.g. powered machine tools
  Automated systems:
    little or no human intervention (e.g. Robot)
    Human: installs programs, reprograms, maintains, etc.
  Consider broomstick vs vacuum vs RoombaTM

## Slide 10: HM System Characteristics
Systems are purposive
  Systems have ≥ 1 objective
Systems can be hierarchical
  Systems may have subsystem levels (1, 2, etc.)
Systems operate in environment (i.e. inside boundary)
  Immediate (e.g. chair)
  Intermediate (e.g. office)
  General (e.g. city)
Components serve functions
  Sensing (i.e. receiving information; e.g. speedometer)
  Information storage (i.e. memory; e.g. disk, CD, flash)
  Information processing and decision
  Action functions (output)
    Physical control (i.e. movement, handling)
    Communication action (e.g. signal, voice)
  See Figure 1-2, pp. 17 (Sanders and McCormick)

## Slide 11: HM System Characteristics
Sensing
(information receiving)
Information processing and decision
Action Function
(physical control or communication)
Information Storage
Info input
Info output

## Slide 12: Cont. HM System Characteristics
Components interact
  components work together to achieve a goal
  components are at lowest level of analysis
Systems, subsystems, components have I/O
  I: input(s)
  O: output(s)
  O’s of 1 system: can be I’s to another system
  I’s:
    Physical (materials)
    Mechanical forces
    Information

## Slide 13: Types of HM Systems
Closed-loop systems
  Require continuous control
  Require continuous feedback (e.g. errors, updates, etc.)
  e.g. car operation
Open-loop systems
  Need no further control (e.g. car cruise-control)
  Feedback causes improved system operation

## Slide 14: System Reliability
Defn: “probability of successful operation”
Measure #1:
  success ratio
  e.g. ATM gives correct cash: 9999 times out of 10,000 ⇒ Rel. = 0.9999
  Usually expressed to 4 d.p.
Measure # 2:
  mean time to failure (MTF)
  i.e. # of times system/human performs successfully (before failure)
  Used in continuous activity

## Slide 15: System Rel.: Components in Series
Successful operation of system ⇒ Successful operation of ALL components (i.e. machines, humans, etc.)
Conditions:
  Failure of 1 component ⇒ failure of complete system!
  Failures occur independently of each other
Rel. of system = Product of Rel. of all components
e.g. System has 100 components
  components all connected in series
  Rel. of each component = 99%
  ⇒ Rel. of system = 0.365 (why?)
  i.e. system will only work successfully: 365 out of 1,000 times!
  Conclusions:
    more components ⇒ less Rel.
    Max. system Rel. = Rel. of least reliable component
    least Rel. component is usually human component (weakest link)
    In reality, system Rel. ≪ least Rel. component

## Slide 16: System Rel: Components in Parallel
≥2 components perform same functions
  AKA: backup redundancy (in case of failure)
System failure ⇒ failure of ALL components
e.g. System has 4 components
  components connected in //
  Rel. of each = 0.7
  ⇒ System Rel. = 1 – (1-Relc1)(1-Relc2)(1-Relc3)(1-Relc4) = 0.992
  Conclusions
    more components in // ⇒ higher Rel.
  Note, Rel. ↓ with time (e.g. 10-year old car vs. new)