## Slide 1: Introduction
Sections:
The Nature of Work
Defining Work Systems
Types of Occupations
Productivity
Organization of the Book
Chapter 1

## Slide 2: Historical Figures Related to Work
Eli Whitney (1765-1825)
  Interchangeable parts manufacture
Henry Ford (1863-1947)
  Moving assembly line
Frederick W. Taylor (1856-1915)
  Scientific management
  Time study
Frank (1868-1924) & Lillian Gilbreth (1878-1972)
  Motion study
Notes: Time and Motion Study: دراسة الوقت والحركة

## Slide 3: Work
Is our primary means of livelihood
Serves an important economic function in the global world of commerce
Creates opportunities for social interactions and friendships
Provides the products and services that sustain and improve our standard of living

## Slide 4: Introduction
The Nature of Work

## Slide 5: The Nature of Work
Work is an activity in which one exerts physical and mental effort to accomplish a given task or perform a duty
Task or duty has some useful objective
Worker applies skills and knowledge for successful completion
The activity has commercial value
The worker is compensated
Notes: Definition 1

## Slide 6: Work (Physics Definition)
The displacement (distance) that an object moves in a certain direction multiplied by the force acting on the object in the same direction.
Units of measurement:
  Newton-meters (N-m) in the International System of Units (metric system)
  Foot-pounds (ft-lb) in U.S. customary units
Notes: 2. W = F * D

## Slide 7: The Pyramidal Structure of Work
Work consists of tasks
  Tasks consist of work elements
    Work elements consist of basic motion elements

## Slide 8: Task
An amount of work that is assigned to a worker or for which a worker is responsible
Repetitive task – as in mass production
  Time required = 30 seconds to several minutes
Non-repetitive task – performed periodically, infrequently, or only once
  Time required usually much longer than for repetitive task

## Slide 9: Work Element
A series of work activities that are logically grouped together because they have a unified function in the task
Example: assembling a component to a base part using several nuts and bolts
Required time = six seconds or longer

## Slide 10: Basic Motion Elements
Actuations of the limbs and other body parts
Examples:
  Reaching for an object
  Grasping the object
  Moving the object
  Walking
  Eye movement
A work element consists of multiple basic motion elements
Notes: Actuation: تنفيذ أو تشغيل

## Slide 11: Pyramidal Structure of Work
Extended to a worker’s career
Notes: Q: What’s the difference between job and career?

## Slide 12: Importance of Time
In many human endeavors, “time is of the essence”
  In sports
  In daily living
  In business and industry
  In work

## Slide 13: Time in Business and Industry
New product introduction
Product cost
Delivery time
Overnight delivery
Competitive bidding
Production scheduling
Notes: Personal note, production is one of the most important intersections between HFE and other IE disciplines

## Slide 14: Importance of Time in Work
Time is the most frequently used measure of work
  How many minutes or hours are required to perform a given task?
Most workers are paid by the time they work
  Hourly wage rate
  Salary
Workers must arrive at work on time
Labor and staffing requirements computed in units of time

## Slide 15: Introduction
Defining Work Systems

## Slide 16: Work System Defined
As a physical entity, a work system is a system consisting of humans, information, and equipment designed to perform useful work
Contributes to the production of a product or delivery of a service
Examples:
  Worker operating a machine tool in a factory
  Robotic welding line in an automobile plant
  Parcel service agent driving a delivery truck to make customer deliveries
  Designer working at a CAD workstation
Notes: i.e. work system is a type of human machine system, the essence of HFE

## Slide 17: A Work System as a Physical Entity

## Slide 18: Work System Defined
As a field of professional practice, work systems include:
Work methods – analysis and design of tasks and jobs involving human work activity
Work measurement – analysis of a task to determine the time that should be allowed to perform the task
Work management – organizational and administrative functions that must be accomplished to achieve high productivity and effective supervision of workers

## Slide 19: Introduction
Types of Occupations

## Slide 20: Jobs and Occupations
Bureau of Labor Statistics of the U.S. Department of Labor identifies 821 occupations in its Standard Occupational Classification (SOC)
The SOC covers virtually every type of work performed for pay or profit in the United States
Occupations are organized into 23 major groups
Groups are established on the basis of type of work and/or the industry in which it is performed

## Slide 21: Jobs and Occupations
Four broad categories that reflect the work content and job function:
  Production workers - make products
  Logistics workers - move materials, products, or people
  Service - provide a service, apply existing information and knowledge, communicate
  Knowledge workers - create new knowledge, solve problems, manage
Notes: Logistics: الإمدادات

## Slide 22: Comparisons: Industries and Workers
Production workers
  Manufacturing, construction, agriculture
Logistics workers
  Transportation, distribution, material handling
Service workers
  Banking, retail, government, health care
Knowledge workers
  Management, engineering, legal, consulting, education

## Slide 23: Comparisons: Worker Discretion
Refers to the need to make responsible decisions and exercise judgment in carrying out duties of the position
Jobs that are highly standardized and routine require minimum worker discretion
  Typical for production and logistics workers
Jobs in which workers must adapt their behavior in response to variations in the work situation require high discretion
  Typical for service and knowledge workers

## Slide 24: Introduction
Productivity

## Slide 25: Productivity
The level of output of a given process relative to the level of input
Process can refer to
  Individual production or service operations
  A national economy
Productivity is an important metric in work systems because
  Improving productivity is the means by which worker compensation can be increased without increasing the costs of products and services they produce

## Slide 26: Labor Productivity
The most common productivity measure is labor productivity, defined by the following ratio:
LPR =
where,
  LPR = labor productivity ratio,
  WU = work units of output,
  LH = labor hours of input
Notes: Watch this video on measures of productivity: https://youtu.be/pZdzYDVlC8c
Another –lengthy– very good video: https://youtu.be/JnBzMKIOm18

## Slide 27: Labor Factor in Productivity
Labor itself does not contribute much to improving productivity
More important factors:
  Capital - substitution of machines for human labor
  Technology - fundamental change in the way some activity or function is accomplished
Notes: Capital: رأس المال

## Slide 28: Examples of Technology Changes
Horse-drawn carts
Steam locomotive
Telephone operator
Dial phone
Manually operated milling machine
DC-3 passenger airplane (1930s)
Railroad trains
Diesel locomotive
Dial phone
Touch-tone phone
Numerically controlled (NC) milling machine
Boeing 747 passenger airplane (1980s)

## Slide 29: Capital versus Technology
Distinctions between capital improvements and technology improvements are often subtle
  New technologies almost always require capital investments
Important to recognize important gains in productivity are more likely to be made
  By the introduction of capital and technology in a work process
  Than by attempting to get more work in less time out of the workers

## Slide 30: Measuring Productivity
Not as easy as it seems because of the following problems:
  Nonhomogeneous output units
  Multiple input factors
    Labor, capital, technology, materials, energy
  Price and cost changes due to economic forces
  Product mix changes
    Relative proportions of products that a company sells change over time
Notes: Q: can you give an example of Product mix changes? (e.g. automobile companies)
product mix: the total range of products offered by a company

## Slide 31: Labor Productivity Index
Measure that compares input/output ratio from one year to the next
LPI =
Where
LPI = labor productivity index,
LPRt = labor productivity ratio for period t, and
LPRb = labor productivity ratio for base period

## Slide 32: Example: Productivity Measurement
During the base year in a small steel mill, 326,000 tons of steel were produced using 203,000 labor hours. In the next year, the output was 341,000 tons using 246,000 labor hours.
Determine: (a) the labor productivity ratio for the base year, (b) the labor productivity ratio for the second year, and (c) the productivity index for the second year.

## Slide 33: Example: Solution
(a) In the base year, LPR = 326,000 / 203,000
= 1.606 tons per labor hour
(b) In the second year, LPR = 341,000 / 246,000
= 1.386 tons per labor hour
(c) Productivity index for the second year
LPI = 1.386 / 1.606 = 0.863
Comment: No matter how it’s measured, productivity went down in the second year.

## Slide 34: Productive Work Content
A given task performed by a worker can be considered to consist of
Basic productive work content
  Theoretical minimum amount of work required to accomplish the task
Excess nonproductive activities
  Extra physical and mental actions of worker
  Do not add value to the task
  Do not facilitate the productive work content
  Take time

## Slide 35: Excess Nonproductive Activities
Can be classified into three categories:
Excess activities due to poor design of product or service
Excess activities caused by inefficient methods, poor workplace layout, and interruptions
Excessive activities caused by the human factor

## Slide 36: Allocation of Total Task Time

## Slide 37: Poor Design of Product or Service
Products with more parts than necessary, causing excess assembly time
Product proliferation
Frequent design changes
Waste of materials
Quality standards too stringent
Notes: Proliferation: تكاثر

## Slide 38: Inefficient Methods, Layout, Etc.
Inefficient layout that increases material handling activities
Inefficient workplace layout that increases hand, arm, and body motions
Methods that include unnecessary work elements that waste time
Long setup times in batch production
Frequent equipment breakdowns
Workers waiting for work

## Slide 39: The Human Factor
Absenteeism
Tardiness
Workers spending too much time socializing
Workers deliberately working slowly
Inadequate training of workers
Industrial accidents caused by human error
Hazardous materials that cause occupational illnesses
Notes: Tardiness: التأخر والبطأ

## Slide 40: Introduction
Organization of the Book

## Slide 41: Organization of the Book