## Slide 1: Microscopes
Function
Parts and Function
Different types

## Slide 2
Scale

## Slide 3: Function of Light compound microscope
Magnification:
Able to see and enlarge microorganisms that could not be seen by naked eye.
Resolution: resolve the image.

## Slide 4: Microscope Resolution
Resolution: The ability to distinguish between two points at short distances from each other.
wavelength of light used is major factor in resolution, shorter wavelength  greater resolution
Resolved
Not resolved
(same magnification)

## Slide 5: sTypes of Microscope
  Bright-field microscope
  Dark-field microscope
  Phase-contrast microscope
  Dissecting microscope
  Inverted microscope
All are compound microscopes
  image formed by action of 2 lenses

## Slide 6: The Bright-Field Microscope
Produces a dark image against a brighter background
Has several objective lenses
Uses ordinary bulb light as source of light.
Total magnification is 1000x
The resolution is 0.2µm
It is mainly used to examine stained preparations.

## Slide 7: Terms Related To Microscopes
Parfocal
Microscopes remain in focus when objectives are changed.
Total magnification
Product of the magnifications of the ocular lens and the objective lens.
To determine the magnification ; multiply the ocular lens by the objective lens
Ocular 10x Objective 40x :10 x 40 = 400

## Slide 8: Working Distance It is the Distance between the objective lens and surface of cover glass or specimen

## Slide 9: Bright field microscope parts

## Slide 10: Parts of Microscope
Ocular Lens/Eyepiece
Magnifies the specimen image 10x
Nose piece
The Nose Piece holds the objective lenses and can be turned to increase the magnification
Objective lens
The Objective Lenses increase magnification (4 or 5 =4x 10x 20x 40x 100x)

## Slide 11
Arm
Used to support the microscope when carried. Holds the body tube, nose piece and objective lenses
Slide holder
Holds the specimen in place. It has 2 clips
Stage
Supports the slide/specimen

## Slide 12
Stage control knobs
It moves stage forwards, backwards.
It moves stage right to left to adjust slide under objective lens.
Coarse adjustment Knob
It moves the stage rapidly to get approximate focusing.
Fine adjustment knob
It moves the stage slowly to get definite focusing

## Slide 13
Condenser
It condenses light rays into a cone shape to enter objective lens for proper illumination.
When using X40 or X100 lens raise the condenser up.
Iris diaphragm
It controls the ring of light that goes into condenser.
When using X100 lens open iris diaphragm.

## Slide 14: Using a light microscope: Immersion Oil
Microscope specimen is on a glass slide.
• Light passes through glass slide air lens
gets refracted
• At high magnification, this refraction (bending) of the light blurs the image
• To eliminate refraction between slide and lens:
Eliminate the air, replace with immersion oil
(Immersion oil same index of refraction as glass)

## Slide 16: The Dark-Field Microscope
Produces a bright image of the object against a dark background.
A special condenser condenses the light on specimen but of the objective lens
A cell or particle will deflect the light into the objective lens thus seen as bright shape against dark background.
It is used to observe living, unstained preparations especially to examine motility.

## Slide 17: Dark Field Microscope

## Slide 18: The Phase-Contrast Microscope
Excellent way to observe living cells in wet preparations.
It has special condenser and phase-plate which retards light waves that go through cells in specimen. This makes contrast between cells and background. The cells appear darker against a brighter background.

## Slide 19: Dissecting Microscope
It is also called stereo- type microscope
It has oculars and stage only.
It magnifies x10 only
It is useful in Mycology and Parasitology.

## Slide 20: Dissecting Microscope

## Slide 21: The Fluorescent Microscope
Exposes specimen to ultraviolet, violet, or blue light
Specimens usually stained with fluorochromes
Shows a bright image of the object resulting from the fluorescent light emitted by the specimen.
It is mostly in immunology for detection of antigen and antibody.

## Slide 23: Inverted microscope
Parts of this microscope are similar to bright field microscope except condenser is located above stage while objectives are below the stage.
There is a bigger working distance to allow use of cell culture flasks.
It is mostly used in virology.

## Slide 24: Electron Microscope
Electrons are used instead of light waves.
2 types:
  Transmission electron microscope
  Scanning electron microscope
Total magnification 100,000-300,000
Resolution .0003um
It is used to examine viruses and internal cell components.

## Slide 25: TEM

## Slide 26: SEM

## Slide 27: Caring for a Microscope
Clean only with a soft cloth/tissue
Make sure it’s on a flat surface
Be gentle with the microscope
Carry it with 2 HANDS…one on the arm and the other on the base