## Slide 1: 322 BCH
Method of Enzyme Assay

## Slide 2
Objective
To study the different methods for determining enzyme activity.

## Slide 3
Enzyme assays: Are laboratory methods for measuring enzymatic activity.
All enzyme assays measure either the consumption of substrate or production of product over time.
Different enzymes require different estimation methods depending on the type of reaction catalyzed, the nature of S and P or coenzyme.
S P + E
E

## Slide 4
1.Fluorescence methods: Using a fluorometer .
** e.g. NAD+ and NADP+ do not fluoresence in their oxidized forms, but the reduced form have a blue fluorescence reduction reaction.
2.Manometric methods: Using a manometer.
** It is suitable for reactions in which one of the component is a gas. e.g. Oxidases (O2 uptake), Decarboxylase(CO2 output)
Methods of quantitatively following enzyme reactions

## Slide 5
3. Eletrode Methods: Using a pH meter.
** Reactions which involve the production of acids where H+ conc. is measured.
4. Polarimetric Method: use polarimeter.
** For isomerases that convert one isomer to another.
e.g. D-glucose  L-glucose

## Slide 6
5. Spectrophotometric methods.
In spectrophotometric assays, you follow the course of the reaction by measuring a change in how much light the assay solution absorbs.

## Slide 7
Wavelength in this instrument is divided into:
-Invisible range(ultraviolet “UV”) from 100 to 360 nm
  [Quartz cuvette are used]
-Visible range (400 -700 nm)
  [Glass or plastic cuvette are used]
  [ If the light is in the visible region you can actually see a change in the color of the assay, these are called colorimetric assays ]
What is blank solution?
It is a solution that contains everything except the compound to be measured.

## Slide 8
1- cases in which product absorb but not the substrate.
e.g.
Fumarate malate
2- the Co-enzyme undergoes change in absorption upon reduction or oxidation
Oxidized form Reduced form
NAD NADH
NADP NADPH
Fumarate hydratase
When the Spectrophotometric methods can be used?
Light
UV. Light (340 nm)
If reduced form was product: increase the absorbance / min
If reduced form was substrate : decrease the absorbance / min

## Slide 9
Alanine transaminase (ALT)
ALT is an enzyme that catalyzes a type of reaction (transamination) between an amino acid and α-keto acid.
It is important in the production of various amino acids.

## Slide 10
ALT diagnostic importance
ALT is found in serum (at low level) but is most commonly is associated with the liver.
thus , an elevated level ALT is a sensitive index of acute hepatocellular injury.
Elevated serum ALT level are found in hepatitis, cirrhosis , and obstructive jaundice.
NORMAL RANGE OF ALT:
( up to 42 ) U/L  males ( up to 32 ) U/L  females

## Slide 11
Enzyme assays can be split into two types:
Continuous assays,
where the assay gives a continuous reading of activity.
Discontinuous (Endpoint) assays,
Where the reaction is stopped and then the concentration of substrates/products determined.
Both types of enzyme assays will be applied in this lab on ALT

## Slide 12
Principle of Continuous Assay
1- ALT “present in serum sample” catalyzes the transfer of an amino group from alanine to α-ketoglutarate in the following reaction:
Alanine + α- ketoglutarate → Pyruvate + glutamate
2- Then, the pyruvate formed in the reaction is reduced to L-Lactate by Lactate dehydrogenase (LDH) “found in ALT reagent”.
Pyruvate + NADH+H+ → L-Lactate+ NAD+ +H2O
3- The absorbance at 340nm is measured each minute without stopping the reaction, resulting in decreased readings due to the oxidation of NADH

## Slide 13
Principle

## Slide 14
Method
Pipette into clean and dry test tubes:
ALT Reagent | 3 ml
Pre-warm at 37°C for 3 minutes and add | 
Serum Sample | 0.2 ml
Mix and incubated at 37 °C for 1 minute, then read absorbance ( at 340 nm against distilled water ) every minute for 3 minutes) and determine ∆A/min | 
ml μl (x 1000)
Choose the following on the spectrophotometer:
2) Applications  2) Simple Kinetics  wave length (340 nm)  1) Seconds  Duration (180 sec = 3 min)  Intervals (60 sec= 1 min)  Print Data Table (off)  Press start (2 times)

## Slide 15
Results
DA/min=((A1-A2)+(A2-A3))/2 | Absorbance 340nm |  | Time
 |  | A1 | 1 min
 |  | A2 | 2 min
 |  | A3 | 3 min
ALT Activity ( U/L) = ΔA/min x 1768
ALT Activity (U/L) =
Calculations

## Slide 16
Principle of Discontinuous Assay
In this method ALT catalyzes the following reaction
Alanine + a-ketoglutarate  pyruvate + glutamate
ALT is assayed by following formation of pyruvate.
The addition of acidic 2,4-dinitrophenylhydrazine (DNPH) stops the reaction and forms the 2,4-dinitrophenylhydrazone. So that it may be measured at 546nm.

## Slide 17
Method:
 |  | BLANK | SAMPLE
ALT Reagent |  | 0.5 ml | 0.5 ml
Pre-warm at 37 C for 5 minutes and add: |  |  | 
Distilled Water | 0.1 ml |  | -
Serum Sample | - |  | 0.1 ml
Mix, and incubate at 37 C for exactly 30 minutes , and add: |  |  | 
Color Reagent (DNPH) | 0.5 ml |  | 0.5 ml
Mix, and return at 37 C for exactly 10 minutes, then add: |  |  | 
Color Developer (NaOH) | 5.0 ml |  | 5.0 ml
Mix, and return to 37 C for exactly 5 minutes. Read absorbance of all tubes at 546nm against blank. |  |  | 
Total time= 50 min

## Slide 18
COLOR REAGENT contains 1 N Hydrochloric acid which causes burns.
COLOR DEVELOPER contains 0.5 N Sodium hydroxide which is corrosive.
In case of contact, flush affected area with large amounts of water. Seek medical attention.
Precautions

## Slide 19
The data shown in the table is used to convert absorbance at 546 nm into enzymatic activity in U/L of serum.
Draw graph using the data in table with absorbance on the Y- axis and enzymatic activity in U/L on the X-axis.
Note: Don’t forget title of the graph “Standard Curve” and the x- axis and y- axis with their units
Results:
Absorbance at 546 nm | ALT activity (U/L)
0.025 | 2.5
0.050 | 5.5
0.075 | 9
0.100 | 12
0.125 | 17
0.150 | 21
0.175 | 25
0.2 | 30
0.225 | 35
0.250 | 41
-Absorbance at 546 nm = ………
-ALT (SGPT) activity (from graph)= …………U/L

## Slide 20
Discussion
  Mention the diagnostic importance of ALT
  Explain the difference in the principle of each ALT assay.
  Compare your result with ALT normal range [in males], and diagnose the patient's state (what disease could the patient have or not).