## Slide 1: VLSM
Variable Length Subnet Mask

## Slide 2: VLSM
If you borrow 4 bits on a Class C network, you end up with 14 valid subnets of 14 valid hosts. A serial link to another router only needs 2 hosts, but with classical subnetting, you end up wasting 12 of those hosts.
Variable-length subnet masking (VLSM) is the process of “subnetting a subnet” and using different subnet masks for different networks in your IP plan. What you have to remember is that you need to make sure that there is no overlap in any of the addresses.

## Slide 4
The steps to create an IP plan using VLSM for the network as follows:
Step 1 Determine how many H bits will be needed to satisfy the largest network.
Step 2 Pick a subnet for the largest network to use.
Step 3 Pick the next largest network to work with.
Step 4 Pick the third largest network to work with.
Step 5 Determine network numbers for serial links.

## Slide 5: Step 1 Determine How Many H Bits Will Be Needed to Satisfy the Largest Network
A is the largest network with 50 hosts.
If 2H – 2 = Number of valid hosts per subnet
Then 2H – 2 ≥ 50 Therefore H = 6 (6 is the smallest valid value for H)
Now have: NNHHHHHH

## Slide 6: Step 2 Pick a Subnet for the Largest Network to Use
You have 2 N bits to work with, leaving you with 2N or 22 or 4 subnets to work with:
NN = 00HHHHHH (The 6 H bits you need for Network A)
01HHHHHH
10HHHHHH
11HHHHHH
If you add all zeros to the H bits, you are left with the network numbers for the four subnets:
00000000 = .0
01000000 = .64
10000000 = .128
11000000 = .192

## Slide 7
Two borrowed H bits means a subnet mask of
11111111.11111111.11111111.11000000
or
255.255.255.192
or
/26
Pick one of these subnets to use for Network A.
The rest of the networks will have to use the other three subnets.

## Slide 8: Step 3 Pick the Next Largest Network to Work With
Network B = 27 hosts
Determine the number of H bits needed for this network:
2H – 2 ≥ 27 H = 5
Pick one of the remaining /26 networks to work with Network B.
For the purposes of this example, select the .128/26 network:
10000000
But you need only 5 H bits, not 6. Therefore, you are left with
10N00000

## Slide 9
you can create two smaller subnets from the original subnet:
10000000
10100000
Converted to decimal, these subnets are as follows:
10000000 =.128
10100000 =.160

## Slide 10
The original subnet mask of /24 was changed into /26 for Network A. You then take one of these /26 networks and break it into two /27 networks:
10000000 and 10100000 both have 3 N bits and 5 H bits.
The mask now equals:
11111111.11111111.11111111.11100000
or
255.255.255.224
or
/27
Pick one of these new sub-subnets for Network B:
10000000 /27 = Network B

## Slide 11: make sure the addresses are not overlapping with each other. So go back to the original table.

## Slide 12: Step 4 Pick the Third Largest Network to Work With
Networks C and Network D = 12 hosts each
2H – 2 ≥ 12 H = 4
You need 4 H bits to satisfy the requirements of Network C and Network D
select the other /27 network—.160/27
10100000 (The 1 in the third bit place is no longer bold, because it is part of the N bits.)
But you only need 4 H bits, not 5. Therefore, you are left with
101N0000
where
      10 represents the original pattern of subnetting.
      N represents the extra bit you have.
      00000 represents the 5 H bits you need for Network B
Because you have this extra bit, you can create two smaller subnets from the original subnet:
10100000 = .160
10110000 = .176

## Slide 13
These new sub-subnets will now have new subnet masks.
Each sub-subnet now has 4 N bits and 4 H bits, so their new masks will be
11111111.11111111.11111111.11110000
or
255.255.255.240
or
/28

## Slide 15: Step 5 Determine Network Numbers for Serial Links
All serial links between routers have the same property in that they only need two addresses in a network—one for each router interface.
Determine the number of H bits needed for these networks:
2H – 2 ≥ 2
H = 2
You need 2 H bits to satisfy the requirements of Networks E, F, G, and H.
You have two of the original subnets left to work with.
For the purposes of this example, select the .0/26 network: 00000000
But you need only 2 H bits, not 6. Therefore, you are left with
00NNNN00
where
00 represents the original pattern of subnetting.
NNNN represents the extra bits you have.
00 represents the 2 H bits you need for the serial links.

## Slide 16
Because you have 4 N bits, you can create 16 sub-subnets from the original subnet:
00000000 = .0/30
00000100 = .4/30
00001000 = .8/30
00001100 = .12/30
00010000 = .16/30
. . .
00111000 = .56/30
00111100 = .60/30
You need only four of them. You can hold the rest for future expansion or recombine them for a new, larger subnet:
00010000 = .16/30
. . .
00111000 = .56/30
00111100 = .60/30
All these can be recombined into the following:
00010000 = .16/28

## Slide 17: Going back to the original table, you now have the following:
Looking at the plan, you can see that no number is used twice. You have now created an IP plan for the network and have made the plan as efﬁcient as possible, wasting no addresses in the serial links and leaving room for future growth. This is the power of VLSM!

## Slide 18
Route Summarization

## Slide 19
A router that needs to advertise ten routes needs ten speciﬁc lines in its update packet. The more routes you have to advertise, the bigger the packet. The bigger the packet, the more bandwidth the update takes, reducing the bandwidth available to transfer data.

## Slide 20
Four-City Network Without Route Summarization

## Slide 21
Jeddah, Medina, and Dammam each have to advertise internal networks to the main router located in Mecca. Without route summarization, Mecca would have to advertise 16 networks to Riyadh. You want to use route summarization to reduce the burden on this upstream router.

## Slide 22: Step 1: Summarize Jeddah’s Routes
  172.16.64.0 = 10101100.00010000.01000000.00000000
  172.16.65.0 = 10101100.00010000.01000001.00000000
  172.16.66.0 = 10101100.00010000.01000010.00000000
  172.16.67.0 = 10101100.00010000.01000011.00000000
  Common bits: 10101100.00010000.010000xx
  172.16.64.0/22

## Slide 23
when sent to the upstream Mecca router, will tell Mecca: If you have any packets that are addressed to networks that have the ﬁrst 22 bits in the pattern of
10101100.00010000.010000xx.xxxxxxxx
then send them to me here in Jeddah.

## Slide 24: Step 2: Summarize Madina’s Routes
172.16.68.0 = 10101100.00010000.01000100.00000000
172.16.69.0 = 10101100.00010000.01000101.00000000
172.16.70.0 = 10101100.00010000.01000110.00000000
172.16.71.0 = 10101100.00010000.01000111.00000000
Common bits: 10101100.00010000.010001xx
172.16.68.0/22

## Slide 25: Step 3: Summarize Dammam’s Routes
172.16.72.0 = 10101100.00010000.01001000.00000000
172.16.73.0 = 10101100.00010000.01001001.00000000
172.16.74.0 = 10101100.00010000 01001010.00000000
172.16.75.0 = 10101100.00010000 01001011.00000000
172.16.76.0 = 10101100.00010000.01001100.00000000
172.16.77.0 = 10101100.00010000.01001101.00000000
172.16.78.0 = 10101100.00010000.01001110.00000000
172.16.79.0 = 10101100.00010000.01001111.00000000
Common bits: 10101100.00010000.01001xxx
172.16.72.0/21

## Slide 26: Four-City Network with Edge Cities Summarizing Routes

## Slide 28: Step 4: Summarize Mecca’s Routes
Take the routes that Jeddah, Madina, and Dammam sent to Mecca, and look for common bit patterns:
172.16.64.0 = 10101100.00010000.01000000.00000000
172.16.68.0 = 10101100.00010000.01000100.00000000
172.16.72.0 = 10101100.00010000.01001000.00000000
Common bits: 10101100.00010000.0100xxxx
you can create one summary route for Meccato send to Riyadh:
172.16.64.0/20
Mecca has now told Riyadh that in one line of a routing update, 16 different networks are being advertised.

## Slide 29
Four-City Network with Complete Route Summarization

## Slide 31: VLSM Subnetting Homework
In each question, find the best 3 efficient combinations of subnets.
1-You have network 192.168.1.0/24, and you want subnets to contain 100 hosts, 25 hosts and 6 hosts.
2- You have network 150.210.0.0/16, and you want subnets to contain 2000 hosts, 500 hosts and 100 hosts.
3- You have network 125.0.0.0/8, and you want subnets to contain 1000 hosts, 200 hosts and 100 hosts.
4- You have network 217.84.19.0/24, and you want subnets to contain 30 hosts, 10 hosts and 2 hosts.
5- You have network 180.32.64.0/23, and you want subnets to contain 120 hosts, 50 hosts and 10 hosts.
6- You have network 152.227.160.0/21, and you want subnets to contain 500 hosts, 80 hosts and 5 hosts.