## Slide 1
WASTEWATER – TYPES, CHARACTERISTICS & REGULATION
Definition of wastewater
Water that has been used
Can be polluted

## Slide 2
Types of wastewater
Domestic: wastewater by residential, shop houses, offices, schools etc. and normally generated from toilets, sinks and bathrooms.
Industrial: wastewater generated by industries. Quantity and quality depends on the type of industry
Storm water: rainwater, may contain pollutants

## Slide 3
Why treat wastewater?
Untreated wastewater harmful to health
Breeding sites for insects, pests and micro organisms
Can cause environmental pollution and affect ecosystem

## Slide 4
Wastewater Characteristics
Physical
Chemical
Biological

## Slide 5
Physical Characteristics
A. Colour:
depends mainly on the wastewater constituent
B. Odour:
not significant if aerobic. Anaerobic wastewater release hydrogen sulphide (smells like rotten egg)

## Slide 6
C. Temperature:
higher than water temperature due to the microbiological activities
D. Turbidity:
caused by the presence of solids mainly suspended solids (SS) from clay, sand, human waste and plant fibres

## Slide 7
6.4 Chemical Characteristics
A. Organic compounds:
Definition
All organic compounds contain carbon in combination with one or more elements.

## Slide 8
Properties of organic compounds
Usually combustible
Have lower melting and boiling points
Less soluble in water
Have very high molecular weight
Most organic compounds can serve as a source of food for micro-organisms

## Slide 9
Source(s):
Nature: fibres, vegetable oils, animal oils and fats, cellulose, starch, sugar.
Synthesis: a wide variety of compounds and materials prepared by manufacturing processes. E.g. DDT, polyvinyl chloride.
Fermentation: Alcohols, acetone, glycerol, antibiotics, acids.

## Slide 10
Classification of organic matter (difference in degradability)
Biodegradable organics
Non-biodegradable organics

## Slide 11
Biodegradable organics
Food for micro-organisms
Fast and easily oxidized by micro-organisms
e.g. starch, fat protein, alcohol, human and animal waste.

## Slide 12
Non-biodegradable organics
Difficult and much more longer to biodegrade
Or toxic to micro-organisms
e.g. PVC, pesticide, industrial waste, cellulose, phenol, lignic acid.

## Slide 13
Effect(s):
  Depletion of the dissolved oxygen in the water
    Destroying aquatic life
    Damaging the ecosystem
  Some organics can caused cancer
    Trihalomethane (THM-carcinogenic compound) are produced in water and wastewater treatment plants when natural organic compounds combine with chlorine added for disinfection purposes.

## Slide 14
Normally, wastewater has high organic content. The organic content are measured by Biochemical Oxygen Demand (BOD) and Chemical Oxygen Demand (COD) and the value is about 100 to 400 mg/L.

## Slide 15
What is Biochemical Oxygen Demand (BOD)?
Definition
The quantity of oxygen utilised by a mixed population of micro-organisms to biologically degrade the organic matter in the wastewater under aerobic condition

## Slide 16
BOD is the most important parameter in water pollution control
It is used as a measure of organic pollution as a basis for estimating the oxygen needed for biological processes, and as an indicator of process performance.

## Slide 17
Organic matter + O2 CO2 + H2O + new cells
BOD test, 5-day at 20oC
3-day at 30oC
microorganism

## Slide 18
Test method (BOD5 @ 20oC)
A water sample containing degradable organic matter is placed in a BOD bottle.
If needed, add dilution water (known quantity). Dilution water is prepared by adding phosphate buffer (pH 7.2), magnesium sulphate, calcium chloride and ferric chloride into distilled water. Aerate the dilution water to saturate it with oxygen before use.
Measure DO in the bottle after 15 minutes (DOi)
Closed the bottle and placed it in incubator for 5 days, at temperature 20oC
After 5 days, measure DO in the bottle (DOt).

## Slide 19: BOD bottle

## Slide 20
Calculation of BOD,
Where
BODt = biochemical oxygen demand,
mg/L
DOi = initial DO of the diluted wastewater
sample about 15 min. after preparation, mg/L
DOt = final DO of the diluted wastewater sample
after incubation for five days, mg/L
P = dilution factor

## Slide 21
P = dilution factor
=

## Slide 22
Why dilution is needed?
For a valid BOD test, the final DO should not be less than 1 mg/L. BOD test is invalid if DOt value near zero.
Dilution can decrease organic strength of the sample. By using dilution factor, the actual value can be obtained.
Dilution of wastes:
- By direct pipetting into 300 mL BOD bottle

## Slide 23
BOD Analysis
In aerobic processes (O2 is present), heterotrophic bacteria oxidise about 1/3 of the colloidal and dissolved organic matter to stable end products (CO2 + H2O) and convert the remaining 2/3 into new microbial cells that can be removed from the wastewater by settling.

## Slide 24
The overall biological conversion proceeds sequentially, with oxidation of carbonaceous material as the first step (known as carbonaceous oxygen demand):
Organic matter + O2 CO2 + H2O + new cells

## Slide 25
Under continuing aerobic conditions, autotrophic bacteria then convert the nitrogen in organic compounds to nitrates (known as nitrification oxygen demand)
and
Organic-Nitrogen Ammonia-Nitrogen (decomposition)
NH3 - N + O2 Nitrate-Nitrogen (nitrification)

## Slide 26: BOD curve
1 2 3 4 5 6 7 8 9 10
Ultimate Carbonaceous BOD,Lo
BOD (mg/L)
Day
5-day BOD
Carbonaceous BOD
Nitrogenous BOD

## Slide 27
The ultimate BOD (Lo) is defined as the maximum BOD exerted by the waste.
The carbonaceous oxygen demand curve can be expressed mathematically as
BODt = Lo (1-10-Kt)
Where
BODt = biochemical oxygen demand at
time t, mg/L
Lo = ultimate BOD, mg/L
t = time, days
K = reaction rate constant, day-1

## Slide 28
Determination of BOD K-Rate
Time (day) BODt (mg/L) [time/BODt]1/3
1 X [1/X]1/3
2 Y [2/Y]1/3
3 Z [3/Z]1/3
From the experiment results of BOD for various values of t, calculate [time/BODt]1/3 for each day.

## Slide 29
Plot [t/ BODt]1/3 versus t
Determine the intercept (A) and slope (B) from the plot.
Calculate K = 2.61 (B/A)

## Slide 30
BOD rate constant, per day
K (base 10)
k (base e)
K = k/2.3

## Slide 31
Effects of Temperature on Reaction Rates and Ultimate BOD
Reaction Rate Constant, K
- most biological processes speed up as the temperature increases and slow down as the temperature drops. The rate of utilization is affected by temperature

## Slide 32
the relationship for the change in the reaction rate constant (K) with temperature is expressed as
Where
KT = reaction rate constant at temperature T, per day
K20 = reaction rate constant at 20oC, per day
 = temperature coefficient = 1.047
T = temperature of biological reaction, oC

## Slide 33
Ultimate BOD (Lo)
where
TLo = ultimate BOD at temperature T,
mg/L
20Lo = ultimate BOD at 20oC, mg/L

## Slide 34
Example:
A BOD test was conducted on a domestic wastewater at 30oC. The wastewater portion added to a BOD bottle was 20 mL and the dissolved oxygen values listed below were measured.

## Slide 35
Time (days) DO (mg/L)
0 7.4
1 5.5
2 4.5
3 3.7
4 2.5
5 2.1
- Calculate values of BOD3
  Determine the BOD rate constant, K30
  Calculate values of BOD5 at 20oC

## Slide 36
Solution

## Slide 37
What is Chemical Oxygen Demand (COD)?
Definition
The quantity of oxygen needed to chemically oxidize the organic compound in sample, converted to carbon dioxide and water.
Commonly used to define the strength of industrial wastewaters

## Slide 38
Test Procedure
Add measured quantities of potassium dichromate, sulphuric acid reagent containing silver sulphate, and a measured volume of sample into a flask.
The mixture is refluxed (vaporized and condensed) for two hours. The oxidation of organic matter converts dichromate to trivalent chromium,

## Slide 39
Organic matter CO2
+ +
Cr2O72- H2O
+ +
H+ 2Cr3+

## Slide 40
The mixture is titrated with ferrous ammonium sulphate (FAS) to measure the excess dichromate remaining in sample.
A blank sample of distilled water is carried through the same COD testing procedure as the wastewater sample.

## Slide 41
COD is calculated from the following equation:
Normality of Fe(NH4)2(SO4)2
Where:
COD = chemical oxygen demand, mg/L
a = amount of ferrous ammonium sulphate
titrant added to blank, mL
b = amount of titrant added to sample, mL
 = volume of sample, mL
8000 = multiplier to express COD in mg/L of oxygen

## Slide 42
Example:
The results of a COD test for raw wastewater (50 mL used) are given. Volumes of FAS used for blank and the sample are 24.53 mL and 12.88 mL, respectively. The normality of FAS is 0.242. Calculate the COD concentration for the sample.

## Slide 43
Solution

## Slide 44
B. Inorganic compounds:
Definition
When placed in water, inorganic compounds dissociate into electrically charged atoms referred to as ions.
All atoms linked in ionic bond.

## Slide 45
Source(s):
May cover heavy metals, nutrients (nitrogen and phosphorus), alkalinity, chlorides, sulphur, and other inorganic pollutants.
Effect(s):
i. Diseases
- NO2-  “blue baby syndrome”
ii. Aesthetic
- Si+4  turbidity
iii. Disturb human activity such as the
formation of scale in boiler system and
excessive usage of soap
- Ca+2, Mg+2  hardness

## Slide 46
3. Biological Characteristics
The principal groups of microorganisms found in wastewater are bacteria, fungi, protozoa, microscopic plants and animals, and viruses. Most microorganisms (bacteria, protozoa) are responsible and are beneficial for biological treatment processes of wastewater.

## Slide 47
Pathogenic organisms are usually excreted by humans from the gastrointestinal tract and discharge to wastewater. Water-borne disease include cholera, typhoid, paratyphoid fever, and diarrhea. The number of pathogenic organisms in wasteaters is generally low in density and they are difficult to isolate and identify.
Therefore, indicator bacteria such as total coliform (TC) and fecal coliform (FC) are used as indicator organisms.

## Slide 48
6.6 Wastewater Quality Standards
Regulations in Environmental Quality (Wastewater and Industrial Effluent), 1978:
Sets standards for wastewater discharged from wastewater treatment plant and industrial effluent
Standard A and Standard B

## Slide 49
STANDARD A APPLIES
The catchment areas referred to in this regulation shall be the areas upstream of surface or above sub-surface water supply intakes, for the purpose of human consumption including drinking.

## Slide 50
STANDARD A - UPSTREAM
BOD

mg/l
SS

mg/l
COD

mg/l
Oil / grease - not detectable
STANDARD B - DOWNSTREAM
BOD



mg/l
SS

mg/l
COD

mg/l
Oil / grease

10 mg/l
UPSTREAM
DOWNSTREAM
STREAM
WATER INTAKE POINT
SEWAGE TREATMENT PLANT
RAW WATER IS PUMPED
TO WATER TREATEMENT PLANT
DISTRIBUTION OF
WATER SUPPLY