## Slide 1: 2.2 Water quality parameter
Can be divided into three types:
Physical
Chemical
Biological
Environmental Engineering

## Slide 2
Physical Parameters
a. Turbidity - measured in NTU/FTU
Source(s):
- Inorganic compounds such as clay, sand
- Organic compounds such as plant fibre, human waste
Effect(s):
- Aesthetic
- Adsorption point/centre for chemicals and micro-organisms
- Health aspect

## Slide 3
b. Odour and Taste
Source(s):
- Inorganic compounds such as minerals, metals, salts (all of them give taste to water but no odour)
- Organic compounds from petroleum and/or degradation of organic matters. (odour and taste)
Effect(s):
- Aesthetic
- Health problems [reaction from sources and other chemicals such as chlorine (Cl2)]

## Slide 4
c. Temperature - measured in oC or oF
Source(s):
- Effect from ambience
- Industrial activities - cooling system
Effect(s):
- Disturb biological activities such as micro-organism and aquatic life
- Chemical properties such as the degree of gas solubility, density and viscosity

## Slide 5
d. Suspended solid - measured in mg/L
Source(s):
- Inorganic compounds such as clay, sand
- Organic compounds such as plant fibre, human waste
Effect(s):
- Aesthetic
- Adsorption point/centre for chemicals and micro-organisms
- Health aspect

## Slide 6
Measurement of Total Solids (TS)
Evaporate a known volume of sample to dryness and weigh the residue. The total solid is expressed as milligrams per litre (mg/L).

## Slide 8
Measurement of Suspended Solids (SS)
Weigh a filter paper on an analytical balance.
Place the filter paper on the filter apparatus.
Apply vacuum and filter 100 mL (or a larger volume if total suspended matter is low) well mixed sample.

## Slide 9
Dry the filter paper in an oven at 103oC to 105oC for at least 1 hour.
After 1 hour, cool the filter paper in a desiccator and weigh.
Repeat the drying cycle until a constant weight is attained or until weight loss is less than 0.5 mg.

## Slide 11
Total Solid (mg/L) = Suspended Solid (mg/L)
+
Total Dissolved Solid (mg/L)
Suspended Solid (mg/L)
= [(A-B) x 1000] / volume of sample
Where:
A = weight of filter paper + suspended
matter
B = weight of filter paper

## Slide 12
Example:
A solid analysis is to be conducted on a sample taken from Sungai UTM as follows:
A Gosh crucible and a filter pad are dried to a constant mass of 25.439 g.
Two hundred millilitres of a well-shaken sample of the wastewater is passed through the filter.
The crucible, filter, pad and removed solids are dried to a constant mass of 25.645 g.
One hundred millilitres of the filtrate [water passing through the filter in (ii) above] is placed in an evaporation dish that had been pre-weighed at 275.419 g.
The sample in (iv) is evaporated to dryness and the dish and residue are weighed at 276.227g.

## Slide 13
Both the crucible from (iii) and the evaporation dish from (v) are placed in a muffle furnace at 550oC for an hour. After cooling, the mass of the crucible is 25.501 g and the mass of the dish is 275.944 g.
Obtain the suspended solids (mg/L), dissolved solids (TDS) (mg/L) and total solids (mg/L) in the sample.

## Slide 14
SOLUTION

## Slide 15
Chemical Parameters
a. Total dissolved solid (TDS)
- Solid left in water after the water is filtered and dried.
Source(s):
- Inorganic compounds - minerals, metals & gases
- Organic compounds – product from degradation of organic matters, organic gas
Effect(s):
- Cause taste, colour and odour problems
- Health aspect

## Slide 16
b. Organic compounds
Definition : All organic compounds contain carbon in combination with one or more elements.
Source(s):
- Nature: fibres, vegetable oils, animal oils and fats, cellulose, starch, sugar.
- Synthesis: a wide variety of compounds and materials prepared by manufacturing processes. E.g. DDT, polyvinylchloride.
- Fermentation: Alcohols, acetone, glycerol, antibiotics, acids.

## Slide 17
Effect(s):
  Depletion of the dissolved oxygen in the water
    Destroying aquatic life
    Damaging the ecosystem
  Some organics can caused cancer
    Trihalomethane (THM-carcinogenic compound) are produced in water and wastewater treatment plants when natural organic compounds combine with chlorine added for disinfection purposes.

## Slide 18
c. Inorganic compounds
Definition
When placed in water, inorganic compounds dissociate into electrically charged atoms referred to as ions.
All atoms linked in ionic bond.
Can be classified into two: metal and non-metal

## Slide 19
i. Metal – Non toxic and toxic
Non-toxic – Ca2+, Mn2+, Na+, Fe2+, Mg2+, Al3+, Cu2+, Zn2+
- dangerous for health if the concentration is high
Source(s):
Mineral, readily available from nature
Effect(s):
- Colour, odour, taste and turbidity
- Deteriorate health (at high concentration)

## Slide 20
Toxic – As2+, Ba2+, Cd2+, Cr2+, Pb2+, Hg2+
Source(s):
- Human activities such as mining and industries
Effect(s):
- Dangerous diseases such as cancer, abortion and deformation in new born baby

## Slide 21
ii. Non-metal – e.g. Si4+, Cl-, NO3-
Source(s): Mineral
Effect(s):
- Diseases
heavy metal, NO2-  “blue baby syndrome”
- Aesthetic
Si+4  turbidity
- Fluoride (F-)
  - Not good for health if it is taken in high concentration
  - Concentration of 1 mg/L is good for the growth of children teeth
  - Excessive concentration – colour on teeth and problem in bone growth

## Slide 22
d. Alkalinity
Definition : The quantity of ions in water to neutralise acid or a measure of water strength to neutralise acid.
Main constituents : bicarbonate (HCO3-), carbonate (CO32-), and hydroxide (OH-) ions.
Source(s):
- Mineral dissolved in water and air.
- Human activities such as detergent (in wastewater), fertilisers, pesticide etc.
Effect(s):
- Non pleasant taste
- Reaction between alkaline constituent and cation (positive ion) produces precipitation in pipe.

## Slide 23
e. Hardness
Definition : A measure of “multivalent” cations in water such as Ca2+, Mg2+, Fe2+, Mn3+.
Ca2+ and Mg2+ are very important
Source(s):
- Natural mineral on earth
Effect(s):
- Excessive soap usage
- Precipitate form on hardware
- Precipitate in pipe - temperature and pH increased

## Slide 24
Two kinds of hardness:
Carbonate hardness
Non-carbonate hardness