## Slide 1
<number>
2. Rock-Forming Minerals
Notes: CE 382 Geotechnical Engineering I 1st Semester 1436/1437 H
<number>
07/28/26

## Slide 2
<number>
We know from physics that atoms are composed of protons, neutrons, electrons. Elements are composed from the same kind of atoms, like gold. Compounds are formed of groups of different kinds of atoms (e.g. Sodium chloride).
Minerals: are naturally occurring (formed) inorganic chemical substance which has a definite chemical composition and a characteristic crystal structure.
Notes: CE 382 Geotechnical Engineering I 1st Semester 1436/1437 H
<number>
07/28/26

## Slide 3
<number>
Has a definite chemical composition
Has a definite characteristics crystal structure
Inorganic
Naturally formed
There are some exceptions to this. Some materials are still considered minerals even though they do not meet all these requirements like mercury.
For any substance to be considered as a mineral, it has to meet the following conditions:
Mineral-like substances that do not fulfill either the composition or crystal structure requirement of minerals are called mineraloids.

## Slide 4
<number>
Why do we care about minerals?
We do care about minerals because they are the building blocks of rocks.
Indeed, the kinds and amounts of the minerals and mineraloids present in the rock, together with textures resulting from the way they are packed are the most important properties used in classifying rocks.
Scientifically rocks are any naturally occurring (formed) solid materials, composed of one or more minerals (and/or mineraloids).

## Slide 5
<number>
However nearly 2500 minerals have been discovered so far. The abundance of minerals depends on the availability of the component elements that are available for its formation at or near the earth’s surface.
By the use of the 118 chemically elements known to exist on earth, it is theoretically possible to make millions of compounds.
Only 12 elements are sufficiently abundant. These elements collectively make up 99.23% of the entire crust. The fact that only 12 elements are abundant answer the discrepancy between the theoretically infinite number of minerals that should exist and the fact that only 2500 are actually exists.
Actually about 75% of earth crust is made of oxygen and silicon.
Elements Versus Minerals

## Slide 6
<number>
Elements
Oxygen O
Silicon Si
Aluminum Al
Iron Fe
Calcium Ca
Magnesium Mg
Sodium Na
Potassium K
Titanium Ti
Hydrogen H
Phosphorus P
Manganese Mu
Weight %
45.2
27.2
8.0
5.8
5.06
2.77
2.32
1.68
0.4
.14
.12
.09
Abundant Elements on Earth Crust
98%

## Slide 7
<number>
Actually because of the overwhelming abundance of oxygen and silicon, the silicate minerals which composed of those two elements are the most plentiful on earth. Thus silicates are called the ROCK-FORMING MINERALS.
Minerals can be classified into:
Silicates Minerals (rock-forming minerals)
Non-Silicates Minerals
Mineraloids

## Slide 8
<number>
Silicate Minerals
All silicate minerals posses the silicate oxyanion (Sio4)-4. The oxyanion resembles a tetrahedron as shown below because the four large oxygen ions are arranged so that their centers form the vertices of a tetrahedron. The small silicon cation sits among the four oxygen in the open space at the center of the tetrahedron.

## Slide 9
<number>
Silicate mineral structures are therefore controlled by the ways tetrahedra packed together.
Modern classification of silicate minerals is based on the way silicate tetrahedra are joined together as follows:
All four oxygens in a tetrahedron are shared with other tetrahedra. Examples: Feldspars and Quartz
1. Framework Silicates
Three oxygen in a tetrahedron are shared with other tetrahedron. Examples: Muscovite (Micas) chlorite, clay minerals, Serpentine.
2. Sheet Silicates
3. Chain Silicates
There are single, double, Triple chains. Two oxygens are shared Example: Pyroxenes and amphiboles

## Slide 10
<number>
4. Island Silicates
The tetrahedra remain as discrete units sharing no common oxygens. Example olivine and garnet.
Whether we have no, one, two, three or four oxygens shared is called the Degree of Polymerization.
By variations in the packing of the tetrahedra or by having another element besides the silicon (like Aluminum) we can have many hundreds of individual silicate minerals. Fortunately, just 11 common mineral groups account for more than 95% of all silicate minerals.

## Slide 11
<number>
Important Silicate Minerals
Quartz (framework)
Widely distributed mineral, most of sands and sandstone are composed largely of quartz.
Feldspar (framework)
The most abundant minerals (make up about 60% of earth’s crust).
Olivine (Isolated)
Occur mainly in igneous rocks.
Pyroxene (Chain)
Very large and complex group of minerals.
Amphibole (Chain)
Very large and complex group of minerals.
Micas (sheet)
Parent of clay minerals.

## Slide 12
<number>
NONSILICATE MINERALS
Although there are many compositional families, only eight in addition to the silicates are important
1. THE OXIDE MINERALS
The most widespread group
of minerals after silicates.
Ex. Magnetite, Hematite
2. THE HYDROXIDE MINERALS
Ex. Gibbsite
3. THE SUPHIDE MINERALS
Ex. Pyrite
4. THE SULFATE MINERALS
Ex. Gypsum, Anhydrite
5. THE CARBONATE MINERALS
Ex. Calcite, Dolomite
6. THE PHOSPATE MINERALS
Ex. Apatite
7. THE HALIDE MINERALS
Ex. Halite (rock-salt)
This type of rock causes very serious problems in the city of Jizan
8. THE NATIVE ELEMENTS
Ex. Graphite, Native Metals
9. MINERALOIDS
Ex. Glass

## Slide 13
<number>
CLAY MINERALS
One of the common silicate minerals with sheet structures are the clay minerals. They formed mainly by the alteration of the minerals, by the action of weathering (of course chemical). The chemical process results in changes in the mineral form of the parent rock due to the action of water (especially if it contains traces of acid or alkali, oxygen, and carbon dioxide).
Clay minerals can be defined as:
They are crystalline particles (Predominantly silicates of Aluminum and/or Iron and Magnesium) resulted from the chemical weathering of parent rocks, mainly:
Feldspars
Mica (Muscovite).

## Slide 14
<number>
Characteristics of Clay Minerals
They have colloidal size (less than 0.002 mm)
Very electrochemically active
Have affinity for water
Gs between 2.0 and 3.0
They have high specific surface (surface area/mass)
Low hardness
Become plastic when mixed with water
The particles are platy, sometimes they are needle or tabular

## Slide 15
<number>
Structure of Clay Minerals
Clay minerals (and hence clay) consist of two fundamental units (basic structural units or building blocks)
1. Sheets of Silicon-Oxygen tetrahedra (silica tetrahedra)
2. Sheets of Aluminum or Magnesium octahedra
Silica Tetrahedron
Silica Sheet
Aluminum Octahedron
Octahedral (Gibbsite) Sheet

## Slide 16
<number>
Each octahedron unit consist of Aluminum or Magnesium cations linked to six hydroxyl anions.
The combination of octahedral units forms a sheet called GIBBSITE if the metalic atom is mainly AL+3 and BRUCITE if it is Mg+2.
The way in which the tetrahedra sheets and octahedral sheets are stacked together with different bonding and different metallic ions form the different clay minerals.

## Slide 17
<number>
Silica Sheet
Gibbsite Sheet
Gibbsite Sheet
Silica Sheet

## Slide 18
<number>

## Slide 19
<number>
Common Clay Minerals
i. KAOLINITE
It consists of alternating layers of Silica and Gibbsite sheets in a 1:1 lattice.
The layers are held together by hydrogen bonding
A kaolinite particles may consist of over 100 stacks
The thickness of the basic unit is 7 Angstroms
The least active of the clay minerals
Specific surface = 15 m2/g
ii. ILLITE
It consists of Gibbsite sheets sandwiched between two layers of Silica sheets.

## Slide 20
<number>
iii. MONTMORILLONITE
It has the same basic structure as Illite, the differences are:
- No potassium ions are present
- The units are held together by H+ ions and occasional Na+ ions
- The space between the units is occupied by water molecules.
Bentonite is a commercial name
very active
Specific Surface = 800 m2/g
Particles have thickness from 10 to 50 Angstroms
The combined sheets are held together by K+ ion
Moderately active
Specific Surface = 80 m2/g
Particles have thickness from 50 to 500 Angstroms