## Slide 1
<number>
226 PHT
Lab # 1

## Slide 2
<number>
Basic Microbiology
Microbiology is the science that deals with the study of too small organism (micro-organisms) that are invisible to the naked eye

## Slide 3
<number>
Laboratory Rules and Safety

## Slide 4: Instructions and Rules
<number>
☠ No eating or drinking.
☠ Lab coat & marker.
☠ Aseptic technique.
☠ Benches must be disinfected.
☠ ☠ Avoid contamination.
(Discarded cultures & infectious materials and broken or spilled living cultures).
Notes: <number>

## Slide 5
<number>
☠ Microscope.
☠ At the end of each lab check:
    Gas tap is turned off.
    Water tap is closed properly.
    Microscope lamp is turned off.
☠ Finally wash your hands thoroughly.

## Slide 6: Introduction to Microbiological Equipments and Materials
<number>
Medium:-
❊ An artificial preparation contains the essential elements and nutrients needed by the m.o to grow (media)

## Slide 7: Culture media
<number>
❊ It may be:
Liquid (broth)
Solid (containing agar)
Semisolid (containing low conc. of agar)

## Slide 8: Introduction to Microbiological Equipments and Materials
<number>
Inoculation: Culturing of sterile media with m.o [Inoculation loop].
Incubation: Placing the culture into the incubator at optimum temperature for growth.
Sterile: Free from any living microorganism
Contamination: Introduction of undesirable m.o.

## Slide 9
<number>
Sterilization:
Killing or removal of all living micro-organisms (from a particular location or material).
Sterile article: completely free of all living micro-organisms
Disinfection:
Destruction of vegetative conspiring micro-organisms.
.
Notes: <number>

## Slide 10
<number>
Disinfectants:
Chemicals which cause disinfection
Bacterial spores, mycobacteria, some viruses → considerable resistance
Antiseptics:
Disinfectants which can be safely applied to skin & mucous membranes.
Notes: <number>

## Slide 11
<number>
Contamination:
Introduction of undesirable m.o.
Asepsis:
Processes designed to prevent m.o. from reaching a protected environment.
Aseptic technique: Practices used by microbiologists to exclude all organisms from contaminating media or contacting living tissues.
Notes: <number>

## Slide 12
<number>
Discard cultures and other infectious materials:
Petri dishes→ Plastic bag → Autoclave.
Test tube cultures → wire basket → Autoclave.
Used pipettes → Plastic bag → Autoclave.
Used slides, covers, and pipettes → Jar containing a disinfectant.
Broken glass → swept in a dustpan → container for broken glass.
NEVER place contaminated material in waste basket.
Notes: <number>

## Slide 13
<number>
Broken or spilled living cultures:
Clothing → Autoclave plastic bag → Autoclave.
Flood the area with a disinfectant ( or paper towels are placed over the spills).
After 20- 30min→ wipe up & discard the waste in autoclavable dustpan→ Autoclave.
Notes: <number>

## Slide 14
<number>
Microscopical Examination:
Characters of cells.
Identification of Bacteria
Macroscopical Examination:
Characters of colonies.

## Slide 15
<number>
Biochemical Tests.
Identification of Bacteria
Additional Tests:
such as seriological tests

## Slide 16: Colony vs. Cell
<number>
Colonies
Cells

## Slide 17: Colony vs. Cell
<number>
Colonies
Cells

## Slide 18: The Microscope
<number>
The microscope is the most important tool used for examination and identification of microorganisms.

## Slide 19: The Microscope
<number>
Uses of microscope:
Identification of microbial groups. (Bacterial, Fungi, Protozoa)
Morphological studies of m.o
(size, shape, arrangement…..)
3. Physiological studies
(motility ….)

## Slide 20: The Microscope
<number>
Types of microscopes:
Optical microscope:
    Use light beams and lenses
    The most common one used in the lab
2. Electronic microscope:
    Use electron beams and magnetic fields
    Used for examination of viruses and sections of bacteria

## Slide 21: Optical microscope vs. Electronic microscope
<number>
Electronic microscope
Optical microscope

## Slide 22
<number>
Optical microscope vs. Electronic microscope
Electronic microscope
Optical microscope

## Slide 23: Optical microscope vs. Electronic microscope
<number>
Electronic microscope
Optical microscope

## Slide 24: The Microscope
<number>
Optical microscope:
There are two types
a- Simple microscope: single system of lenses
  b- Compound microscope: has two lens system, the ocular lens and the objective lens
The two lenses system give greater magnification

## Slide 25: Components of the compound microscope
<number>
Ocular lens
Objective lens
Lamp box
Iris diaphram
Stage
Coarse
adjustment
Fine adjustment
Slide movement knob

## Slide 26: Theoretical principles of microscopy
<number>
Magnification:
It means enlargement of the linear diameter of an object.
It is the function of two lens system [the ocular and the objective lens]

## Slide 27: Theoretical principles of microscopy
<number>
Total magnification =
mag. power of ocular lens X mag. power of objective lens used
N.B (oil immersion lens is used)
Objective lens mag. Power
Scanning lens 4×
Low power objective lens 10×
High power objective lens 40×
Oil immersion lens 100×

## Slide 28: Theoretical principles of microscopy
<number>
The magnification power of ocular lens (eye piece) is 10×
The total magnification will be 40, 100, 400, 1000 times.

## Slide 29: Theoretical principles of microscopy
<number>
Working distance:
It is the distance between the objective lens and the slide.
General rule, as the magnification of the lens increase the working distance decrease.

## Slide 30: Theoretical principles of microscopy
<number>
Resolution:
It is the ability of a lens to reveal two closely adjacent points as separate and distance.
The resolving power of the oil immersion lens depends on the addition of special oil (Ceder wood oil) between the specimen slide and the objective lens.

## Slide 31: Resolution:
<number>
Higher Resolution; note the “Sharpness” of the Image.
Lower Resolution; it is less sharp.
Which image is least resolved?

## Slide 32: Oil Immersion Increases Resolution
The Mineral Oil has the same Index of Refraction as glass (so light does not bend).
Air has a different Index of Refraction from glass (so light bends).
Air has a different Index of Refraction from water (so light bends).
Notes: <number>

## Slide 33
<number>
oil
Objective lens
Lost light
Saved light
specimen
Light source

## Slide 34
<number>
Thank you