## Slide 1: King Saud University College of Engineering IE – 341: “Human Factors Engineering” Fall – 2017 (1st Sem. 1438-9H)
Chapter 3. Information Input and Processing
Part 1: Information Display – Coding
Prepared by: Ahmed M. El-Sherbeeny, PhD

## Slide 2: Chapter Overview
Information Processing and Compatibility
Information Display – Coding (Ch. 3)
Fitts’ Law (Ch. 3, Ch. 9)
Hick Hyman Law (Ch. 3)
Signal Detection Theory (Ch. 3)
Memory - Attention (Ch. 3)
Compatibility - Part 1 - Spatial Compatibility (Ch. 10)
Compatibility - Part 2 - Movement - Modality Compatibility (Ch. 10, Ch.3)

## Slide 3: Lesson Overview
Information Display and Coding (Chapter 3)
Displaying Information
  Information Presented by Displays
  Selection of Display Modality
Coding of Information
  Coding
  Characteristics of a Good Coding System
Compatibility
  Conceptual Compatibility
  Movement Compatibility
  Spatial Compatibility
  Modality Compatibility

## Slide 4: DISPLAYING INFORMATION
Human information input and processing depends on the sensory reception of relevant external stimuli which contain the information
The original source of information (the distal stimulus) is some object, event, or environmental condition
Information from the distal stimulus may come to us:
  directly (e.g. direct observation of plane), or
  indirectly (e.g. radar or telescope)

## Slide 5: Cont. DISPLAYING INFORMATION
In the case of indirect sensing, the new distal stimuli may be
  coded stimuli (e.g. visual or auditory displays), or:
  reproduced stimuli (e.g. TV, radio, hearing aids)
  In both cases the coded or reproduced stimuli become the actual distal stimuli to the human sensory receptors
Human factors are required when indirect sensing applies
Display is a term that applies to any indirect method of presenting information (e.g. highway traffic sign, radio)

## Slide 6: INFORMATION PRESENTED BY DISPLAYS (General)
Information presented by displays can be dynamic or static.
Dynamic information:
  changes continuously or is subject to change through time
  e.g.: traffic lights, radar displays, temperature gauges
Static information:
  remains fixed over time
  e.g.: alphanumeric data, traffic signs, charts, graphs, labels
  Note that static information presented through VDT’s (video display terminals) is considered static information.

## Slide 7: INFORMATION PRESENTED BY DISPLAYS (Detailed)
Quantitative: such as temperature or speed
Qualitative: represents approximate value, trend or rate of change
Status: reflects the condition of a system
  e.g.: on or off, traffic lights
Warning and signal: indicating danger or emergency

## Slide 8: INFORMATION PRESENTED BY DISPLAYS (Detailed)
Representational: pictorial or graphical representation of objects, areas, or other configurations
  e.g. photographs, maps, heartbeat oscilloscope
Identification: used to identify a condition, situation or object
  e.g. traffic lanes, colored pipes
Alphanumeric* and symbolic:
  e.g. signs, labels, printed material, computer printouts
Time-phased:
  Display of pulsed or time-phased signals
  The duration and inter-signal intervals are controlled
Notes: * note, “alpha” comes from letters and “numeric” comes from numbers

## Slide 9: SELECTION OF DISPLAY MODALITY
Visual or auditory displays? Tactual sense? The selection of the sensory modality depends on a number of considerations
Table 3.1 helps in making a decision regarding visual or auditory presentation of information*
Notes: * This is, of course, highly associated with modality compatibility

## Slide 10: CODING OF INFORMATION
Coding takes place when the original stimulus information is converted to a new form and displayed symbolically
Examples are:
  radar screens where the aircrafts are converted and presented as dots on the screen
  maps displaying populations of different cities with different symbols.

## Slide 11: CODING OF INFORMATION (Cont.)
Information is coded along various dimensions
Examples:
  Varying the size, brightness, color and shape of targets on a computer screen
  Varying the frequency, intensity, or on-off pattern of an audio warning signal
Each of the above variations constitutes a dimension of the displayed stimulus, or a stimulus dimension

## Slide 12: CODING OF INFORMATION (Cont.)
The usefulness of any stimulus dimension in conveying information depends on the ability of people to:
  Identify a stimulus based on its position along the stimulus dimension (such as identifying a target as bright or dim, large or small)
    This is an example of absolute judgment* (see below)
  Distinguish between two or more stimuli which differ along the stimulus dimension (such as indicating which of the two stimuli is brighter or larger)
    This is an example of relative judgment*
Notes: * people are generally able to make fewer discriminations on an absolute basis than on a relative basis. For example, Mowbray and Gebhard (1961) found that people could discriminate on a relative basis about
1800 tone pairs differing only in pitch. On an absolute basis, however, people can identify only about 5 tones of different pitch.

## Slide 13: CHARACTERISTICS OF A GOOD CODING SYSTEM
Detectability of codes:
  stimulus must be detectable by human sensory mechanisms under expected environmental conditions
  e.g. is worker able to see the control knob in mine?
Discriminability of codes:
  every code symbol must be discriminable (differentiable) from other symbols
  the number of coding levels is important
Meaningfulness of codes:
  coding system should use codes meaningful to user
  Meaning could be
    inherent in the code (e.g. bent arrow on traffic sign)
    or learned (e.g. red color for danger)
  Meaningfulness: related to conceptual compatibility
Notes: Note, the topics of coding and compatibility will be revisited several time during the course (e.g. when discussing vision, hearing, controls, etc.)

## Slide 14: CHARACTERISTICS OF A GOOD CODING SYSTEM (cont.)
Standardisation of codes:
  when a coding system is to be used by different people in different situations, it is important that the codes be standardised, and kept the same for different situations
  e.g. meaning of the red color in different parts of a factory
Use of multidimensional codes:
  this can increase the number and discriminability of coding stimuli used
  e.g. using different size-color combinations greatly increases the number of stimuli that can be identified on an absolute basis*
Notes: * Refer back to Table 3-2 for absolute discrimination

## Slide 15: COMPATIBILITY
It is the relationship between the stimuli and the responses to human expectations
A major goal in any design is to make it compatible with human expectations
It is related to the process of information transformation
  the greater the degree of compatibility, the less recording must be done to process information
  This leads to faster learning and response time, less errors, and reduced mental workload
  People like things that work as they expect them to work
Notes: Note, the topics of coding and compatibility will be revisited several time during the course (e.g. when discussing vision, hearing, controls, etc.)

## Slide 16: COMPATIBILITY (Cont.)
Four types of compatibility:
  Conceptual
  Movement
  Spatial
  Modality
1. Conceptual compatibility:
  related to degree that codes, symbols correspond to conceptual associations people have
  It relates to how meaningful codes and symbols are to people who use them
  e.g.: airplane symbol to denote an airport on a map means much more than a square or circle
  e.g.: creating meaningful abbreviations and names for computer applications

## Slide 17: COMPATIBILITY (Cont.)
2. Movement compatibility:
  relates to the relationship between the movement of the displays and controls and the response of the system being displayed or controlled.
  e.g.: to increase the volume on the radio, we expect to turn the knob clockwise.
  e.g.: upward movement of a pointer is expected to correspond to an increase in a parameter

## Slide 18: COMPATIBILITY (Cont.)
3. Spatial Compatibility
  Refers to the physical arrangement in space of controls and their associated displays
  e.g. how displays are lined-up with respect to corresponding control knobs*
Notes: * Q: what do you think the number in each figure above stands for?

## Slide 19: COMPATIBILITY (Cont.)
4. Modality compatibility:
  refers to the fact that certain stimuli-response modality combinations are more compatible with some tasks than with others
  this is simply related to the how our brains are “wired”
  e.g.: responding to a verbal command that needs verbal action is faster than responding to a written or displayed command requiring the same verbal action* (another e.g. is shown below)
Notes: * This will be revisited when we discuss modality compatibility in detail
Source of figure (study): Stelzel_Schumacher_Schubert_Desposito_2006_Psych_Res

## Slide 20: References
  Human Factors in Engineering and Design. Mark S. Sanders, Ernest J. McCormick. 7th Ed. McGraw: New York, 1993. ISBN: 0-07-112826-3.
  The neural effect of stimulus-response modality compatibility on dual-task performance: an fMRI study. C Stelzel, et al, Psychological Research, 2006.