## Slide 1: King Saud University College of Engineering IE – 341: “Human Factors” Fall – 2016 (1st Sem. 1437-8H)
Chapter 3. Information Input and Processing
Part – 5: Memory – Attention
Prepared by: Ahmed M. El-Sherbeeny, PhD

## Slide 2: Contents
Memory
Attention

## Slide 3
Memory

## Slide 4: Memory
Memory: storage of information
Human Memory Subsystems
  Sensory storage
  Working memory
  Long-term memory
Discuss here
  Each of 3 subsystems (see next slide)
  How information is coded in each
  Practical applications in each subsystem
Notes: Source: Sander and McCormick (Ch. 3), 1993

## Slide 5: Cont. Memory

## Slide 6: Cont. Memory
Sensory Storage
Mechanism
  Part of each sensory channel
  Keeps record of stimulus for short period after stimulus is finished then fades
  Allows further processing of stimulus
  Associated with visual system
    “iconic storage”
    Lasts
  Associated with auditory system
    “echoic storage”
    Last: few seconds
Information Representation:
  Information not coded
  Info. kept in original representation
  Sensory representation cannot be prolonged
  To keep for longer time  transfer to working memory
Notes: Source: Sander and McCormick (Ch. 3), 1993

## Slide 7: Cont. Memory
Working Memory (aka Short-term memory)
Information coded as
  Visual code
  Phonetic code
  Semantic code
  Note, all 3 can exist at same time in WM for particular stimulus
Visual and phonetic codes
  Visual or auditory representations of stimuli
  Generated:
    Internally from long-term memory (without hearing or seeing)
    Using opposite stimulus
      e.g. when seeing word DOG  coded as sound (the word)
      e.g. when hearing the word DOG  visual code/picture of dog
Semantic code
  Abstract representations of meaning of stimulus
  Important in long-term memory
Notes: Source: Sander and McCormick (Ch. 3), 1993

## Slide 8: Cont. Memory
Cont. Working Memory
Capacity of Working Memory
  Information maintained by rehearsal (i.e. paying attention to process)
  Example:
    Think of four letters (e.g. J, T, N, L)
    Count backwards by from
    What happens? You forget letters after , why? No rehearsal*
  When list of items in memory increases
    This “decay” occurs faster
    Due to greater gap  delay in rehearsing each item
  Imp. Q: what is max. # of items that can be held in working memory?
    Miller, 1956: “magical number”: (i.e. ) items/units
    Made of “chunks” of familiar units (e.g. words), i.e. chunks
    This increases capacity of working memory
    Example:
      C.A.T.D.O.G.R.A.T.: string of 9 items
      But CAT.DOG.RAT: 3 chunks (within limit)
Notes: * Try it with Arabic or English letters

## Slide 9
0 5 3 4 2 9 6 7 5 1
055 649 5378
Notes: Exercise: show slide for a few seconds, then ask a few seconds later what were numbers on screen; numbers below are chunked (3) and so easier to rehearse and keep in Working Memory
Note, same can be done with symbols (e.g. on car plates)

## Slide 10: Cont. Memory
Cont. Working Memory
Cont. Capacity of Working Memory
  Summary:
    Don’t present more than chunks of information to remember
    Make chunks meaningful (e.g. )
    Provide training on recalling chunked information
Searching Working Memory
  Time to search for item in WM list (e.g. names) ↑ as list items ↑ linearly
  Time to search for item in WM per item of memory
  All items are searched for equally
Notes: * Try it with Arabic or English letters

## Slide 11: Cont. Memory
Long-term memory
Transferring information from WM to LTM
  Transferred by semantic coding
  i.e. by adding meaning to information + linking to items already in LTM
  e.g.: studying for exams:
    If by repeating material  hard to recall info.
    Effective method: semantically encode info.
Ways to recall information from LTM
  Analyze, compare, relate to past knowledge
  Organizing info. at start  easier to transfer to LTM  more organized info. in LTM  easier to recall/retrieve info. from LTM
  Using “mnemonics” to organize info.:
    i.e. use first letter of item in a list and attach word/image to it
    Makes info. retrieval faster
Notes: Source: Sander and McCormick (Ch. 3), 1993

## Slide 12: Cont. Memory

## Slide 13
Attention

## Slide 14: Attention
Four types of attention tasks / situations
  Selective attention
  Focused attention
  Divided attention
  Sustained attention
Notes: Source: Sander and McCormick (Ch. 3), 1993

## Slide 15: Cont. Attention
Selective attention
  Monitoring several sources of info. (aka channels) to perform a single task
  E.g.: A pilot scanning the instruments
  E.g.: player looking for opening in soccer field
Improving selective attention
  Use as few channels to be scanned for signals as possible
  Tell user which channel is more important  more effective attention
  Reduce level of stress on person  scan more channels
  Show person where signal is more likely to show up
  Train person on how to scan effectively
  Visual channels: keep close together (to scan easier)
  Auditory channels: make sure they don’t mask each other
Notes: Source: Sander and McCormick (Ch. 3), 1993

## Slide 16: Cont. Attention
Focused attention
  Attending one source of information and excluding other sources
  e.g.: trying to read while someone is talking on the phone
  e.g.: listening to a person talk in a crowded, noisy gathering
Improving focused attention
  Make competing channels as distinct as possible from channel of interest
  Separate (in physical space) competing channels from channel of interest
  Reduce number of competing channels
  Make channel of interest (vs. competing channels)
    Larger
    Brighter
    Louder, etc.
Notes: Source: Sander and McCormick (Ch. 3), 1993

## Slide 17: Cont. Attention
Divided attention
  Paying attention to
    Two (or more) sources of information,
    Perform two (or more) tasks simultaneously (aka time-sharing)
  E.g.: driving a car while talking to a passenger
    Driving: visual input and manual response
    Talking: auditory input and vocal responses
  E.g.: eating dinner while watching evening news
  Theories existing to explain performance in divided attention:
    Single-resource theories: 1 source of resources, shared by all mental processes
    Multiple-resource theories: multiple, independent resource pools
Improving divided attention
  Minimize as much as possible sources of information
  Decrease as much as possible difficulty of tasks
  Make tasks as different as possible in terms of input/output modes
  Good way to divide attention: prioritize tasks relatively
Notes: Source: Sander and McCormick (Ch. 3), 1993

## Slide 18: Cont. Attention
Sustained attention (aka monitoring, vigilance)
  Attention over long period of time to detect infrequently occurring signals
  E.g.: security guards viewing TV monitors for the infrequent intruder
  E.g.: air defense radar operator waiting to see missile
  E.g.: inspector on assembly line looking for defect in endless line of products moving by
  Vigilance decrement:
    Decline in speed of signal detection with time for task
    Decline in accuracy of detection with time for task
    Occurs for first of “vigil” (see next slide)
Improving vigilance:
  Scheduled rest breaks, task variation
  Increase conspicuity of signal (e.g. make it larger, brighter, etc.)
  Insert false signals to see how operator will respond
  Motivation (i.e. show importance of task)
  Stimulants (e.g. coffee)
  Keep noise, temp., illumination, other environmental factors: optimum
Notes: Source: Sander and McCormick (Ch. 3), 1993

## Slide 19: Cont. Attention
Notes: Source: Sander and McCormick (Ch. 3), 1993