## Slide 1: Experiment 4 LDH Enzyme Assays
How can you specifically measure the amount of LDH?
LDH converts lactate to pyruvate and NAD to NADH. while using lactate as substrate. You can measure NADH production spectrophotometrically
you can therefore supply NAD and lactate, and measure LDH activity by following NADH production.
Iman Alshehri

## Slide 2
0.1 M of Tris, PH7.4- Dissolve 12.114 g of Tris in 50 ml distilled water, adjust pH with concentrated HCl to pH 7.4, add distilled water to make the total volume 1000 ml.
22.7 mM sodium pyruvate - Dissolve 0.12g of sodium pyruvate in 50 ml distilled water
5 mM NADH (Prepared fresh) - Dissolve 0.16 g of NAD+ in 50 ml distilled water.
22.7 mM Lactate - Dissolve 0.1022 g of sodium lactate in50 ml distilled water.
5 mM NAD+ (Prepared fresh).- Dissolve 0.16 g of NAD+ in 50 ml distilled water.
Cuvettes – Quartz
Reagents
Iman Alshehri

## Slide 3: Procedure
The assay mixture contains 2.7 ml of 0.1 M of Tris, PH7.4, 0.1 ml of 22.7 mM sodium pyruvate and 0.1 ml of 5 mM NADH (Prepared fresh). The reaction initiated by addition of 0.1 ml of enzyme. Blank contains all the components except the NADH. This assay has been used for isoenzymes found in liver and kidney.
The assay mixture contains 2.7 ml of 0.1 M of Tris, PH7.4, 0.1 ml of 22.7 mM Lactate and 0.1 ml of 5 mM NAD+ (Prepared fresh). The reaction initiated by addition of 0.1 ml of enzyme. Blank contains all the components except the NAD+. This assay has been used for isoenzyme that found in Muscle.
Iman Alshehri

## Slide 4: Results
DA/min=((A1-A2)+(A2-A3))/2 | Absorbance 340nm |  | Time
 |  | A1 | 1 min
 |  | A2 | 2 min
 |  | A3 | 3 min
Calculation
LDH Activity ( U/L) = ΔA/min x 0.48
LDH Activity (U/L) =
One unit (U/L) is the amount of enzyme that will reduce one micromole of NAD per minute per liter of sample at specified temperature
Choose the following on the spectrophotometer:
2) Applications  2) Simple Kinetics  wave length (340 nm)  1) Seconds  Duration (180 sec = 3 min)  Intervals (60 sec= 1 min)  Print Data Table (off)  Press start (2 times)

## Slide 5: Calculation
The following equation has been used:
Units = (Δ absorbance/Δ min) ÷ 6220 M-1 cm-1 × 106 μM/M × 0.003 L = μmol/min
Or units = (Δ absorbance/Δ min) × 0.48
6220 : Millimolar extinction coefﬁcient of NADH
Iman Alshehri

## Slide 6: Purification Table
Purification procedure | Volume (ml) | Protein concentration (mg ml-1) | Total protein (mg) | Specific activity (units mg protein-1) | Total activity | Fold purity | % yield
Crude Extract |  |  |  |  |  | 1 | 100
Ammonium sulfate precipitation 40 % (sat) |  |  |  |  |  |  | 
Ammonium sulfate precipitation 60% (sat) |  |  |  |  |  |  | 
DEAE ION exchange |  |  |  |  |  |  | 
Iman Alshehri

## Slide 7: Calculation
Total protein (TP) = protein mg ml-1 X volume (ml)
Specific activity (SA) (units/mg protein) = Total units of protein in a fraction / total protein in a fraction protein (mg)
Total activity (TA) = units* mg–1 protein (SA) × total protein (TP)
Iman Alshehri