## Slide 1
BCH 302 [PRACTICAL]
Proteins II

## Slide 2
Objective:
-Quantitative Proteins Estimation by lowry method.
[determination of unknown protein concentration in a sample using standard curve obtained using lowry method]
-What is a standard curve???

## Slide 3
Quantitative
Qualitative
refers to descriptions or distinctions based on some quality or characteristic rather than on some quantity or measured value. It can be a form of analysis that yields the identity of a compound.
refers to a type of information based in quantities or else quantifiable data

## Slide 4
-Quantitative assays e.g Determine the concentration of a substance.
-Protein assays are one of the most widely used methods in life science research. Estimation of protein concentration is necessary in protein, cell biology, molecular biology and other research applications.
-Is necessary before processing protein samples for isolation, separation and analysis.
Importance of determining concentration of protein

## Slide 5
Specificity and Sensitivity of the method
Specificity of an assay relates to how good the assay is in discriminating between the requested analyte and interfering substances
Sensitivity of an assay is a measure of how little of the analyte the method can detect.

## Slide 6
Most familiar spectrophotometric methods for Determination of proteins concentration:
Lowry method.
Bicinchoninic acid (BCA, Smith) Method.
Bradford Method.
Warburg-Christian Method ( A280/ A260 Method).
Biuret method.
The factors that you should consider in choosing a method:
Sensitivity
The presence of interfering substance
Time available of the assay
Notes: <number>

## Slide 7
Lowery Method
Is based on two chemical reactions:
The first reaction is the reduction of copper ions under alkaline conditions, which forms a complex with peptide bonds .
The second reaction is the reduction of Folin-Ciocalteu reagent by the copper-peptide bond complex, which subsequently causes a color change of the solution into blue with an absorption in the range of 650 to 750 nm detectable with a spectrophotometer.
-The advantages of this assay are its sensitivity, and most importantly, accuracy.
-However, it requires more time than other assays.
Notes: <number>

## Slide 8
Fig: two chemical reactions of lowery method

## Slide 9
How a spectrophotometer works

## Slide 10
A standard curve:
- It is a graph that shows the relationship between different known concentrations of a substance and the absorbance at a specific wave length .
-Standard curve are most commonly used to determine the concentration of a substance, using serial dilution of solutions of known concentrations[standard solution ].
So, what is standard solutions???
standard solution is a solution containing a precisely known concentration of an element or a substance.

## Slide 12
Increased concentration => Increased color intensity => Increased absorbance value