## Slide 1
Dr.Salwa Alsaleh
Salwams@ksu.edu.sa
fac.ksu.edu.sa/salwams
Thermal & Statistical Physics
PHYS 343

## Slide 2: Lecture 13
Air Conditioners
Air Conditioners
Air Conditioners
Air Conditioners

## Slide 3: Question
If you operate a window air conditioner on a table in the middle of a room, the average temperature in the room will
become colder
become hotter
stay the same
342 phys- Dr.S.Al Saleh
<number>

## Slide 4: Observations About Air Conditioners
They cool room air on hot days
They emit hot air from their outside vents
They consume lots of electric power
They are less efficient on hotter days
They can sometimes heat houses, too
342 phys- Dr.S.Al Saleh
<number>

## Slide 5: Heat Machines
Air conditioners
  use work to transfer heat from cold to hot
  are a type of heat pump
Automobiles
  use flow of heat from hot to cold to do work
  are a type of heat engine
342 phys- Dr.S.Al Saleh
<number>

## Slide 6: Thermodynamics
Rules governing thermal energy flow
Relationships between
  thermal energy and mechanical work
  disordered energy and ordered energy
Codified in four laws of thermodynamics
342 phys- Dr.S.Al Saleh
<number>

## Slide 7: 0th Law
Law about Thermal Equilibrium
“If two objects are in thermal equilibrium with a third object, then they are in thermal equilibrium with each other.”
342 phys- Dr.S.Al Saleh
<number>

## Slide 8: 1st Law
Law about Conservation of Energy
“Change in internal energy equals heat in minus work out”
where:
Internal energy: thermal + stored energies
Heat in: heat transferred into object
Work out: external work done by object
342 phys- Dr.S.Al Saleh
<number>

## Slide 9: Order versus Disorder
It is easy to convert ordered energy into thermal (disordered) energy
It is hard to converting thermal energy into ordered energy
Statistically, order to disorder is one-way
342 phys- Dr.S.Al Saleh
<number>

## Slide 10: Entropy
Entropy is measure of object’s disorder
  Includes both thermal and structural disorders
Isolated system’s disorder never decreases
But entropy can move or be transferred
342 phys- Dr.S.Al Saleh
<number>

## Slide 11: 2nd Law
Law about Disorder (Entropy)
“Entropy of a thermally isolated system never decreases”
342 phys- Dr.S.Al Saleh
<number>

## Slide 12: 3rd Law
Law about Entropy and Temperature
“An object’s entropy approaches zero as its temperature approaches absolute zero”
342 phys- Dr.S.Al Saleh
<number>

## Slide 13: More on the 2nd Law
According to the 2nd Law:
  Entropy of a thermally isolated system can’t decrease
  But entropy can be redistributed within the system
  Part of the system can become hotter while another part becomes colder!
342 phys- Dr.S.Al Saleh
<number>

## Slide 14: Natural Heat Flow
Heat naturally flows from hot to cold
  Removing heat from a hot object, entropy
  Adding heat to a cold object,  entropy
Entropy of combined system increases
1 J of thermal energy is more disordering to a cold object than to a hot object
342 phys- Dr.S.Al Saleh
<number>
Notes: <number>
Demonstration: Animation: Hot box, Cold box, Entropy block, and Entropy meter

## Slide 15: Unnatural Heat Flow
Heat can’t naturally flow from cold to hot
  Removing heat from cold object, entropy
  Adding heat to hot object,  entropy
  More entropy removed than added
  Energy is conserved, but  total entropy
To save 2nd law, we need more entropy
Ordered energy must become disordered
342 phys- Dr.S.Al Saleh
<number>
Notes: <number>
Demonstration: Animation: Hot box, Cold box, Entropy block, and Entropy meter
Demonstration: Hand-Generator-Powered Heat Pump

## Slide 16: Air conditioners, Part 1
Moves heat against its natural flow
  Flows from cold room air to hot outside air
  Converts ordered into disordered energy
  Doesn’t decrease the world’s total entropy!
  Uses fluid to transfer heat – working fluid
    Fluid absorbs heat from cool room air
    Fluid releases heat to warm outside air
342 phys- Dr.S.Al Saleh
<number>
Notes: <number>
Demonstration: Animation: Hot box, Cold box, Entropy block, and Entropy meter

## Slide 17: Air conditioners, Part 2
Evaporator – located in room air
  transfers heat from room air to fluid
Condenser – located in outside air
  transfers heat from fluid to outside air
Compressor – located in outside air
  does work on fluid and creates entropy
342 phys- Dr.S.Al Saleh
<number>

## Slide 18: Evaporator, Part 1
Heat exchanger made from long metal pipe
Fluid approaches evaporator
  as a high pressure liquid near room temperature
A constriction reduces the fluid’s pressure
Fluid enters evaporator
  as a low pressure liquid near room temperature
342 phys- Dr.S.Al Saleh
<number>

## Slide 19: Evaporator, Part 2
Working fluid evaporates in the evaporator
  Breaking bonds uses thermal energy
  Fluid becomes colder gas
  Heat flows from room air into fluid
Fluid leaves evaporator
  as a low pressure gas near room temperature
Heat has left the room!
342 phys- Dr.S.Al Saleh
<number>
Notes: <number>
Demonstration: Liquid Nitrogen Evaporating
Demonstration: CO2 Cylinder Making Dry Ice

## Slide 20: Compressor
Working fluid enters compressor
  as a low pressure gas near room temperature
Compressor does work on fluid
  Pushes gas inward as the gas moves inward
  Gas temperature rises (first law)
  Ordered energy becomes disordered energy
Fluid leaves compressor
  as hot, high pressure gas
342 phys- Dr.S.Al Saleh
<number>
Notes: <number>
Demonstration: Pump Air into a Gallon Jug with Thermometer

## Slide 21: Condenser, Part 1
Heat exchanger made from metal pipe
Fluid enters condenser
  as a hot, high pressure gas
  heat flows from fluid to outside air
342 phys- Dr.S.Al Saleh
<number>

## Slide 22: Condenser, Part 2
Working Fluid condenses in condenser
  forming bonds releases thermal energy
  Fluid becomes hotter liquid
  More heat flows from fluid into outside air
Fluid leaves condenser
  as high-pressure room-temperature liquid
Heat has reached the outside air!
342 phys- Dr.S.Al Saleh
<number>
Notes: <number>

## Slide 23: Air conditioner Overview
Evaporator – located in room air
  transfers heat from room air to fluid
Compressor – located in outside air
  does work on fluid, so fluid gets hotter
Condenser – located in outside air
  transfers heat from fluid to outside air,
    including thermal energy extracted from inside air
    and thermal energy added by compressor
342 phys- Dr.S.Al Saleh
<number>
Notes: <number>
Demonstration: Pump Air into a Gallon Jug with Thermometer and Pop the Top
Demonstration: Air Conditioner/Refrigerator/Dehumidifier Opened and Operating

## Slide 24: Question
If you operate a window air conditioner on a table in the middle of a room, the average temperature in the room will
become colder
become hotter
stay the same
342 phys- Dr.S.Al Saleh
<number>

## Slide 25: Summary About Air Conditioners
They pump heat from cold to hot
They don’t violate thermodynamics
They consume ordered energy
They are most efficient for small temperature differences
342 phys- Dr.S.Al Saleh
<number>