## Slide 1
Notes: <number>

## Slide 2: Overview
Part 1 – Gate Circuits and Boolean Equations
  Binary Logic and Gates
  Boolean Algebra
  Standard Forms
Part 2 – Circuit Optimization
  Two-Level Optimization
  Map Manipulation
  Multi-Level Circuit Optimization
Part 3 – Additional Gates and Circuits
  Other Gate Types
  Exclusive-OR Operator and Gates
  High-Impedance Outputs

## Slide 3: Binary Logic and Gates
Binary variables take on one of two values.
Logical operators operate on binary values and binary variables.
Basic logical operators are the logic functions AND, OR and NOT.
Logic gates implement logic functions.
Boolean Algebra: a useful mathematical system for specifying and transforming logic functions.
We study Boolean algebra as foundation for designing and analyzing digital systems!

## Slide 4: Binary Variables
Recall that the two binary values have different names:
  True/False
  On/Off
  Yes/No
  1/0
We use 1 and 0 to denote the two values.
Variable identifier examples:
  A, B, y, z, or X1 for now
  RESET, START_IT, or ADD1 later

## Slide 5: Logical Operations
Chapter 2 - Part 1 <number>
The three basic logical operations are:
  AND
  OR
  NOT
AND is denoted by a dot (·).
OR is denoted by a plus (+).
NOT is denoted by an overbar ( ¯ ), a single quote mark (') after, or (~) before the variable.

## Slide 6: Notation Examples
Chapter 2 - Part 1 <number>
Examples:
  is read “Y is equal to A AND B.”
  is read “z is equal to x OR y.”
  is read “X is equal to NOT A.”
Note: The statement:
  1 + 1 = 2 (read “one plus one equals two”)
is not the same as
  1 + 1 = 1 (read “1 or 1 equals 1”).

B
A
Y

y
x
z


A
X


## Slide 7: Operator Definitions
Chapter 2 - Part 1 <number>
Operations are defined on the values "0" and "1" for each operator:
AND
0 · 0 = 0
0 · 1 = 0
1 · 0 = 0
1 · 1 = 1
OR
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 1
NOT
1
0

0
1


## Slide 8: Truth Tables
Chapter 2 - Part 1 <number>
0
1
1
0
X
NOT
X
Z

Truth table  a tabular listing of the values of a function for all possible combinations of values on its arguments
Example: Truth tables for the basic logic operations:
1
1
1
0
0
1
0
1
0
0
0
0
Z = X·Y
Y
X
AND
OR |  | 
X | Y | Z = X+Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 9: Logic Gate Symbols and Behavior
Chapter 2 - Part 1 <number>
Logic gates have special symbols:
And waveform behavior in time as follows:

## Slide 10: Logic Diagrams and Expressions
Chapter 2 - Part 1 <number>
Boolean equations, truth tables and logic diagrams describe the same function!
Truth tables are unique; expressions and logic diagrams are not. This gives flexibility in implementing functions.
X
Y
F
Z
Logic Diagram
Equation
Z
Y
X
F


Truth Table
1
1 1 1
1
1 1 0
1
1 0 1
1
1 0 0
0
0 1 1
0
0 1 0
1
0 0 1
0
0 0 0
X Y Z
Z
Y
X
F




## Slide 11: Boolean Algebra
Chapter 2 - Part 1 <number>
1.
3.
5.
7.
9.
11.
13.
15.
17.
Commutative
Associative
Distributive
DeMorgan
’
s
2.
4.
6.
8.
X
. 1
X
=
X
. 0
0
=
X . X
X
=
0
=
X . X
An algebraic structure defined on a set of at least two elements, B, together with three binary operators (denoted +, · and ) that satisfies the following basic identities:
10.
12.
14.
16.
X + Y
Y + X
=
(X + Y)
Z
+
X + (Y
Z)
+
=
X(Y +
Z)
XY
XZ
+
=
X + Y
X . Y
=
XY
YX
=
(XY)
Z
X(Y
Z)
=
X
+ YZ
(X + Y)
(X + Z)
=
X . Y
X + Y
=
X
+ 0
X
=
+
X
1
1
=
X + X
X
=
1
=
X + X
X = X

## Slide 12: Boolean Operator Precedence
Chapter 2 - Part 1 <number>
The order of evaluation in a Boolean expression is:
1.
Parentheses
2.
NOT
3.
AND
4.
OR
Consequence: Parentheses appear around OR expressions
Example: F = A(B + C)(C + D)

## Slide 13: Boolean Function Evaluation
Chapter 2 - Part 1 <number>
z
x
y
x
F4
x
z
y
x
z
y
x
F3
x
F2
xy
F1






z
y
z

y

Notes: <number>
F3 is 1 for x’y’z’, x’yz, xy’z’ and xy’z => F3 = 1,0,0,1,1,1,0,0
F4 is 1 for xy’z’, xy’z, x’y’z and x’y z => F4 = 0,1,0,1,1,1,0,0

## Slide 14: Complementing Functions
Chapter 2 - Part 1 <number>
Use DeMorgan's Theorem to complement a function:
  1. Interchange AND and OR operators
  2. Complement each constant value and literal
Example: Complement F =
F = (x + y + z)(x + y + z)
Example: Complement G = (a + bc)d + e
G =
x

z
y
z
y
x
Notes: <number>