## Slide 1: Fundamentals & Ethics of Information Systems IS 201
Chapter 3
Binary Number System and Logic Gates
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 2: Learning Objectives
Know the different types of number systems
Describe positional number notation
Convert base 10 numbers into numbers of other bases and vice versa
Describe the relationship between bases 2, 8, and 16
Identify the basic Boolean logic operations
Identify the basic gates and describe the behavior of each using Boolean expressions and truth tables
Explain how a Boolean expression can be converted into circuits
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 3: Chapter Overview
Why to learn binary system?
Number Systems
Conversions from the Decimal System
Converting binary to octal and hexadecimal
Binary Arithmetic
Boolean Algebra
Logic Gates
Building Computer Circuits
Summary
Chapter3 – Binary System and Logic Gates

## Slide 4: 1. Why Learn the Binary System?
Modern computer systems do not represent numeric values using the decimal system.
Computers use a binary or two's complement numbering system.
To understand how the basic operations of the processor are done.
To be aware of the limitations of computer arithmetic, you must understand how computers represent numbers.
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 5: 2. Number Systems
There are four number bases commonly used in programming. These are:
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 6: Decimal Number System
The Decimal Number System uses base 10. It includes the digits from 0 through 9. The weighted values for each position is as follows:
When you see a number like "123", you don't think about the value 123. Instead, you generate a mental image of how many items this value represents. In reality, the number 123 represents:
104 103 102 101 100 10-1 10-2 10-3
10000 1000 100 10 1 .1 .01 .001
1 * 102 + 2 * 101 + 3 * 100 =
1 * 100 + 2 * 10 + 3 * 1 =
100 + 20 + 3 =
123
Chapter3 – Binary System and Logic Gates

## Slide 7: Decimal Number System (Cont.)
7*102 + 2*101 + 5*100 + 1*10-1 + 9*10-2 + 4*10-3 =
7*100 + 2*10 + 5*1 + 1*0.1 + 9*0.01 + 4*0.001 =
700 + 20 + 5 + 0.1 + 0.09 + .0004 =
725.194
Each digit appearing to the left of the decimal point represents a value between zero and nine times power of ten represented by its position in the number.
Digits appearing to the right of the decimal point represent a value between zero and nine times an increasing negative power of ten.
For example, the value 725.194 is represented as follows:
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 8: Binary Number System
The smallest "unit" of data on a binary computer is a single bit.
Modern computer systems operate using binary logic. The computer represents values using two voltage levels (usually 0V for logic 0 and either +3.3 V or +5V for logic 1).
The binary number system works like the decimal number system except the Binary Number System uses base 2 which includes only the digits 0 and 1.
The weighted values for each position is determined as follows:
27 26 25 24 23 22 21 20 2-1 2-2
128 64 32 16 8 4 2 1 .5 .25
0,1
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 9: Binary to Decimal Conversion
Let’s convert the following two binary numbers to decimal numbers: 10011 and 1101.01
1*24 + 0*23 + 0*22 + 1*21 + 1*20 =
1*16 + 0*8 + 0*4 + 1*2 + 1*1 =
16 + 0 + 0 + 2 + 1 =
19
1*23 + 1*22 + 0*21 + 1*20 + 0*2-1 + 1*2-2 =
1*8 + 1*4 + 0*2 + 1*1 + 0*.5 + 1*.25 =
8 + 4 + 0 + 1 + .25 =
13.25
10011
1101.01
Chapter3 – Binary System and Logic Gates

## Slide 10: Octal Number System
The Octal Number System uses base 8 and includes only the digits 0 through 7:
The weighted values for each position is as follows:
85 84 83 82 81 80
32768 4096 512 64 8 1
0,1,2,3,4,5,6,7
Chapter3 – Binary System and Logic Gates

## Slide 11: Octal to Decimal Conversion
7*82 + 3*81 + 6*80 =
7*64 + 3*8 + 6*1 =
448 + 24 + 6 = 478
6*82 + 7*81 + 0*80 + 3*8-1 + 2*8-2 =
6*64 + 7*8 + 0*1 + 3*.125 + 2*.015625 = 440.6875
Let’s convert the following two octal numbers to decimal numbers: 736 and 670.32
736
670.32
Chapter3 – Binary System and Logic Gates

## Slide 12: Hexadecimal Number System
163 162 161 160
4096 256 16 1
The Hexadecimal Number System uses base 16 and includes the digits 0 through 9 and the letters A, B, C, D, E, and F:
The weighted values for each position is as follows:
0,1,2,3,4,5,6,7,8,9,A,B,C,D,E, and F
Chapter3 – Binary System and Logic Gates

## Slide 13: Hex to Decimal Conversion
To convert from Hex to Decimal, multiply the value in each position by its hex weight and add each value. Using the value from the previous example, 0AFB2, we would expect to obtain the decimal value 44978.
A*163 + F*162 + B*161 + 2*160 =
10*4096 + 15*256 + 11*16 + 2*1 =
40960 + 3840 + 176 + 2 =
44978
0AFB2
Chapter3 – Binary System and Logic Gates

## Slide 14: 3. Conversion of Decimal Numbers
Decimal to Binary Conversion
Decimal to Octal conversion
Decimal to Hexadecimal system
Chapter3 – Binary System and Logic Gates

## Slide 15: Decimal to Binary Conversion
This method consists of two steps:
Step 1
  Dividing the integer part E by 2 until its value is 0 and to keep the remainder R at each division.
Step 2
  Concatenate the remainders starting by the bottom-up
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 16: Decimal to Binary Conversion (Cont.)
Converting the decimal number 18 into the binary system.
Thus the decimal number 18 is translated into the binary number 10010
1810 = 100102
Chapter3 – Binary System and Logic Gates

## Slide 17: Decimal to Binary Conversion (cont.)
Note in the table:
Decimal number 9 is translated into binary number 1001 910 = 10012
Decimal number 4 is translated into binary number 100 410 = 1002
Decimal number 2 is translated into binary number 10 210 = 102
Decimal number 1 is translated into binary number 1 110 = 12
Chapter3 – Binary System and Logic Gates

## Slide 18: Decimal to Octal conversion
The same method is applied in this case except that we will perform successive divisions by 8
Example: Translating the decimal number 18 into the octal system. Base is then 8
Thus the decimal number 18 is translated into the octal number 22 or 1810 = 228
Note in the table:
Decimal number 2 is translated into octal number 2
Chapter3 – Binary System and Logic Gates

## Slide 19: Decimal to Hexadecimal conversion
The same method is applied in this case except that we will perform successive divisions by 16
Example: Translating the decimal number 18 into the hexadecimal system. Base is then 16
Thus the decimal number 18 is translated into the hexadecimal number 12 or 1810 = 1216
Chapter3 – Binary System and Logic Gates

## Slide 20: 4. Conversion of Binary Numbers
A major problem with the binary system is the large number of digits needed to represent even small values. To represent the decimal value 202 requires eight binary digits compared to only three for the decimal system.
When dealing with large numeric values, binary numbers quickly become unmanageable.
The hexadecimal (base 16) numbering system solves these problems. Hexadecimal numbers offer the two features:
  hex numbers are very compact
  it is easy to convert from hex to binary and binary to hex.
Chapter3 – Binary System and Logic Gates

## Slide 21: Converting Binary Numbers
Converting Binary to Octal
Converting Binary to Hexadecimal
Chapter3 – Binary System and Logic Gates

## Slide 22
Chapter3 – Binary System and Logic Gates

## Slide 23: Converting Binary to Octal
Groups of Three (from right)
Convert each group
10101011 10 101 011
2 5 3
10101011 is 253 in base 8
17
Chapter3 – Binary System and Logic Gates

## Slide 24: Converting Binary to Hexadecimal
Groups of Four (from right)
Convert each group
10101011 1010 1011
A B
10101011 is AB in base 16
18
Chapter3 – Binary System and Logic Gates

## Slide 25: 5. Binary Arithmetic
Binary Addition
Binary Substraction
Chapter3 – Binary System and Logic Gates

## Slide 26: Addition
In the binary system, there are four addition cases taking into account the digits 0 and 1 and the possible carry:
Operation result carry
0+0 0 0
0+1 1 0
1+1 0 1
1+1+1 1 1
Chapter3 – Binary System and Logic Gates

## Slide 27: Addition (Cont.)
Perform the addition of the following binary numbers:
110010 and 100111
100111
110010
1011001
+
1
1
Carry values
Chapter3 – Binary System and Logic Gates

## Slide 28: Subtraction
There are four subtraction cases taking into account the digits 0 and 1 and the possible carry:
Operation result carry
0-0 0 0
1-0 1 0
0-1 1 1
1-1 0 0
Chapter3 – Binary System and Logic Gates

## Slide 29: Example
Perform the subtraction of the following binary numbers:
110101 and 100110
100110
110101
001111
-
1
1
Carry values
1
Chapter3 – Binary System and Logic Gates

## Slide 30: Exercises
1 - Convert the following numbers into decimal numbers
  (01)2, (111)2, (10011.11)2, (11010.101)2
  (756)8, (1110.01)8, (6632.45)8,
  (A)16, (1101)16, (FFB23.CD)16
2 - Convert the following decimal numbers into the following bases:
  Binary base 0, 10, 56, 1999
  Octal base 111, 965, 14569
  Hex. Base 01, 111, 56, 965
3 - Perform the following binary operations:
  11 + 11, 1101.1 + 111.1, 11101.1101 + 100011
  11 - 10, 110.1 - 011.01, 11101.1101 - 100011
Chapter3 – Binary System and Logic Gates

## Slide 31: 6. Boolean Algebra
Boolean Algebra describes operations on true/false values
Boolean logic operations on electronic signals can be built out of transistors and other electronic devices
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 32
Chapter3 – Binary System and Logic Gates

## Slide 33: Boolean Algebra Components
Chapter3 – Binary System and Logic Gates

## Slide 34: Boolean Operations
a AND b
  True only when a is true and b is true
a OR b
  True when a is true, b is true, or both are true
NOT a
  True when a is false and vice versa
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 35: Boolean Operations
A | B | A AND B
F | F | F
F | T | F
T | F | F
T | T | T
Chapter3 – Binary System and Logic Gates
A | B | A OR B
F | F | F
F | T | T
T | F | T
T | T | T
A | NOT A
F | T
T | F

## Slide 36: Boolean Expressions
Boolean expressions
  Constructed by combining together Boolean operations and variables
    Example: (a AND b) AND c
Truth tables capture the output/value of a Boolean expression
  A column for each input plus the output
  A row for each combination of input values
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 37: Boolean Expressions
Example:
  (a AND b) AND c
a | b | c | a AND b | ((A AND b) AND c)
F | F | F | F | F
F | F | T | F | F
F | T | F | F | F
F | T | T | F | F
T | F | F | F | F
T | F | T | F | F
T | T | F | T | F
T | T | T | T | T
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 38: Boolean function
    F(a,b,c) = (a AND b) AND c
Chapter3 – Binary System and Logic Gates
a | b | c | F
F | F | F | F
F | F | T | F
F | T | F | F
F | T | T | F
T | F | F | F
T | F | T | F
T | T | F | F
T | T | T | T

## Slide 39: Boolean Algebra and Hardware
Boolean variables ----- signals
Boolean values (F,T) ----- signal value (0,1)
Boolean operations ----- logic gates
Boolean function ------ logic circuit
Chapter3 – Binary System and Logic Gates

## Slide 40: 7. Logic Gates
Gates are hardware devices built from transistors to mimic Boolean Operations
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 41: Logic Gates (cont.)
AND gate
  Two input lines, one output line
  Outputs a 1 when both inputs are 1
OR gate
  Two input lines, one output line
  Outputs a 1 when either input is 1
NOT gate
  One input line, one output line
  Outputs a 1 when input is 0 and vice versa
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 42: Three Basic Gates
The Three Basic Gates, Their Symbols and Truth Tables
Truth Tables
Symbols
Basic Gates
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 43: Hardware Design
Abstraction in hardware design
  Map hardware devices to Boolean logic
  Design more complex devices in terms of logic, not electronics
  Conversion from logic to hardware design (electronics) can be automated
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 44: 8. Building Computer Circuits
A circuit is a collection of logic gates
  Transforms a set of binary inputs into a set of binary outputs
  Values of the outputs depend only on the current values of the inputs
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 45: Building Computer Circuits
Diagram of a Typical Computer Circuit
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 46: Circuit Design
Truth table captures every input/output possible for circuit
Repeat process for each output line
  Build a product term using AND and NOT for each 1 of the output line
  Combine together all product terms with ORs
  Design a circuit from the whole Boolean expression
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 47: Design Example
Circuit Design and Construction
  Compare-for-equality (CE) circuit
Chapter3 – Binary System and Logic Gates
A
B
F
comparator
a0
b0
a3
b3
Notes: <number>

## Slide 48: A Compare-for-Equality Circuit
Compare-for-equality circuit
  CE compares two unsigned binary integers for equality
  Built by combining together 1-bit comparison circuits (1-CE)
  Integers are equal if corresponding bits are equal (AND together circuits for each pair of bits)
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 49: 1-CE truth table
a | b | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 50: 1-CE logic circuit
Chapter3 – Binary System and Logic Gates
Notes: <number>

## Slide 51: CE circuit
Chapter3 – Binary System and Logic Gates
1-CE
1-CE
1-CE
1-CE
AND
gate
F
a0
a1
a2
a3
b0
b1
b2
b2

## Slide 52: More Gates
XOR
NAND
NOR
Gates with more than 2 inputs
Chapter3 – Binary System and Logic Gates

## Slide 53: XOR Gate
4–<number>
Various representations of an XOR gate

## Slide 54: NAND and NOR Gates
The NAND and NOR gates are essentially the opposite of the AND and OR gates, respectively
Various representations of a NAND gate
Various representations of a NOR gate

## Slide 55: Gates with More Inputs
4–<number>
Gates can be designed to accept three or more input values
A three-input AND gate, for example, produces an output of 1 only if all input values are 1
Various representations of a three-input AND gate

## Slide 56: Basic logic gates
NOT
AND
OR
NAND
NOR
XOR

## Slide 57: Properties of Boolean Algebra
4–<number>

## Slide 58: Analysis Example 1
Find the output of the following circuit
Answer: (x+y)y
x+y
y
(x+y)y
__

## Slide 59: Analysis Example 2
Find the output of the following circuit
Answer: xy = x+y
x
y
x
y
x
y
_ _
___

## Slide 60: Design Example 1
Design the circuits for the following Boolean algebraic expressions
x+y
__
x
x+y

## Slide 61: Design Example 2
Design the circuits for the following Boolean algebraic expressions
(x+y)x
_______
x+y
x+y
(x+y)x

## Slide 62: XOR Design
x  y  x.y + x.y
x  y  (x + y) (x + y)
x  y  (x + y)(xy)
x | y | xy
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x+y
xy
xy
(x+y)(xy)
____
___
___
___
___

## Slide 63: The half-adder
Sum = x y
Carry = x .y
x | y | Carry | Sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 64: Circuit equivalence
4–<number>
(AB + AC)

## Slide 65: Circuit equivalence (cont.)
4–<number>
We have therefore just demonstrated circuit equivalence
  That is, both circuits produce the exact same output for each input value combination
Boolean algebra allows us to apply provable mathematical principles to help us find simpler design for the logical circuits.
This is called minimization

## Slide 66: 9. Summary
Number Systems: Decimal, Binary, Octal, Hexadecimal
Convert Decimal to other number systems and vice versa
Binary arithmetic
Boolean logic and basic Boolean operations
Gates and Boolean logic
Circuits are constructed using Boolean expressions as an abstraction
Chapter3 – Binary System and Logic Gates