## Slide 1: King Saud University College of Engineering IE – 341: “Human Factors Engineering” Fall – 2016 (1st Sem. 1437-8H)
Chapter 10. Human Control of Systems (Compatibility) – Part I
Prepared by: Ahmed M. El-Sherbeeny, PhD

## Slide 2: Contents
Introduction
Spatial Compatibility (p1)
  Applications
Movement Compatibility (p2)
  Applications
Modal Compatibility (from ch. 3)
  Application

## Slide 3: Introduction
Human function in system control:
  Receive information
  Select action mode
  Execute action
Human action:
  Becomes control input to the system
  Remember (Ch. 1) output of 1 system  input to another system
  Output of system: usually as feedback regarding effects of action
  Then human function starts again (as listed above, and so forth)
Human functions involved with system control:
  Compatibility (discussed here; most important), also:
  Tracking (discussed later)
  Supervisor control (not discussed here)
Notes: Source: Sander and McCormick (Ch. 10), 1993

## Slide 4: Cont. Introduction
Compatibility:
  Considers relation between controls and displays
  Determines how easy and convenient people choose and perform correct actions given several alternatives
Definition:
  “degree to which relationships are consistent with human expectations”
Types of compatibility
  Conceptual, Spatial, Movement, and Modality (discussed in ch. 3)
  Discuss here: spatial and movement i.t.o. relation between control & display
Effect of compatibility:
  Faster learning
  Faster reaction/response time (RT)
  Less errors
  Higher user satisfaction
Notes: Source: Sander and McCormick (Ch. 10), 1993
i.t.o.: in terms of

## Slide 5: Cont. Introduction
Effect of non-compatibility:
  People can get used to non-compatible (“out of sync”) systems, but:
  There’s higher information processing burden on user (i.e. more thinking)
  Under stress conditions: user may make compatible (i.e. natural response)  which (here) will be incorrect response  error or accident
Special considerations for compatibility relationships
  Some are stronger than others
    E.g. when shared by a larger group of population than others
  Sometimes it is necessary to violate a compatibility relationship to make use of another one
    E.g. study by Bergum (1981) for subject group 93% expected upward movement of pointer  increase 71% (of same group) expected numbers to increase: top to bottom!
Notes: Source: Sander and McCormick (Ch. 10), 1993

## Slide 6
Spatial Compatibility
Notes: Cognitive: المعرفي

## Slide 7: Spatial Compatibility
Types of spatial compatibility
  Physical similarities of displays and controls
  Physical arrangement of displays and controls
Physical similarities of displays and controls
  Involves design of displays/controls in order to have similar:
    Physical features
    Modes of operation
Case 1: study by Fitts and Seeger (1953)
  Three displays / three controls (all combinations used) (see next slide)
  Displays: lights in various arrangements
  With light operation  subject moves stylus along corresponding channel to turn light off
  Each group of subjects attempted each of 9 possible combinations
  Performance measured as: RT, errors, information lost (bits)
  Results:
    Best performance: when stimulus panel resembled response panel
    Best combinations (Sa-Ra, Sb-Rb , Sc-Rc)
Notes: Source: Sander and McCormick (Ch. 10), 1993

## Slide 8: Cont. Spatial Compatibility
Cont. A. Physical similarities of displays and controls
Notes: Source: Sander and McCormick (Ch. 10), 1993

## Slide 9: Cont. Spatial Compatibility
Cont. A. Physical similarities of displays and controls
Case 2: keyboard and screen (Bayerl, et al, 1988)
  Keys on keyboard arranged as:
    Rows on top or
    Columns on one side (see next slide)
  Meaning of keys depends on software (as screen label for each key)
  Authors compared different screen vs. keyboard layouts, i.t.o:
    Mean time to find and press keys (i.e. RT)
  Result:
    RT is smaller (i.e. higher compatibility) when labels (on screen) and keyboard configurations are physically similar
Notes: Source: Sander and McCormick (Ch. 10), 1993

## Slide 10: Cont. Spatial Compatibility
Cont. A. Physical similarities of displays and controls
Notes: Source: Sander and McCormick (Ch. 10), 1993

## Slide 11: Cont. Spatial Compatibility
Physical arrangement of displays and controls
  This involves applications of findings of first two experiments
  Most famous: burner control arrangement on 4-burner stove
Control-Burner arrangement experiments
  Several studies conducted (Chapanis, 1959; Ray, 1979) (see next slide)
  Subjects:
    Presented with various arrangements of controls / burners
    Asked to turn on specific burners
  Number of errors recorded
  Results:
    Two studies similarly ranked various arrangements
    Exercise: rank arrangements on following slide from best to worst
Notes: Source: Sander and McCormick (Ch. 10), 1993
Best arrangement: I (offset burners), then for aligned burners: II

## Slide 12: Cont. Spatial Compatibility
Cont. B. Physical arrangement of displays and controls
Notes: Source: Sander and McCormick (Ch. 10), 1993

## Slide 13: Cont. Spatial Compatibility
Cont. B. Physical arrangement of displays and controls
Cont. Control-Burner arrangement experiments
  Another experiment (Shinar, 1978):
  Subjects asked to indicate burners for unmarked controls 
    31% chose arrangement III
    25% chose arrangement II (yet with less errors than III)
  Conclusions:
    People don’t always choose options resulting in optimum performance
    Better to use performance measures (vs. subjective measures) to decide on best display/control arrangements
Notes: Source: Sander and McCormick (Ch. 10), 1993

## Slide 14: Cont. Spatial Compatibility
Cont. B. Physical arrangement of displays and controls
Cont. Control-Burner arrangement experiments
  Another experiment (Osborne, 1987):
  Added “sensor lines” to stove top (see next slide):
    Lines are drawn from controls to corresponding displays
    Senor lines: either partial or complete set
    They used arrangement II (from first experiments)
  Offset arrangement (from first experiments) also added for comparison
  Which do you think gave: least RT, least errors?
  Results: sensor lines  greatly reduced RT, almost eliminated errors
Errors | Response Time | Arrangement
0 |  | Offset (I)
0 |  | Aligned (II) – complete sensor lines
0 |  | Aligned (II) – partial sensor lines
 | Most time* | Aligned (II) – no sensor lines
Errors | Response Time | Arrangement
0 |  | Offset (I)
0 |  | Aligned (II) – complete sensor lines
0 |  | Aligned (II) – partial sensor lines
 | Most time* | Aligned (II) – no sensor lines
Notes: Source: Sander and McCormick (Ch. 10), 1993
* Text states that adding sensor lines reduced RT by 113 ms, but how much was the original RT?

## Slide 15: Cont. Spatial Compatibility
Cont. B. Physical arrangement of displays and controls
Notes: Source: Sander and McCormick (Ch. 10), 1993

## Slide 16: Cont. Spatial Compatibility
Cont. B. Physical arrangement of displays and controls
Cont. Control-Burner arrangement experiments
  Watch example in YouTube video:
  “Ergonomics and Design” (from start until 4:06)
  https://youtu.be/LAKlmdMHpdE?list=PLV-xlApuz3HbJ66G4pqxzdYO7o_3xZEi1
  Note the Stove example (@3:17)
Notes: Source: Sander and McCormick (Ch. 10), 1993
* Text states that adding sensor lines reduced RT by 113 ms, but how much was the original RT?