## Slide 1: Work Charting Methods
Topics:
Pareto Chart – part 1
Fishbone (Cause-Effect) Diagram – part 1
Operation Process Charts – part 1
Flow Process Charts – part 1
Flow Diagrams – part 2
Worker and Machine Process Charts – part 2
Gang Process Charts – part 2
Two-Handed Process Charts – part 2

## Slide 2: Objectives of Work Charting Methods
Objectively document the work task or process for analysis
Examine some of many available methods (new ones invented regularly)
Break down job into sub-components (tasks)
Describe the tasks in a meaningful way
Notes: What do we mean by objectively? i.e. using values and quantities (not subjectively, e.g. high, low, etc.)

## Slide 3: Work Charting Methods
Pareto Chart

## Slide 4: 1 - Pareto Chart
Items of interest:
  identified
  measured on a common scale
  then ordered in ascending order
  used to create a cumulative distribution
Pareto principle:
  80% of total activity found in first 20% of items
Goal: identify appropriate 20% for analysis
  e.g. 80% of inventory associated 20% of parts
  e.g. 80% of injuries associated 20% of jobs
Notes: * This is a partial repeat from chapter 2: “Introduction to Methods Engineering”

## Slide 5: 1 - Pareto Chart
Notes: Q: can you interpret the above distribution? 20% of the models represent almost 80% (45 + 35) of the relative frequency (e.g. sales)

## Slide 6: Work Charting Methods
Fishbone (Cause-Effect) Diagram

## Slide 7: 2 - Fishbone (Cause-Effect) Diagram
Identifies components that lead to undesirable event in a process
Event / problem / effect: identified at “fish head”
Associated contributing factors:
  grouped into categories (shown in boxes)
  potential root causes identified using tree type structure (using arrows)
Closely related to many different charts used in safety analysis (Fault-Tree method)
Notes: * This is a partial repeat from chapter 2: “Introduction to Methods Engineering”

## Slide 8: 2 - Fishbone (Cause-Effect) Diagram

## Slide 9: 2 - Fishbone (Cause-Effect) Diagram
Notes: Note how the categories for the contributing factors are almost the same in all cases (e.g. process/method, equipment/machine, materials, workers/humans, etc.)

## Slide 10: 2 - Fishbone (Cause-Effect) Diagram
Simple Fault-Tree
Notes: Can you compare between fishbone diagram and fault-tree? (conditions here are compound unlike fishbone diagram)

## Slide 11: Work Charting Methods
Operation Process Charts

## Slide 12: 3 - Operation Process Charts
Represents the chronological sequence of:
  Operations
  Inspections
  Time allowances, and
  Materials used in a process
Spans time from
  arrival of raw material to
  packaging of finished product
Focuses on products and/or facilities
Two symbols used in the chart (see next slide):
  Operations: denoted using a small circle
  Inspections: denoted using a small square

## Slide 13: 3 - Operation Process Charts
Process Flow Diagram Symbols
Notes: Note how “process” and “operation” mean the same thing; same for “check” and “inspection”

## Slide 14: 3 - Operation Process Charts
Vertical lines: indicate general flow of process as work is completed
Horizontal lines feeding into vertical lines: parts or subassemblies (see next slide)
Lines should not cross in the chart.
  Time* values are assigned on the chart to:
  operations and
  inspections
Notes: Note, time values can be omitted from OPC’s (since they are analyzed in another type of chart; which will be mentioned in a future chapter)

## Slide 15: 3 - Operation Process Charts
Notes: Q: what is the difference between horizontal and vertical lines in operations? A: horizontal line: usually means more than operation at the same time; vertical line: denotes the next step (flow)

## Slide 16: 3 - Operation Process Charts
Notes: Note how all operations here involve only inspections and operations; also in this type of OPC time values have been omitted.
Q: where are the junctions in this OPC (operation process chart)? A: between P-A and P-B; between P-A&B and P-C (note there are no reworks or alternative paths here)

## Slide 17: 3 - Operation Process Charts
Notes: Note how all operations here involve only inspections and operations, no matter how detailed or complex the process(es).
Q: how many operations and how many inspection? Can you trace the sequence (flow) of events in the process here? How many junctions?

## Slide 18: Work Charting Methods
Flow Process Charts

## Slide 19: 4 - Flow Process Charts
Identify functions involved in making a part or completing a process:
  Operations
  Inspections
  Materials
  Moves
  Storages and
  Delays
Show all events in the correct sequence
Show the relationship between
  Parts and
  Fabrication complexity

## Slide 20: 4 - Flow Process Charts
Used for
  Workers
  Components, or
  Sub-assemblies
Distinguish between
  Produced and
  Purchased parts.
Provide information on
  Number of employees utilized and
  Time* required to perform each
    Operation and
    Inspection
Notes: * Time here is optional

## Slide 21: 4 - Flow Process Charts
More details than operations process charts
Two types are commonly used:
  Product (or material)
  Operative (or person)
Help identify nonproduction (hidden) costs:
  Distances traveled
  Delays, and
  Temporary storage

## Slide 22: 4 - Flow Process Charts
The ASME standard set of process chart symbols
Notes: Note how mentioning of time here is omitted (since obtained from time study charts – to be discussed in a future chapter)
Fun fact: the five symbols can be easily memorized as: DISTO (like distance)

## Slide 23: 4 - Flow Process Charts
Notes: Fun fact: the five symbols can be easily memorized as: DISTO (like distance)
Q: can you guess what the “handle” symbol consists of?

## Slide 24: 4 - Flow Process Charts
Notes: Note how if nonstandard symbol (above) is used, priority (basis) is given to the one outside; e.g. last one is primarily transportation (with element of operation/production)

## Slide 25: 4 - Flow Process Charts
advertising
Notes: Note how mentioning of time here is omitted (since obtained from time study charts – to be discussed in a future chapter)

## Slide 26: 4 - Flow Process Charts
8
Notes: Although time is mentioned here, the total event time (see top of FPC) is not mentioned, why?

## Slide 27: 4 - Flow Process Charts
8
Notes: Although time is mentioned here, the total event time (see top of FPC) is not mentioned, why?