## Slide 1: Software Quality assurance (SQA) SWE 333
Dr Khalid Alnafjan
kalnafjan@ksu.edu.sa
Software Quality Planning and
control

## Slide 2: Quality Plan
Quality plan Defines the Quality goals and activities performed to ensure the satisfaction of these goals.

## Slide 3
1. List of quality goals
2. Review activities
3. Software tests
4. Configuration management plans: tools, procedures and data for version releases
The elements of software quality
Quality plan

## Slide 4: Elements of quality Plan
Quality goals: Refers to the developed software quality requirements. The quality goals should reflect the major acceptance criteria indicated in the customer’s requirement document (i.e., the RFP document). As such, quality goals serve as measures of the successful achievement of the customer’s quality requirements.

## Slide 5: Quality goal example
See Table 6.1

## Slide 6: Elements of quality Plan
Planned review activities: A list of all SDLC activities and deliverables to be reviewed to ensure that quality meets requirements
    Example: Development plan review, software requirements specification review, preliminary design review, detailed design review, database design review, test plan review, software test procedure review, operator manual review, installation plan review, training objectives review

## Slide 7: Elements of quality Plan
Planned software tests : The quality plan should provide a complete list of planned software tests, with the following designated for each test:
■ The unit, integration or the complete system to be tested
■ The type of testing activities to be carried out.
■ The planned test schedule

## Slide 8: Elements of quality Plan
Configuration management
The quality plan should specify configuration management tools and procedures, including those change-control procedures meant to be applied throughout the project.

## Slide 9: Your Project
As part of your course project you are required to create a software quality plan
Use the previous guidelines in the slides to prepare your software quality plan required in your project
Search the web for “Software quality Plan samples” to obtain several samples

## Slide 10: Quality Control and Quality assurance
Quality control is designed to:
    detect and correct defects,
whereas quality assurance is oriented toward:
    preventing them.
Quality assurance is a managerial function that prevents problems by heading them off, and by advising restraint and redirection.

## Slide 11: Quality Control
Quality control consists of well-defined checks on a product that are specified in the product quality plan.
For software products, quality control typically includes specification reviews, inspections of code and documents, and checks for user deliverables.

## Slide 12: Quality Control
Quality control is defined as the processes and methods used to monitor work and observe whether requirements are met. It focuses on reviews and removal of defects before shipment of products.
This involves checking the software development process to ensure that procedures and standards are being followed.
  Automated software assessment and software measurement.

## Slide 13: Quality Control
Quality control is usually performed using two methods.
Reviews of documents such as requirements documents and design documents.
And testing of code and modules

## Slide 14: Quality Assurance vs. Quality Control
Quality Assurance
An overall
management plan to
guarantee the
integrity of data
(The “system”)
Quality Control
A series of
analytical
measurements used
to assess the
quality of the
analytical data
(The “tools”)

## Slide 15: Quality Assurance vs. Quality Control
Quality assurance prevents mistakes by several means such as training and the use of quality tools (Guidelines, User manuals, Standards, Check lists, Templates)
Quality control tries to detect and correct mistakes using reviews for documentation and testing for coding

## Slide 16: Reviews
This is the principal method of validating the quality of a process or of a product.
A group of people carefully examine part or all of a software system and its associated documentation to find potential problems.
Code, designs, specifications, test plans, standards, etc. can all be reviewed.
Software or documents may be 'signed off' at a review which signifies that progress to the next development stage has been approved by management.

## Slide 17
DPR – Development Plan Review
SRSR – Software Requirement Specification Review
PDR – Preliminary Design Review
DDR – Detailed Design Review
DBDR – Data Base Design Review
TPR – Test Plan Review
STPR – Software Test Procedure Review
VDR – Version Description Review
OMR – Operator Manual Review
SMR – Support Manual Review
TRR – Test Readiness Review
PRR – Product Release Review
IPR – Installation Plan Review
Some common
reviews

## Slide 18: Quality Control Review types
The main technique for achieving quality control is the software checklist, walkthrough and inspection.
These are different types of reviews
Walkthrough is an informal review performed by peers. It need no prior preparation.
Checklists are list of items that should be checked during the review.

## Slide 19: Walkthrough
In Walkthrough a piece of work is given to one or more colleague
They review that work and give their comments in order to enhance the job
Comments are usually in terms of problems detected or suggestions for further improvement
Walkthrough is informal and hence these comments might not be made

## Slide 20: Inspection
Inspection is the most formal review type
In an inspection a piece of document is given to group of inspector in advance with the specific intent of finding errors in it.
The inspection group usually includes:
    Moderator - leads the inspection, schedules meetings, controls the meetings, reports inspection results, and follows up on rework issues. each

## Slide 21: Inspection
    Author - created or maintains the work product being inspected. The author may answer questions asked about the product during the inspection, and he also looks for defects. The author cannot serve as moderator, reader, or recorder.
    Reader - describes the sections of the work product to the team as they proceed through the inspection. The reader may paraphrase what is happening in the product, such as describing what a section of code is supposed to do, but he does not usually read the product verbatim.

## Slide 22: Inspection
    Inspector - attempts to find errors in the product. All participants actually are acting as inspectors, in addition to any other responsibilities.

## Slide 23: Inspection and walkthrough
Inspections and walkthroughs are primarily intended to discover defects in software code or documentation..
Inspections and walkthrough can be held a various points in development process.
Inspections and walkthrough have proven to be very successful tools for improving software quality

## Slide 24: Checklists
Check lists are useful to support reviews, inspections, walkthroughs
Expertise is captured in a list format
  Less experienced people can use
    Straightforward to use (each check should be clear, simple to assess/apply)
  Improve consistency of assessments

## Slide 25: Quality Control walkthrough and Checklist
Inspection is a formal type of review. It requires preparation on the part the review team members before the inspection meeting takes place. A follow- up stage is also a requirement of the inspection. This ensures that any re-working is carried out correctly.

## Slide 26: Quality Control Checklist for reviewing java code
Check list for java code:
are any while or if conditions closed with semicolon “;” ?
are all variables declared ?
does every ‘‘{’’ have a matching ‘‘}’’?
does every equality comparison have a double ‘‘=’’?

## Slide 27: Quality Control Checklist for reviewing software design
Check list for reviewing software design:
Are all significant functions shown in design?
Are all significant attributes specified in design?
Are all names related to purpose and type and are they unambiguous?
Are all relationships between classes specified?
Do all functions have the data necessary for the function to execute?