## Slide 1
Lab # 2
Notes: <number>

## Slide 2: Antimicrobial Therapy
Natural antibiotic agents:
Produced by microorganisms:
  Penicillium notatum – penicillin
Semi-synthetic antibiotic agents:
chemically modified natural agents (large group of modern antibiotics)
synthetic antibiotic agents:
Chemically related to natural antibiotics but completely industrially manufactured
Notes: <number>

## Slide 3: Why do we do sensitivity testing??
To know which drug we use to the patient.
To Know the dose of antibiotic.
It is important to use the lowest effective concentration of the antibiotic to avoid toxicity in patient.

## Slide 4: Organism Used Standard Organism (Quality Control organism)
Staphylococcus aureus ATCC 25923
Pseudomonas aeruginosa ATCC 27853
Escherichia coli ATCC 25922
Enterococcus faecalis ATCC 29212
Klepsiella pneumoniae ATCC 700603
Streptococcus pneumoniae ATCC 49619
Haemophilus influenzae ATCC 49247

## Slide 6: Broth Dilution Method
antibiotic
(dilution series)
+
bacterial suspension
(standard amount)
growth ?
MIC – minimal inhibitory concentration
Notes: <number>

## Slide 7: Definitions:
Minimum Inhibitory Concentration MIC:
  The lowest concentration of antimicrobial required to stop growth of bacteria.
Minimum Bactericidal Concentration MBC:
  The lowest concentration of antimicrobial required to kill bacteria.
Notes: <number>

## Slide 8: Definitions:
Muller Hinton Broth:
  It is a special media used for sensitivity testing, it dose not interfere with test results it has a:
    Standard PH
    Standard electrolytes
Notes: <number>

## Slide 9: Definitions:
Standard inoculum size:
  A standard concentration of bacterial cells to be inoculated.

## Slide 10: Broth Dilution Method
Prepare 2 sets of 9 sterile tubes.
1 ml  broth in each tube.
1 ml  antibiotic of interest in tube #1.
Take 1 ml of tube #1 & add to next tube & so on tell tube #8
Take 1 ml of tube #8 & discard.
Notes: <number>

## Slide 11: Broth Dilution Method
Add 1 drop of test organism in each tube of set 1 using a pastuer pipette.
Add one drop of control organism in each tube of set 2
Incubate 24 hr x 37C
Notes: <number>

## Slide 12: Results:
MIC  last tube showing no growth.
Tube #9 has no antibiotic  has to be turbid.
2
1
4
5
6
7
8
9
3
Control tube
Only organism
0.5 Mg/ml
0.125 Mg/ml
0.0625 Mg/ml
0.0312 Mg/ml
0.0156 Mg/ml
0.25Mg/ml
Notes: <number>

## Slide 13: Trouble shooting
  If all tubes turbid 
    ?started with low antibiotic conc.
    ?resistant organism
    ?antibiotic not working
  If all tubes clear except tube #9 
    ? Started with high antibiotic conc.

## Slide 14: Results
MIC  the last dilution at which no growth is observed.
The more resistant the organism is  the higher the MIC
MBC  the last dilution at which no growth is observed ; And its subculture have no growth on plate.
Notes: <number>

## Slide 15: MIC
Notes: <number>

## Slide 16: MBC

## Slide 17: Etest (strip test)
Notes: <number>

## Slide 18: Microscan
Uses standard size microtiter trays
Detection of growth:
  Photometrically  24 h incubation
  Fluorimetrically  short incubation
Data managed using computer-based algorithms
Notes: <number>

## Slide 19: Phoenix
Broth Microdilution test.
For growth detection it usese:
  Redox indicator.
  Bacterial turbidity testing.
Notes: <number>

## Slide 20: Vitek
Uses thin plastic card, comprising 30 wells  linked by capillaries
Bacterial suspension will rehydrate reagent in wells.
Growth determined turbidometrically every h  for 15 h.
Can test up to 20 antibiotics

## Slide 21
Thank You
Notes: <number>