## Slide 1
NUR 422
<number>
CARDIAC PACING

## Slide 2: Out line
2008/F.ABUDAYAH
<number>
Introduction
Definition of cardiac pacing
Clinical Indication
Pacemaker design
Pacemaker function
Types of pacing
Nursing diagnosis
Nursing intervention
Pt’s education
Notes: <number>

## Slide 3: Normal conductive system of the heart
2008/F.ABUDAYAH
<number>

## Slide 4: Definition of cardiac pacing
2008/F.ABUDAYAH
<number>
It is an electric device that delivers direct electrical stimulation to stimulate the myocardium to depolarize ,initiating a mechanical contraction.

## Slide 5: Dual-chamber (bipolar) pacemaker
2008/F.ABUDAYAH
<number>

## Slide 6: Clinical Indication
2008/F.ABUDAYAH
<number>
Symptomatic bradycardia
Symptomatic heart block
2nd degree heart block
3rd or complete heart block
Bifasicular or transfasicular bundle branch blocks.

## Slide 7: Pacemaker Design
2008/F.ABUDAYAH
<number>
Pulse generator
leads

## Slide 8: Pacemaker Design
2008/F.ABUDAYAH
<number>
Pulse generator
Transcutanus external pacing system house the generator in a piece of equipment similar to portable ECG monitor.

## Slide 9: Pacemaker Design
<number>
Pacemaker lead
Single chamber (unipolar) pacemaker
Lead placed in atrium or ventricle
Dual-chamber (bipolar) pacemaker
One Lead located in the atrium and one in the ventricle

## Slide 10: Single chamber (unipolar
2008/F.ABUDAYAH
<number>

## Slide 11
2008/F.ABUDAYAH
<number>

## Slide 12
2008/F.ABUDAYAH
<number>

## Slide 13: Pacing types
2008/F.ABUDAYAH
<number>
Permanent
Temporary
biventricular

## Slide 14: Types of pacing
Permanent pacemaker
Used to treat chronic heart condition
Surgically placed transvenuosly under local anesthesia
Pulse generator placed in a pocket subcutaneously ,can be adjusted externally

## Slide 15: Permanent pacemaker
2008/F.ABUDAYAH
<number>

## Slide 16: Types of pacing
<number>
Temporary pacemaker
Placed during emergencies
Indicated for pts’ high degree heart block or unstable bradycardia

## Slide 17
<number>
Biventricular pacemaker
Used in sever heart failure
Utilize three leads in right
atrium, right ventricle and
left ventricle to coordinate
ventricular coordination
and improve cardiac
out put
Types of pacing

## Slide 18: INSERTION SITES
<number>
Left Subclavian (most reliable)
Internal jugular (lower incidence of pneumothorax)
Femoral vein
Brachial vein

## Slide 19: Complication
<number>
Movement and dislocation of the lead
Injury
Bleeding and hematoma
Ventricular ectopy or VT from wall stimulation
Infection
Cardiac tamponad
Notes: <number>

## Slide 20: Nursing diagnosis
<number>
Decreased cardiac output related to potential pacemaker mal function
Risk for injury related to peumothorax
Impaired physical mobility related to restriction of movement.
Acute pain related to surgical incision or external pacing stimuli.
Disturbed body image related to pacemaker implementation.

## Slide 21: Nursing intervention
<number>
Maintain adequate cardiac output
Record information after insertion pacemaker model ,mode, program setting,pt’s rhythm
Attach ECG for continues monitoring
Analyze rhythm strips as per protocol
Monitor vital signs
Monitor urine output
Observe for dysrhythmia

## Slide 22: Nursing intervention
<number>
Avoid injury
Obtain chest x-ray to check lead wire position
Monitor for sign and symptom of hemothorax
Monitor for sign and symptom of pneumothorax
Evaluate evidence for bleeding

## Slide 23: Nursing intervention
<number>
Monitor for evidence of lead migration and perforation of heart
Observe for muscle twitching and hiccups
Evaluate chest pain
Auscultate foe friction rub
Observe for signs of cardiac tamponade

## Slide 24: Nursing intervention
<number>
Provide electrically safe environment
Protect exposed parts of electrode leads with rubber
Wear rubber gloves when touching a temporary pacing lead

## Slide 25: Nursing intervention
<number>
Be aware of hazards in the facility that can interfere pacemaker and cause failure
Avoid use of electrical razor
Avoid direct placement of defibrillator paddles over the generator, should be placed 4-5 inches away.
Pt’s with permanent pacemaker should never exposed to MRI because it may alter and erase the program memory.
Caution must be used if pt will receive radiation therapy.

## Slide 26: Nursing intervention
<number>
Prevent accidental pacemaker malfunctions
Use external plastic covering over external generator all times
Secure temporary pace maker over pt’s chest or wrist never hang it over iv pole

## Slide 27: Nursing intervention
<number>
Relieving anxiety
Reliving pain.
Maintaining a positive body image
Minimizing the effect of immobility
Rest for 24-48 hrs post pacing insertion
Deep breathing exercise
Restrict movement of affected extremity

## Slide 28: Patient education
<number>
Anatomy and physiology of the heart
Pacemaker function
Activity
Specific instruction include
Not to lift items over 1.4kg or perform difficult arm maneuver.
Avoid excessive stretching or bending excessive.
Avoid contact sport,tennis,gulfing until advised by doctor.
Sexual activity can be resumed when desired

## Slide 29: Patient education
<number>
Pacemaker failure
Teach pt to check own pulse
at least weekly for 1 min
Report slowing on the pulse
less or greater than the setting rate
Report sign and symptom as palpitation ,fatigue ,dizziness ,prolonged hiccups
Wear identification bracelet and carry a pacemaker identification cared.

## Slide 30: Patient education
<number>
Electromagnetic interference
Caution pt that EMI could interfere with pacemaker function.
Explain that high energy radar, TV and radio transmetters,MRI,large motors antitheft devices and airport security alarmsmay affect the pacemaker function.
Teach pt to move 4-6 m away from source and check pulse. it should return to normal.
Household and kitchen appliance will not affect pacemaker

## Slide 31: Patient education
<number>
Care of pacemaker site.
Wear loose-fitting
clothes around pacemaker
Watch sign and symptom
of infection
Keep incision site clean
and dry. not to scrub site
Advise well balanced diet.