## Slide 1: King Saud University College of Engineering IE – 341: “Human Factors” Fall – 2014 (1st Sem. 1435-6H)
Human Capabilities
Part - B. Speech Communications
(Chapter 7)
Prepared by: Ahmed M. El-Sherbeeny, PhD

## Slide 2: Lesson Overview
Introduction
The Nature of Speech
Criteria for Evaluating Speech
Components of Speech Communication Systems

## Slide 3: Introduction
Speech is form of “display”
  i.e. form of auditory information
Source of speech
  Mostly human (focus of this lesson)
  Could also be synthesized
    i.e. machine; e.g. voice mail, access confirmation)
Receiver of speech
  Mostly human
  Could also be machine: “voice recognition”
    not advanced as synthesized sound

## Slide 4: The Nature of Speech
Speech: closely associated with breathing
Organs associated with speech:
  Lungs
  Larynx
    contains vocal cords
  Pharynx
    channel bet. larynx & mouth
  Mouth (AKA: oral cavity):
    tongue, lips, teeth, velum
  Nasal cavity
Velum

## Slide 5: Cont. The Nature of Speech
Vocal cords
  Contains vibrating folds
  Opening between folds: glottis / epiglottis
  Vibrates 80-400 times/sec.
  Rate of vibration of vocal cords: controls freq. of resulting speech sounds
  Watch “Vocal Cords in Action”: www.youtube.com/watch?v=iYpDwhpILkQ
  Speech/sound waves:
    Produced by: vocal cords
    Further modified by “resonators”:
      pharynx, oral cavity, nasal cavity
    Further articulated by “manipulators”:
      Mouth: tongue, lips, velum
      Nasal cavity: velum, pharynx muscles

## Slide 6: Cont. The Nature of Speech
Types of Speech sounds
  Phonemes
    Basic unit of speech
    Defn: “shortest segment of speech which, if changed, would change the meaning of a word”
    Phonemes in English language:
      Vowel sounds: 13 (e.g. u sound in put, u sound in but)
      Consonant sounds: 25 (e.g. g sound in gyp, g in gale)
      Diphthongs (i.e. sound combinations): e.g. oy sound in boy; ou sound in about
      Can you compare these to Arabic phonemes?
    Combining phonemes:
      Phonemes form syllables ⇒ syllables form words (e.g. ac·a·dem·ic) ⇒ words form sentences
      Note Phonemes > letters (why?): since phonemes change when combined together (e.g. d in di different than du)

## Slide 7: Cont. The Nature of Speech
Depicting Speech
  Sound is generated by variations in air pressure
  This is represented in several graphical ways
  Method 1: waveform
    Shows intensity variation over time (relative scale)
    Listen to file below for verse “بسم الله الرحمن الرحيم”*
Notes: *The clip shown was created using program “Wavepad Sound Editor”; clip is by Sh. Abdul-Bassitt Abdul-Samad

## Slide 8: Cont. The Nature of Speech
Cont. Depicting Speech
  Method 2: spectrum
    Shows for given phoneme / word: intensity of various frequencies in that sound sample (see right)
    Which freq. has highest intensity in shown figure?
  Method 3: sound spectrogram
    Frequency: vertical scale
    Time: horizontal scale
    Intensity: degree of darkness on plot (see right)

## Slide 9: Cont. The Nature of Speech
Intensity of Speech (AKA “Speech Power”)
  Variation among phonemes
    Vowels speech power » consonants
    e.g. a in “talk” has speech power: 680 times > th in then (i.e 28 dB difference)
  Variation among speech types
    conversational speech: 45-55 dBA*
    Telephone/lecture speech: 65 dBA
    Loud speech: 75 dBA
    Shouting: 85 dBA
  Variation: Male & Female
    Male > female by 3-5 dB (in general)
    Men in lower freq. has higher intensity than women (see right)
Notes: *note: A in dBA: most widely used sound filter (i.e. used to control noise in sound); sound level meter is thus less sensitive to very high and very low frequencies; C filter is used for v. high sounds (dBC)

## Slide 10: Criteria for Evaluating Speech
Speech Intelligibility
  Defn: “degree/percentage to which a speech message (e.g. group of words) is correctly recognized”
  This’s major criterion for evaluating speech
  Assessment of speech intelligibility:
    Either repeating back read material
    Or answering questions regarding material
  Speech Intelligibility tests:
    Nonsense syllables (e.g. un, us, mus, sub, sud, …)
      these have least intelligibility
    Phonetically balanced (PB) word lists
      Nonsense syllables < words Intelligibility < sentences
    Complete sentences
      These have highest intelligibility, even when some words are not recognized (i.e. depends on context)
      e.g. “Did you go to the store” may sound as “Dijoo …”

## Slide 11: Cont. Criteria for Evaluating Speech
Speech Quality
  Another criterion for evaluating speech
  May be important in identifying a specific speaker e.g. on phone (i.e. absolute identification)
  Also important to choose bet. different products e.g. speaker phone on home phones, mobile phones
  Assessment of speech quality
    Usually done using rating system
    e.g. people listen to speech and asked to rate quality: excellent, fair, poor, unacceptable, etc.
    May also be done by comparing to some standard speech quality

## Slide 12: Components of Speech Communication Systems
Components
  Speaker
  Message
  Transmission System
  Noise Environment
  Hearer
Discussed here in terms of
  Effects on intelligibility of speech communications
  Methods to improve intelligibility of system

## Slide 13: Cont. Speech Communication Systems
Speaker
  Intelligibility of speaker usu. called “enunciation”
  Research found higher intelligibility is caused by:
    Longer syllable duration
    Speaking with high intensity
    Making use of speech time with spoken words and little pauses
    Variation of speech frequencies
  Differences bet. Intelligibilities generate from:
    Structure of articulators (sound-producing organs)
    Speech habits that people acquire
    Speech training may improve speech intelligibility (but not very much)

## Slide 14: Cont. Speech Communication Systems
Message
Affected by: phonemes used, words, context
  Phoneme Confusions
    Some speech sounds more easily confused than others
    e.g. letters in each group (consonants) can be confused with each other: DVPBGCET, FXSH, KJA, MN
    Avoid using single letters in presence of noise
  Word Characteristics: for higher intelligibility use:
    More familiar words
    Longer words: for longer words even if part of word is dropped, rest can still be figured out
    e.g. “word-spelling” alphabet: alpha, bravo, charlie, delta, … instead of A, B, C, D

## Slide 15: Cont. Speech Communication Systems
Cont. Message
  Context features: for higher intelligibility use:
    Sentences (rather than words)
    Meaningful sentences (rather than non-sense phrases)
      e.g. “This book is great” rather than “is great book this”
    Less vocabulary (words) in the presence of noise
      More words with noise ⇒ less intelligibility (see below)
      Note, -ve SNR means noise is more intense than signal
      Also note, monosyllable: words with only one syllable (e.g. hit, ant, cube, fish)

## Slide 16: Cont. Speech Communication Systems
Transmission System
Transmission Systems
  Natural: air
  Artificial: telephone, radio, etc.
Artificial systems cause distortions, e.g.
  Frequency distortion
  Amplitude distortion
  Filtering
    Low-pass filter: eliminates freq. above some level
    High-pass filter: eliminates freq. Below level
    Filtering: freq. > 4000 Hz, < 600 Hz: little effect on intelligibility; but how about > 1000 Hz, < 3000 Hz?

## Slide 17: Cont. Speech Communication Systems
Noise Environment
  causes biggest harm to speech intelligibility
  SNR (signal to noise ratio):
    Simplest way to evaluate impact of noise on intelligibility
    Study: for noise level of 35-100 dB ⇒ SNR = 12 dB for threshold of intelligibility (what to do for loud noise?)
    However, SNR does not take frequency into consideration (only intensity)
  Other measures (taking freq. into consideration):
    Articulation index (AI): a measure (0-1) of speech intelligibility while knowing the noise environment
    Preferred-octave speech interference level (PSIL): rough measure of effect of noise on speech reception
    Preferred noise criteria (PNC) curves: suggest acceptable noise level for different work environments (e.g. offices)
Notes: Shouting is required for loud noise since SNR = 12 dB @ noise = 100 dB ⇒ signal = 112 dB

## Slide 18: Cont. Speech Communication Systems
Cont. Noise Environment
  Reverberation:
    Bouncing effect of noise from walls, floor, ceiling in a closed room
    Greatly decreases speech intelligibility (e.g. classrooms)
    In general, the longer the reverberation time, the more the speech intelligibility decreases
    Examine the linear relation (right) for decaying a 60 dB noise

## Slide 19: Cont. Speech Communication Systems
Hearer
To receive speech under noise: hearer should
  Have normal hearing
  Be trained to receive messages
  Be able to withstand stress of situation
Age
  Also affects speech reception (i.e. intelligibility); see right
  20-29 age group: base level
  Note, unaltered speech: 120 wpm vs. speeded speech: 300 wpm
Hearing protection
  Prevents hearing loss
  May improve SI for noise >80 dBA
  Decreases SI for noise <80 dBA
Notes: Note the large SI drop at the 60 year mark

## Slide 20: References
  Human Factors in Engineering and Design. Mark S. Sanders, Ernest J. McCormick. 7th Ed. McGraw: New York, 1993. ISBN: 0-07-112826-3.