## Slide 1: King Saud University College of Engineering IE – 341: “Human Factors Engineering” Fall – 2017 (1st Sem. 1438-9H)
Human Capabilities
Part – A. Vision (Chapter 4)
Part 1: Visual Capabilities - Discrimination
Prepared by: Ahmed M. El-Sherbeeny, PhD

## Slide 2: Lesson Overview: Vision
Part 1 (this part):
Process of Seeing (Vision)
Visual Capabilities
  Accommodation
  Visual Acuity
  Convergence
  Color Discrimination
  Dark Adaptation
  Perception
Factors Affecting Visual Discrimination
  Luminance Level
  Contrast
  Exposure Time
  Target Motion
  Age
  Training

## Slide 3: Cont. Lesson Overview: Vision
Part 2:
Alphanumeric Displays
  Characteristics
  Typography
  Typography Features
    Hardcopy
    Visual Display Terminals (VDT)
Graphic Representations
Symbols
Codes

## Slide 4
Vision and Visual Capabilities

## Slide 5: Process of Seeing (Vision)

## Slide 7: Process of Seeing (Vision)
The human eye works like a camera.
Light rays reflected from object
  enter the transparent cornea
  pass through
    clear fluid (aqueous humor) that fills the space between the cornea
    and the pupil (a circular variable aperture)
    and adjustable lens behind the cornea (light rays are transmitted and focused)
      Close objects: lens bulges
      Distant objects: lens relaxes (flattens)
Muscles of the iris change size of pupil:
  larger in the dark (about 8 mm diameter; dilation),
  smaller in bright conditions (2 mm; constriction)

## Slide 8: Cont. Process of Seeing (Vision)
Light rays transmitted through pupil to lens
  refracted by adjustable lens
  then transverse the vitreous humor (a clear jellylike fluid filling the eyeball, behind the lens).
In normal or corrected vision persons
  light rays are focused exactly on the sensitive retina
The retina consists of
  about 6 to 7 million cones
    receive daytime, color vision
    concentrated near center of retina (fovea)
  and about 130 million rods
    rods important in dim light, night.
    distributed in the outer retina, around the sides of the eyeball.

## Slide 9: Cont. Process of Seeing (Vision)
Greatest sensitivity is in the fovea
  The “dead center” of the retina
  For clear vision, the eye must be directed so that the image of the object is focused on the fovea.
The image on the retina is inverted.
Cones and rods connected to optic nerve
  Transmits neural impulses to the brain which integrates impulses, giving visual impression of object
  process also corrects inverted image on the retina.
  More information about vision and human eye:
  https://youtu.be/nbwPPcwknPU

## Slide 10: Visual Capabilities: 1. Accommodation
Accommodation: ability of the lens to focus light rays on the retina
Near point: closest distance possible for focus (i.e. any closer will be blurry)
Far point: farthest dist. for focus (usu. = ∞)
Diopter: measure of focus (for eye, camera)
  Diopter [D] = 1 / target distance
  e.g. 1 D = 1 m; 2 D = 0.5 m; 3 D = 0.33 m; 0 D =∞
  More powerful lens ⇒ higher diopters
Dark focus: eye accommodation in dark (=1D)
Nearsightedness (myopia): far point: too close; i.e. lens remains bulged with far objects
Farsightedness (hyperopia): near point: too far (i.e. can’t see close objects); lens: flat for close objects

## Slide 11: Visual Capabilities: 2. Visual Acuity
Visual Acuity:
  ability of eye to discriminate fine details
  depends largely on accommodation
Minimum separable acuity:
  most common measure of VA (see figure 4-2)
  Defn: smallest feature or space between the parts of a target (e.g. letter ‘E’ below) that eye can detect
Visual angle: (<10º):
  H = stimulus height
  D = dist. from eye
  H,D: same units
  Normal VA = 1 min.
  Note, 1º = 60 min.

## Slide 12: Visual Capabilities: 2. Visual Acuity
Notes: Which of these have you seen the most in vision tests? (optometrist tests)

## Slide 13: Visual Capabilities: 2. Visual Acuity
Cont. Visual angle (VA):
  reciprocal of VA (for smallest detail that eye can see) is used as measure for visual acuity
  i.e. Visual Acuity = [1 / VA]
    e.g. VA = 1.5 min. ⇒ Acuity = 0.67
    e.g. VA = 0.8 min. ⇒ Acuity = 1.25
    Note, as acuity ↑ ⇒ detail that can be resolved is ↓
  Clinical testing: D = 20 ft (i.e. 6 m) from chart
    e.g. Snellen acuity: 20/30 (6/9) ⇒ person barely reads @ 20 ft what normal (20/20, 6/6) person reads @ 30 ft
    e.g. 20/10 ⇒ person reads @ 20 ft what normal person must bring to 10 ft to read (far- or near-sightedness?*)
    e.g. 20/20 ⇒ resolving 1 min. arc of detail @ 20 ft (normal vision)
    e.g. Given VA = 1.75 min. ⇒ Snellen Acuity = 20 / x i.e. x = (20) (1.75) = 35 ⇒ Snellen Acuity = 20 / 35
  Watch nice, short video about acuity: https://youtu.be/ovuyPrffiqg
Notes: * It is neither; this is called “super” vision (only few people have this, and usually is necessary for jobs where such vision is necessary, e.g. pilots)

## Slide 14: Visual Capabilities: 2. Visual Acuity
Other types of visual acuity measures:
  Vernier acuity: ability to differentiate the lateral displacement of one line from another
  Minimum perceptible acuity: ability to detect a spot from its background
  Stereoscopic acuity: ability to differentiate different images received by the retinas of the two eyes of a single object with depth (i.e. converting 2D → 3D).
    Most difference is when the object is near the eyes.
    Try the following game to see if you have Stereo vision
      Center your nose over the brown eye and focus on the eye
      Put a free thumb in front of your nose
      Continue to focus on the eye
      If both eyes are on, you see two thumbs framing one eye.
      Now, switch your focus to your thumb
      You should see two eyes framing one thumb
      Source: http://www.vision3d.com/frame.html

## Slide 15: Visual Capabilities: 3. Convergence
Two eyes must converge on an object ⇒
  images of the object on the two retinas are in corresponding positions to get the impression of a single object (the images are fused).
Convergence is controlled by muscles surrounding the eyeball.
  Some individuals converge too much
  others tend not to converge enough
  These two conditions are called phorias
  This cause double images which are visually uncomfortable and may cause muscular stresses and strains
Orthoptics:
  aims to strengthen eye muscles to correct common eye problems (e.g. convergence insufficiency)

## Slide 16: Visual Capabilities: 4. Color Discrimination
Cones
  Located in fovea (center of retina)
  basis for color discrimination
  3 types of cones, each sensitive to light wavelengths corresponding to primary colors: Red, Green, Blue
  In dark: cones not activated ⇒ no color is visible
Color vision:
  Trichromats: people distinguishing different colors
  Color deficiency (color blind):
    Monochromats (v. v. rare): non-color vision
    Dichromats: deficiency in red or green cones
      Inherted or acquired (e.g. accident or disease)
      Existent in ~ 8% males and 0.5% females
      Poorer performance in practical tasks vs. trichromats (e.g. traffic signals)
  See more about color vision deficiency: https://youtu.be/tU1krrUM26Q*
Notes: *Test your color vision strength here: https://youtu.be/xHIykZgE7HY

## Slide 17: Visual Capabilities: 4. Color Discrimination
Color Images:
  This slide: trichromat vs. dichromat
  Optical Illusions
    Next slide: “rotating turtles”
    Slide 17: “doughnut of rotating snakes”
    Note slides 16, 17: static -not dynamic- images! (how?????)
    Source (much more fun): www.diycalculator.com/ sp-cvision.shtml

## Slide 18: Visual Capabilities: 4. Color Discrimination
Notes: rotating turtles

## Slide 19
Notes: doughnut of rotating snakes
Watch the following video on optical illusions: https://youtu.be/VYIr40D7wNw

## Slide 20: Visual Capabilities: 5. Adaptation
Adaptation: changes in sensitivity to light
Entering dark room:
  This is dark adaptation
  Pupil increases in size (aka dilation) ⇒ more light enter eyes
  Sensitivity of eye ↑ gradually (up to 30-35 mins.)
  Cones lose most sensitivity in dark (mostly rods)
Exiting dark room to light
  This is light adaptation
  Pupil contracts (aka constriction) to limit light entering eyes
  Adaptation requires about 1 min. (why faster?)
  More light ⇒ cones are activated

## Slide 21: Visual Capabilities: 6. Perception
When viewing visual displays
  Displayed features and information may not be enough to make appropriate decisions
  Meaning of displayed information must also be understood
Perception*: interpreting sensed information
The interpretation process
  sometimes straightforward
  most displays: depends on previous learning (experience or training)
Visual displays design must meet 2 objectives
  display must be seen clearly
  design must help viewer to correctly perceive/understand meaning of display
Notes: * Remember the human information processing model (chapter 3)?

## Slide 22
Factors Affecting Visual Discrimination

## Slide 23: Factors Affecting Visual Discrimination
Visual discrimination depends mostly on visual acuity.
Some factors external to the individual affect visual discrimination:
Luminance Level:
  As light or background light levels ↑
  ⇒ cones are activated ⇒ visual acuity ↑
  This is required for complex, intricate tasks
Contrast (AKA brightness contrast):
  Refers to difference in luminance of viewed objects
  Most important consideration: difference in luminance between: object (target) and background
  When contrast is low, target must be larger to be equally discriminable to target with greater contrast

## Slide 24: Cont. Factors Affecting Vis. Discrimin.
Cont. Contrast:
  Measure # 1: Michelson Contrast: measures deviation above and below a mean luminance
    LMAX: max. luminance in pattern
    Lmin: min. luminance in pattern
    Note, MC varies bet. 0 and 1
  Measure # 2: Luminous Contrast :
  Measure # 3: Contrast Ratio:
    it’s recommended to have CR:
    3:1 for target: adjacent surrounding
    10:1 for target: remote darker area
    1:10 for target: remote lighter area
  Note, Can you show the mathematical relation between each of these 3 formulae?

## Slide 25: Cont. Factors Affecting Vis. Discrimin.
Exposure Time:
  Under high illumination
    As exposure time ↑ ⇒ Acuity ↑ for first 100-200 ms.
    After that acuity levels off
Target Motion:
  Acuity ↓ with motion of:
    Target
    Observer
    or Both
  Dynamic visual acuity:
    Ability to make visual discriminations under such conditions (e.g. driver looking at objects on sidewalk)
    This acuity rapidly ↓ as rate of motion ↑

## Slide 26: Cont. Factors Affecting Vis. Discrimin.
Age:
  Visual acuity, contrast sensitivity (ability to see details at low contrast levels) ↓ with age
  Decline starts at age 40
  At age 75: acuity = 20/30
  ⇒ visual displays for old people must provide:
    Large targets
    Adequate illumination
Training:
  Besides contacts, glasses, eye surgery, vision can be improved by:
  Training to improve focus
    Improves Snellen acuity by 14%
    Improves contrast sensitivity by 32%
  Dynamic visual acuity can be improved with practice

## Slide 27: References
Human Capabilities - Vision
  Human Factors in Engineering and Design. Mark S. Sanders, Ernest J. McCormick. 7th Ed. McGraw: New York, 1993. ISBN: 0-07-112826-3.
More Optical Illusions Sites
  http://upload.wikimedia.org/wikipedia/commons/6/60/Grey_square_optical_illusion.PNG
  http://www.illusion-optical.com/Optical-Illusions/Circles.php