## Slide 1: King Saud University College of Engineering IE – 341: “Human Factors Engineering” Fall – 2017 (1st Sem. 1438-9H)
Human Capabilities
Part – A. Vision (Chapter 4)
Part 2: Displays – Symbols – Codes
Prepared by: Ahmed M. El-Sherbeeny, PhD

## Slide 2: Lesson Overview: Vision
Part 1:
Process of Seeing (Vision)
Visual Capabilities
  Accommodation
  Visual Acuity
  Convergence
  Color Discrimination
  Dark Adaptation
  Perception
Factors Affecting Visual Discrimination
  Luminance Level
  Contrast
  Exposure Time
  Target Motion
  Age
  Training

## Slide 3: Cont. Lesson Overview: Vision
Part 2 (this part):
Alphanumeric Displays
  Characteristics
  Typography
  Typography Features
    Hardcopy
    Visual Display Terminals (VDT)
Graphic Representations
Symbols
Codes

## Slide 4
Alphanumeric Displays

## Slide 5: Alphanumeric Displays
Most important characteristics:
Visibility:
  quality of the character that makes it separately visible from its surroundings (i.e. detectability)
Legibility:
  attribute that makes a character identifiable from others (i.e. discriminability)
  depends on stroke width, form of characters, contrast, and illumination
Readability:
  ability to recognize information content of material when represented by alphanumeric characters, words, sentences (i.e. meaningfulness)
  depends more on spacing between lines and letters, etc. than on specific features of characters
  Watch this video about legibility and readability: https://youtu.be/74sZJ4b0_Lc

## Slide 6: Alphanumeric Displays: Typography
Typography:
  various features of alphanumeric displays
Circumstances when it is important to use preferred forms of typography:
  Viewing conditions are unfavorable (e.g. low illumination, limited viewing time)
  Information is important/critical (e.g. emergency labels, important instructions)
  Viewing occurs at a distance
  Displays for low vision people
Note, above forms must still satisfy all conditions mentioned in last slide
When faced with ≥ 1 of these conditions, typography features must be considered:

## Slide 7: A-N Displays: Typography Features
Hardcopy
  Stroke Width
  Width-height Ratio
  Styles of Type
  Size of Characters
    at Reading Distance
    at a Distance
  Layout of Characters
  VDT Screens
  Illuminated Alphanumeric Characters
  Character Distance and Size

## Slide 8: A-N Displays: 1. Stroke Width
Stroke-Width-to-height-ratio ≡ ratio of the thickness of the stroke (s) to the height (h) of the letter/number (stroke ratio for short)
Example (right):
  Stroke width-to-height:1:5 = 0.2
  Note, width-to-height: 3:5 = 0.6
Stroke Width is affected by:
  Background
    black on white or
    white on black
  Illumination

## Slide 9: A-N Displays: 1. Stroke Width (Cont.)
Irradiation:
  causes white features on a black background to appear to ‘spread’ into adjacent dark areas
  But reverse (black on white) isn’t true (no spread)
  Thus, black-on-white letters should be thicker i.e. lower ratios than white-on-black letters
  With good illumination, stroke width ratios:
    Black on white: 1:6 to 1:8
    White on black: 1:8 to 1:10
  With reduced illumination:
    Thick letters become more readable (both types above)
    Letters should be: boldface with low stroke ratios (e.g. 1:5)
  For highly luminous letters, ratios: 1:12 to 1:20.
  For black letters on a very highly luminous background, very thick strokes are needed

## Slide 10: A-N Displays: 1. Stroke Width (Cont.)

## Slide 11: A-N Displays: 2. Width-height ratio
Width-to-height (AKA width-height ratio):
  Relationship between width and height of alphanumeric character
  Expressed as ratio (e.g. 3:5 = 0.6; back 3 slides)
  e.g. B: width-height ratio = 3:5
    3 vertical strokes (or layers)
    5 horizontal strokes
  Most letters can be expressed with ratio 3:5
  Heglin:
    Disagrees with fixed ratios for letters:
    For O: perfect circle
    For A and V: equilateral triangles

## Slide 12: A-N Displays: 2. Width-height Cont.
Cont. width-height ratio
  3:5 satisfactory for most purposes
  wider letters: appropriate certain circumstances:
    e.g. engraved legends
    such cases 1:1 ratios are more appropriate
    Below: letters: 1:1 (except?); numbers: 3:5 (except?)

## Slide 13: A-N Displays: 3. Styles of Type
Styles of type (AKA typefaces, fonts)
  > 30,000 exist!
  4 major classes (each including many types)
  Roman: most common class; letters have serifs (little flourishes, embellishments)
  Sans serif (AKA Gothic): uniform stroke width;
  Script: simulate modern handwriting. (eg wedding cards)
  Block Letter: resembles German manuscript handwriting used in the fifteenth century (above)
Roman: most used styles for conventional text
Italics: emphasis, titles, names, special words, etc
Boldface: headings, labels, special emphasis, legibility in poor reading conditions
Last slide: style used for military (non-standard)
Notes: Watch this great video on the font, “comic sans”: http://youtu.be/GUCcObwIsOs

## Slide 14: A-N Displays: 4. Character Size
Size
  used to measure size of type in printing business
  1 point (pt) = 1/72 in. (0.35 mm)
  this is the height of the slug on which the type is set, e.g.
    tail of the letter “q” (called descender)
    top of letter “h” (called ascender)
    space between lines of text
    Capital letters
  Better approximation to letter size:
    1 pt = 1/100 in. (0.25 mm)
  e.g. letter size, with slug size, heights of cap. letters (in.):
    This line is set in 4-pt type (slug = 0.055; letters = 0.04).
    This line is set in 6-pt type (slug = 0.084; letters = 0.06).
    This line is set in 8-pt type (slug = 0.111; letters = 0.08).
    This line is set in 9-pt type (slug = 0.125; letters = 0.09).
    This line is set in 10-pt type (slug = 0.139; letters = 0.10).
    This line is set in 11-pt type (slug = 0.153; letters = 0.11).
    This line is set in 12-pt type (slug = 0.167; letters = 0.12).

## Slide 15: A-N Displays: 4. Size (Cont.)
For Close-Up Reading:
  Normal reading distance (e.g. book)
    12-16 in.
    14 in. (35.5 cm): nominal reading distance
  Type size in most printed material
    from 7 to 14 pt
    most common about 9 to 11 pt
    i.e. letters = 0.09 – 0.11 in. (2.3-2.8 mm; VA = 22-27 min??)
  Character heights should be increased:
    poor illumination (see table)

## Slide 16: A-N Displays: 4. Size (Cont.)
For Distance Reading:
  Readability and legibility of alphanumeric characters are equal at various distances, provided that:
    As viewing distance ↑ ⇒
    Characters size ↑ (and vice versa) ⇒
    VA (visual angle) subtended at the eye stays the same
  Formula: letter height as function of distance and Snellen visual acuity:
    Ws= 1.45 * 10-5 * S * d
    HL = Ws/R
      Ws, d, HL must be in same units (mm, in.)
      Ws: stroke width
      S: denom. of Snellen visual acuity (e.g. acuity = 20/40 ⇒ S = 40)
      d: reading distance
      HL: letter height
      R: stroke width-to-height ratio of font (e.g. R = 0.20 for ratio: 1:5)
  For low illumination, low contrast ⇒ use large letters
  Design signs for people with at best: Snellen acuity:20/40

## Slide 17: A-N Displays: 5. Layout of Characters
Previous discussion: design of characters
Layout of characters can influence reading:
  Interletter Spacing:
    i.e. how “tight” are letters packed (i.e. density)
    High-density letters: read faster than low density
    Reason: more characters viewable in quality visual field (i.e. fovea) at each fixation (see figure below)
  Interline Spacing:
    More spacing ⇒ ↑ text clarity
    Less spacing ⇒ eye strain, headache

## Slide 18: A-N Displays: 6. Illuminated AN Characters
Characters also presented on
  VDT (visual display terminal), AKA:
  VDU (visual display unit, i.e. computer screen)
Characters on VDT
  readable: 20-30% slower than on hardcopy
  reason:
    Dot-matrix VDT: composed of pixels “picture elements”
    Horiz. line of pixels form “raster scan” or scan lines
    Pixels are lit (turned “on” and “off” to form images)
    e.g. 640 * 480 VDT screen: 480 lines by 640 pixels
    Higher “resolution” ⇒ more pixels per image ⇒ less difference between reading from VDT vs. hardcopy
    Lower resolution (or old VDT): poor accommodation

## Slide 19: A-N Displays: 6. Illuminated Characters (Cont.)
Dot-Matrix displays:
  Characters made up of a matrix of pixels
  Individual character: matrix 5 * 7 to 15 * 24
  See e.g. below: 7 * 9 dot matrix letter ‘B’
  Note, ALL letters/numbers can be created on this formation of dots
  7 * 9: minimum size for reading continuous text
  Small matrices (e.g. 5 * 7):
    individual matrix pixels: visible
    ⇒ reading is affected
  Large matrices:
    Individual pixels: not distinct
    ⇒ performance improves

## Slide 20: A-N Displays: 7. Distance & Size (VDT)
Distance
  VDT Viewed normally farther than hardcopy text
  Eye-to-screen distances:
    24-36 in. (61-93 cm)
    Mean: 30 in. (76 cm)
  ANSI standard: viewing monitor: upright position
    18-20 in.
    Take 20 in. (50 cm): nominal VDT reading distance
Size
  At 20 in. reading distance
    Recommended subtended VA = 11-12 min. of arc
    ⇒ character height = 0.06–0.07 in. (1.5-1.8 mm) (?)
    This is smaller than for hardcopy (0.09-0.11 in.)

## Slide 21: A-N Displays: 7. Distance & Size (cont.)
Size (Cont.)
  ANSI: size for high legibility reading (@ 20 in.)
    Minimum: 16 min. ⇒ Height = 0.09 in. (2.3 mm)
    Preferred: 20-22 min. ⇒ 0.116-0.128 in. (2.9 – 3.3 mm) Note, these are closer to hardcopy reading heights
    Maximum: 24 min. ⇒ 0.14 in. (3.6 mm)
      This is threshold height for comfortable reading
      When character size ↑ ⇒ more foveal fixation required

## Slide 22
Graphic Representations

## Slide 23: GRAPHIC REPRESENTATIONS
Graphic Representations of Text
  Pictorial information: important for speed
  Text information: important for accuracy
  Instructional material: should combine:
    Pictures + Text ⇒ speed + accuracy + retention
Graphic Representations of Data
  Data graphs:
    e.g. Pie charts, bar charts, line graphs
    2-D graphs, 3-D graphs (next slide)
  graph should be
    consistent with numerical data
    Properly, clearly labelled (all variables, units, etc.)
  Some representations: distort data perception
    e.g. May change differences between 2 variables
    e.g. May give impression of false increases

## Slide 24: GRAPHIC REPRESENTATIONS (cont.)

## Slide 25: GRAPHIC REPRESENTATIONS (cont.)

## Slide 26: GRAPHIC REPRESENTATIONS (cont.)

## Slide 27
Symbols

## Slide 28: SYMBOLS
Visual symbols should be very clear
  e.g. men vs. women restroom sign
Comparison of Symbolic & Verbal Signs
  Verbal sign may require “recoding” (i.e. interpretation)
    E.g. sign saying “beware of camels”
  Symbols mostly do not require “recoding”
    E.g. Road sign showing camels crossing
    ⇒ no recoding (i.e. immediate meaning)
  Note, some symbols require learning & recoding
  Ells and Dewar (1979):
    Conducted study on traffic signs and symbols
    Mean reaction time for correct response was less for symbols (next slide)

## Slide 29: SYMBOLS
Comparison of Symbolic & Verbal Signs
  Cont. Ells and Dewar (1979): see results below
Notes: Q: what is meant by degraded viewing condition?

## Slide 30: SYMBOLS (cont.)
Objectives of Symbolic Coding Systems
  Symbolic coding system consists of:
    symbols: that best represent their referents
    referents: concept that symbol represents
  Objective: strong association: symbol-referent
  Association depends on:
    any established association, “recognizability”
    ease of learning such an association
  Guidelines for using coding systems (discussed earlier)
    Detectability
    Discriminability
    Compatibility
    Meaningfulness
    Standardization

## Slide 31: SYMBOLS (cont.)
Symbols:
  Either are used confidently
  Tested experimentally for suitability
Criteria for Selecting Coding symbols
  Recognition: Subjects presented with symbols and asked:
    to write down
    or say what each represents
  Matching:
    symbols are presented to subjects along with a list of all referents represented
    Subjects match each symbol with its referent
    ⇒ confusion matrix : indicating number of times each symbol is confused with every other one
    Also reaction time may be measured

## Slide 32: SYMBOLS (cont.)
Criteria for Selecting Coding symbols (cont)
  Preferences and Opinions: subjects are asked to express their preferences or opinions about design of symbols
Examples of Code Symbol Studies
  Mandatory-Action Symbols
    E.g.: “recognition” testing of symbols + training

## Slide 33: SYMBOLS (cont.)
  Examples of Code Symbol Studies (cont.)
  Comparison of Exit Symbols for Visibility:
    Example of symbol recognition/matching
    Note, Some “no-exit” symbols: perceived as “exit”!

## Slide 34: SYMBOLS (cont.)
  Examples of Code Symbol Studies (cont.)
  Generalizations about features of signs
    Filled figures superior to outline figures
    Square or rectangular backgrounds: better identified than circular figures
    Simplified figures (i.e. reduced number of symbol elements) are better than complex figures

## Slide 35: SYMBOLS (cont.)
Perceptual Principles of Symbolic Design
  Figure to Ground: e.g. Direction must be clear
  Figure Boundaries:
    solid boundary better than outline boundary
  Closure: figure should be closed (ie continuous)
  Simplicity: include only necessary features
  Unity:
    Include text and other detail close to symbol

## Slide 36: SYMBOLS (cont.)
Standardization of Symbolic Displays
  Symbols should be standardized if:
    Used for same referent
    Used by the same people
    E.g. international road signs (below)

## Slide 37
Codes

## Slide 38: CODES
Coding elements:
  Referents: items to be coded
  Code: sign/symbol used to indicate referent
  coding dimensions: visual stimuli used (e.g. colors, shapes, sizes, numbers, letters)
  codes could have
    single dimension
    or more than one dimension (multidimensional)

## Slide 39: CODES (cont.)
Single Coding Dimensions
  Experiments done to see best dimension
  Experiment: Smith and Thomas: varied
    Shapes, geometric form, symbols, colors (below)
    Mean time to count target class was measured
    Color showed greatest superiority (see next slide)

## Slide 40: CODES (cont.)
Single Coding Dimensions
  cont. Experiment by Smith and Thomas
    Results shown below: why is color the best code?

## Slide 41: CODES (cont.)
Single Coding Dimensions (cont.)
  Different coding dimensions differ in relevance for various tasks and situation
  Table (right): guide to selecting appropriate visual code

## Slide 42: CODES (cont.)
Color coding
  Color is a very useful visual code
  Q: What is # of distinct colors that normal color vision person can differentiate (absolute basis)?
  Jones (1962) found that the normal observer could identify 9 surface colors
  With training, people are able to identify around 24 colors
  But when dealing with untrained people, it is wise to use a smaller number of colors
  Color coding is very useful in “searching”/ “spotting” (as compared to other dimensions)
    e.g. searching maps, items in a file, identifying color-coded wires
  Note, color not universal “identification” code

## Slide 43: CODES (cont.)
Multidimensional codes
  Recommended: no more than 2 dimensions be used together for rapid interpretation
  Certain combinations do not ‘go well’ together (see figure)
  ⇒ not always more effective than single- dimension codes

## Slide 44: References
Human Capabilities - Vision
  Human Factors in Engineering and Design. Mark S. Sanders, Ernest J. McCormick. 7th Ed. McGraw: New York, 1993. ISBN: 0-07-112826-3.