## Slide 1
Tata McGraw

## Slide 2
Chapter 4
Product and Service Design

## Slide 3
Product Development Process
Economic Analysis of Development Projects
Designing for the Customer
Design for Manufacturability
Measuring Product Development Performance
OBJECTIVES
4-<number>
Notes: 2

## Slide 4
Companies continuously bring new products to market
Product design is integral to success
Product design differs significantly depending on the industry
Companies often outsource major functions
  Contract manufacturer: an organization capable of manufacturing and/or purchasing all the components needed to produce a finished product

## Slide 5
Core competency: the one thing a company can do better than its competitors
A core competency has three characteristics:
  It provides potential access to a wide variety of markets
  It increases perceived customer benefits
  It is hard for competitors to imitate

## Slide 6
Phase 0: Planning
Phase 1: Concept development
Phase 2: System-level design
Phase 3: Design detail
Phase 4: Testing and refinement
Phase 5: Production ramp-up

## Slide 7
Precedes project approval
Begins with corporate strategy
Includes assessment of technology developments and market objectives
Output is the project mission statement

## Slide 8
Needs of the target market are identified
Alternative product concepts are generated and evaluated
One or more concepts are selected for further development and testing
  Concept: a description of the form, function, and features of a product

## Slide 9
Definition of the product architecture
Decomposition of the product into subsystems and components
Final assembly scheme for the production system is usually defined
Output:
  Geometric layout of the product
  Functional specifications for each subsystem
  Preliminary process flow diagram

## Slide 10
Complete specification of the geometry, materials, and tolerances for all parts
Identification of all the standard parts to be purchased from suppliers
Process plan is established
Tooling is designed
Output:
  Drawings describing the geometry of each part and its tooling
  Specifications of purchased parts
  Process plan

## Slide 11
Construction and evaluation of multiple preproduction versions of product
  Same geometry and material as production version
  Not necessarily fabricated with the actual production processes
Prototypes tested to determine if the product will work as designed

## Slide 12
Product is made using the intended production system
Need to train workers and resolve any remaining problems
Products may be supplied to preferred customers for evaluation
Transition to ongoing production is gradual

## Slide 14: Economic Analysis of Project Development Costs
Using measurable factors to help determine:
  Operational design and development decisions
  Go/no-go milestones
Building a Base-Case Financial Model
  A financial model consisting of major cash flows
  Sensitivity Analysis for “what if” questions
4-<number>

## Slide 15
Quality Function
Deployment
Value Analysis/
Value Engineering
Ideal Customer Product
House of Quality

## Slide 16
Interfunctional teams from marketing, design engineering, and manufacturing
Begins with listening to the customer
  Uses market research
  Customer preferences are defined and broken down into customer requirements
House of quality
Notes: 6

## Slide 17
Customer requirements information forms the basis for this matrix, used to translate them into operating or engineering goals

## Slide 18
Purpose is to simplify products and processes
Objective is to achieve better performance at a lower cost while maintaining all functional requirements defined by the customer
  Does the item have any design features that are not necessary?
  Can two or more parts be combined into one?
  How can we cut down the weight?
  Are there nonstandard parts that can be eliminated?
Notes: 8

## Slide 19
Traditional approach
  “We design it, you build it” or “over the wall”
Concurrent engineering
  “Let’s work together simultaneously”
Notes: 9

## Slide 20
Greatest improvements related to DFMA arise from simplification of the product by reducing the number of separate parts:
  During the operation of the product, does the part move relative to all other parts already assembled?
  Must the part be of a different material or be isolated from other parts already assembled?
  Must the part be separate from all other parts to allow the disassembly of the product for adjustment or maintenance?
Notes: 10

## Slide 21
Service products are very different
Direct customer involvement introduces significant variability in the process
Questions to address:
  How will this variability be addressed?
  What are the implications for operational cost and the customer service experience?

## Slide 22: Measuring Product Development Performance
Measures
Freq. Of new products introduced
Time to market introduction
Number stated and number completed
Actual versus plan
Percentage of sales from new products
Time-to-market
Productivity
Quality
Engineering hours per project
Cost of materials and tooling per project
Actual versus plan
Conformance-reliability in use
Design-performance and customer satisfaction
Yield-factory and field
Performance
Dimension
4-<number>
Notes: 17