## Slide 1
Human Capabilities
Part – I. Hearing (Chapter 6*)
Prepared by: Ahmed M. El-Sherbeeny, PhD
<number>

## Slide 2
Hearing
  Nature and Measurement of Sounds
    Frequency of Sound Waves
    Intensity of Sound
    Complex Sounds
  Masking
Auditory Displays
  Detection of Signals
  Relative Discrimination of Auditory Signals
  Absolute Identification of Auditory Signals
  Sound Localization
Noise
<number>

## Slide 3
Direct vs. Indirect hearing:
  Direct hearing: e.g. baby’s natural cry
  Indirect hearing: e.g. doorbell ⇒ someone at door
  Indirect stimulus can be more effective than direct
    e.g. fire alarm (100% detectable) vs. heat/smoke (75%)
Nature and Measurement of Sounds
  Sound is created by vibrations from a source and is transmitted through a medium (such as atmosphere) to the ear
  Two primary attributes of sound:
    Frequency
    Intensity (or amplitude)
<number>

## Slide 4
Frequency of Sound Waves :
  When sound is generated,
    vibration ⇒ air molecules to move back and forth
    this alternation ⇒ ↑ and ↓ in air pressure
  Vibration forms sinusoidal (sine) waves
    height of wave above and below the midline represents the amount of above-normal and below-normal air pressure respectively
    The waveform above the midline is the image of the waveform below the midline in a sine wave.
    The waveform repeats itself again and again in a sine wave
    frequency of sound:
      “number of cycles per second”
      expressed in: hertz (Hz) ; 1 Hz ≡ 1cycle / 1 second
<number>

## Slide 5
Cont. Frequency of Sound Waves :
  Sinusoidal wave created by a simple sound-generating source
<number>

## Slide 6
Cont. Frequency of Sound Waves :
  The human ear is sensitive to frequencies
    20 to 20,000 Hz
    highest sensitivity: between 1,000 to 3,000 Hz
  Ear is not equally sensitive to all frequencies
  People differ in their relative sensitivities to various frequencies
Intensity of Sound (amplitude/loudness):
  defined in terms of power per unit area
  The Bel (B) [after Alexander Graham Bell] is the basic unit for measuring sound (log scale)
  The most convenient measure is:
    decibel (dB)
    1 dB=0.1B
<number>

## Slide 7
Cont. Intensity of Sound
  Figure 6-2: Decibel levels for various sounds.
  Note ↑ 10 dB ⇒ ↑ 100-fold sound pressure
  Signal-to-Noise Ratio (SNR): difference bet. meaningful signal, & background noise
    e.g. 90 dB signal, 70 dB noise ⇒ SNR = +20 dB
<number>

## Slide 8
Complex Sounds:
  Very few sounds are pure
  Most complex sounds are non-harmonic
  Figure 6-3: waveform of a complex sound formed by 3 individual sine waves
<number>

## Slide 9
Masking (defined):
  Condition when one component of the sound environment reduces the sensitivity of the ear to another component
  It is amount that the “threshold of audibility” of a sound (the masked sound) is raised by the presence of another (masking) sound
  Q: Can you a give an example of “masked” and “masking” sounds from our everyday lives?
  Q: difference between masked and complex sounds?
<number>

## Slide 10
Chapter 3: auditory vs. visual modality (e.g. auditory preferred: message is short, simple)
4 types of human functions/tasks involved in the reception of auditory signals:
Detection (i.e. whether a signal is present)
Relative discrimination (differentiating bet. ≥2 signals presented together)
Absolute identification (only 1 signal is present)
Localization (knowing the direction that the signal is coming from)
<number>

## Slide 11
Detection of signals
  Signals can occur in “peaceful” surroundings or noisy surroundings
  The signal plus noise (SN) should be distinct from the noise (N) itself
  Otherwise, signal cannot always be detected in the presence of noise
    i.e. signal (masked sound) + noise (masking sound) ⇒ threshold of detectability is elevated
    ⇒ signal must be > threshold to detect signal
  Using filters ⇒ noise removed ⇒ ↑ detectability, SNR ⇒ more audible sound
<number>

## Slide 12
Relative Discrimination of Auditory Signals
  Relative discrimination of signals on basis of
    intensity
    frequency
  A common measure of discriminability: just-noticeable difference (JND):
    JND: “the smallest difference or change along a stimulus dimension (frequency, intensity) that can just be detected 50% of the time by people.”
    The smaller the JND, the easier it is for people to detect differences on the dimension being changed.
      Small JND ⇒ subjects could detect small changes
      Large JND ⇒ large change necessary before noticing change
<number>

## Slide 13
Absolute Identification
  This is used when it is necessary to make an absolute identification of an individual stimulus (by itself)
  e.g. identify
    someone’s pitch/frequency
    specific animal/bird
    certain car siren/honk tone
    Sound durations
  Number of levels along a continuum (range or scale) that can identified usually is quiet small
  It is better to use more dimensions with fewer steps or levels of each dimension, than to use fewer dimensions and more levels of each
<number>

## Slide 14
Localization
  Stereophony: “the ability to localize (guess/predict) the direction from which the sound is emanating (coming from)”
  Primary factors/cues used to determine direction
    intensity of sound
    phase (lag) of sound
    e.g. if sound reaches directly one side of head first, sound reaches the nearer ear approx. 0.8 ms before other ear ⇒ localizing sounds below 1500 Hz
    For frequencies > 3000 Hz, intensity is used to localize sound (e.g. try to gradually increase volume in one speaker and decrease volume in opposite speaker)
    Sounds between 1500-3000 Hz: hard to localize
<number>

## Slide 15
Special purpose auditory displays:
  Warning and alarm signals
    Each signal having preferred frequency, intensity
    Each causing certain “attention-getting” and “noise-penetration” ability
  Aids for the blind
    Mobility aids (go-no-go safety signals at certain distance)
    Environmental sensors (information about surrounding, e.g. surface characteristics, directional information, distance)
<number>

## Slide 16
Noise ≡
  “Unwanted sound”
  Information theory: “auditory stimulus of stimuli bearing no informational relationship to the presence or completion of the immediate task”
Effects of noise
  Hearing loss (e.g. occupational hearing loss)
  Temporary loss, permanent loss
  Physiological effects
  Psychological effects
<number>

## Slide 17
Human Capabilities - Hearing
  Human Factors in Engineering and Design. Mark S. Sanders, Ernest J. McCormick. 7th Ed. McGraw: New York, 1993. ISBN: 0-07-112826-3.
  Slides by: Dr. Khaled Al-Saleh; online at: http://faculty.ksu.edu.sa/alsaleh/default.aspx
<number>
Notes: <number>