## Slide 1: Motion Study and Work Design
Sections:
Basic Motion Elements and Work Analysis – part 1
Micromotion Analysis – part 1
Principles of Motion Economy and Work Design – part 2

## Slide 2: Definitions
Motion study - analysis of the basic hand, arm, and body movements of workers as they perform work
Work design - design of the methods and motions used to perform a task
Includes:
  Workplace layout and environment
  Tooling and equipment used in the task

## Slide 3: Motion Study and Work Design
Basic Motion Elements and Work Analysis

## Slide 4: The Pyramidal Structure of Work
Remember?
Work consists of tasks
  Tasks consist of work elements
    Work elements consist of basic motion elements

## Slide 5: Basic Motion Elements
Therbligs* – 17** basic motion elements
  Basic building blocks of virtually all manual work performed at a single location
  Invented/refined by Frank and Lillian Gilbreth (1908 – 1924): “motion cycles”
  Used to
    examine smallest of motions
    categorize motions
    Identify unnecessary / fatigue producing motions
  Note, not related to “time study” (only motion)***
Notes: * Can you guess where the name Therbligs came from? A: -mostly- Gilbreth spelled backwards
* * Anywhere between 15 – 18 elements, depending on classification or textbook (we will stick here with these 17)
MTM stands for: Methods-Time Measurement; MOST: Maynard Operation Sequence Technique; MTM, MOST: modern work measurement systems that utilize Therbligs
* * * Time would be identified later when adding time to Therbligs plotted on a SIMO chart, in order to identify positions of time-wasting motions

## Slide 6: Basic Motion Elements
  Watch movie “Frank & Lillian Gilbreth” https://youtu.be/ZsQ7KPO6DOw
Reading assignment: “Therbligs: The Keys to Simplifying Work”
  http://web.mit.edu/allanmc/www/Therblgs.pdf
  Or here:
  http://gilbrethnetwork.tripod.com/therbligs.html
Notes: * Can you guess where the name Therbligs came from? A: -mostly- Gilbreth spelled backwards
* * Anywhere between 15 – 18 elements, depending on classification or textbook (we will stick here with these 17)
MTM stands for: Methods-Time Measurement

## Slide 7: Therbligs
Therbligs symbols chart (18)
*
Notes: * Find (F) Therblig is non-existent in some textbooks; Read in handout [Therbligs The Keys to Simplifying Work] “Dr. Barnes eliminated this Therblig, explaining that it was a mental reaction, at the end of the Search cycle.” Source: http://web.mit.edu/allanmc/www/Therblgs.pdf
Note how each Therblig has a specific color (to help identify it; see how HFE course was important in specifying this)

## Slide 8: Therbligs
Therbligs symbols chart (18)

## Slide 9: Therbligs
Transport empty (TE) – reach for an object
  {icon shows an empty hand}
Grasp (G) – grasp an object
  {icon suggesting by a hand poised over an object, ready to grasp it}
Transport loaded (TL) – move an object with hand and arm
  {icon shows a hand cupped, holding an object}

## Slide 10: Therbligs
Hold (H) – hold an object
  {icon suggested by a horseshoe magnet holding a bar}
Release load (RL) – release control of an object
  {icon suggested by a hand with an object poised to drop}
Use (U) – manipulate a tool
  {icon is simple the letter U ---for Use}

## Slide 11: Therbligs (continued)
Pre-position (PP) – position object for next operation
  {icon suggests a bowling pin being placed into proper position}
Position (P) – position object in defined location
  {icon suggests an object, such as a pen, being placed in the hand, ready to Use}
Assemble (A) – join two parts
  {icon shows several items (lines) placed together}

## Slide 12: Therbligs (continued)
Disassemble (DA) – separate multiple parts that were previously joined
  {icon shows Assemble symbol with one part removed}
Search (Sh) – attempt to find an object using eyes or hand
  {icon suggested by an eye turned, as if searching}

## Slide 13: Therbligs (continued)
Select (St) – choose among several objects in a group
  {icon suggested by an arrow aimed at an object, much the same as a computer cursor in form and intent}
Plan (Pn) – decide on an action
  {icon shows a worker with fingers on head, thinking}
Inspect (I) – determine quality of object
  {icon suggests a magnifying glass}

## Slide 14: Therbligs (continued)
Unavoidable delay (UD) – waiting due to factors beyond worker control
  {icon suggested by a man bumping his nose unintentionally}
Avoidable delay (AD) – worker waiting
  {icon shows a worker intentionally lying down on the job}
Rest (R) – resting to overcome fatigue
  {icon shows a person resting in a seated position}

## Slide 15: Classification of Therbligs
Effective therbligs:
Transport empty
Grasp
Transport loaded
Release load
Use
Assemble
Disassemble
Inspect
Rest
Ineffective therbligs:
Hold
Pre-position
Position
Search
Select
Plan
Unavoidable delay
Avoidable delay
Notes: Q: can you identify the reason for each of the effective and ineffective therbligs?

## Slide 16: Classification of Therbligs
Types of Therbligs
Motions required for performing an operation
Motions that tend to slow down type 1 motion
Motions that do not perform an operation
Notes: Note, this is another classification (from another source on the same topic)

## Slide 17: Classification of Therbligs
Types of Therbligs
Motions required for performing an operation:
  Transport empty
  Grasp
  Transport loaded (carry)
  Position
  Use
  Assemble
  Disassemble
  Release load
  Inspect

## Slide 18: Classification of Therbligs
Types of Therbligs
Motions that tend to slow down type 1 motion :
  Search
  Find*
  Select
  Plan (person thinking)
  Pre-position (set up)
Notes: * Find (F) Therblig is non-existent in some textbooks; Read in handout [Therbligs The Keys to Simplifying Work] “Dr. Barnes eliminated this Therblig, explaining that it was a mental reaction, at the end of the Search cycle.” Source: http://web.mit.edu/allanmc/www/Therblgs.pdf

## Slide 19: Classification of Therbligs
Types of Therbligs
Motions that do not perform an operation :
  Hold
  Unavoidable delay
  Avoidable delay (standby)
  Rest

## Slide 20: Benefits of Classification
Use motions which are easy and effective,
Discard motions which are awkward, fatiguing and ineffective
People who accomplish the most do not necessarily work hardest
Watch video on application of therbligs on a simple task: https://youtu.be/z2EYyPA2Gik
Notes: Here is another very good (detailed) video on therbligs: https://youtu.be/O77elB7-CYE (watch first part only for now: motion study; time study later)

## Slide 21: Benefits of Classification
Identifying/solving avoidable delay
  e.g. person selecting parts for assembly
    exclusively with one hand
    while the other remains idle
  Effects:
    work is slowed down, also
    hand being used is becoming more fatigued
  Solution: use of both hands
  How? encouraging workers to become more “ambidextrous”
Notes: Ambidextrous: the ability to use both hands for work

## Slide 22: Motion Study and Work Design
Micromotion Analysis

## Slide 23: Micromotion Analysis
Activities of two or more workers on group work
Relationship: operator’s activities and machine
Timing operation
Obtain time-motion data for time standards
Permanent record of method and time
Research (motion and time study)

## Slide 24: Micromotion Analysis
Main objectives:
  Finding the preferred method of doing work
  Training individuals to understand the meaning of motion study
  Analysis of therbligs that make up a repetitive task

## Slide 25: Micromotion Analysis
Detailed objectives:
  Eliminate ineffective therbligs if possible
  Avoid holding objects with hand – Use workholder
  Combine therbligs – Perform right-hand and left-hand motions simultaneously
  Simplify overall method
  Reduce time for a motion, e.g., shorten distance

## Slide 26: Micromotion Analysis – Technique
Filming operation
Analyzing the film
Charting the results
Developing an improved method
Reading assignment 2: “Micromotion Analysis Checklist for Possible Improvements” (course website)

## Slide 27: Micromotion Analysis – Example
Part of “Micromotion study analysis sheet” (aka left-right hand chart)
Operation: Finish hand filing copper work piece
Notes: Note how this greatly resembles the “two handed process chart”, but of course the intention here is different, here we want to show/emphasize basic motion elements (not flow of processes)
Source: http://www.yourarticlelibrary.com/ergonomics/simo-simultaneous-motion-cycle-chart-meaning-method-to-improve-and-construction/34465/
Note, chart above must also include the following info: Micro motion Study
Dept……………………………………………. Film No……………….
Analysis Sheet
Operation: Finish hand fillings
Charted By……………….
Date……………………………………………………………………………….. Operator…………………

## Slide 28: Micromotion Analysis – Exercise
Sitting at her desk, the writer reached for the mechanical pencil, picked it up, positioned it, and then began to write on notepad of paper. After finishing one sentence, she lifted the pencil, and read the sentence. She then put the pencil aside and reached for the rectangular eraser nearby. Grasping and positioning it, she erased one of the words in the sentence.
Write a list of the therbligs that comprise this motion sequence and label each basic motion with a brief description.