## Slide 1: Chapter 9
Communications and Networks
McGraw-Hill
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>

## Slide 2: Competencies (Page 1 of 2)
Discuss connectivity, the wireless revolution, and communication systems.
Describe physical and wireless communications channels.
Discuss connection devices, and services including dial-up, DSL, cable, satellite/air, and cellular.
Describe data transmission factors, including bandwidths and protocols.
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>

## Slide 3: Competencies (Page 2 of 2)
Discuss networks and key network terminologies.
Describe different types of networks, including local, home, wireless, personal, metropolitan, and wide area networks.
Describe network architectures, including topologies, and strategies.
Describe organization issues related to Internet technologies and network security.
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>

## Slide 4: Introduction
We live in a truly connected society.
Increased connectivity potentially means increased productivity especially in the business world.
You will learn more about the concept of connectivity and the impact of the wireless revolution in this chapter.
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>

## Slide 5: Communications
1-<number>
The process of sharing data, programs, and information between two or more computers
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>
Ask students to give examples of communication devices that they use daily

## Slide 6: Communications Today
Numerous applications depend on communication systems—E-mail, Instant messaging (IM), Internet telephone, and Electronic commerce
Connectivity uses computer networks to link people and resources
Going wireless has been the most dramatic change
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>
Connectivity is a concept related to using computer networks to link people and resources
Microcomputers. minicomputers, and mainframes can all be connected
Wireless revolution
  Use of mobile or wireless devices
  The revolution is the support of more than just the wireless telephone
  Many devices can and will connect to one another without any physical connection

## Slide 7: Communication Systems
Four basic elements
  Sending and receiving devices
  Communication channel
  Connection devices
  Data transmission specifications
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>
Electronic systems that transmit data from one location to another
Communication systems can be wired or wireless
Basic elements
  Sending and receiving devices – computer or a specialized communication device
  Communication channel – carries the message
  Connection devices – act as an interface between sending and receiving devices; convert outgoing messages into packets (key term) that can travel across the communication channel
  Data transmission specifications – rules and procedures that coordinate the sending and receiving devices

## Slide 8: Communication Channels
Channels carry data from one computer to another
Two categories of communication channels
  Physical connection
  Wireless connection
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>
Channels are essential to a communication system
They carry data
Types of channels
  Telephone lines (key term)
  Coaxial cables(key term)
  Fiber-optic cable (key term)
  Infrared (key term)
  Broadcast radio (key term)
  Microwave (key term)
  Satellite (key term)

## Slide 9: Physical Connections
Ethernet cable
(Twisted pair cables)
Coaxial cable
Fiber-optic cable
1-<number>
Return
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>
Ethernet cable – consists of twisted pair cable; slowest; being phased out by more advanced and reliable media
Coaxial cable – single solid copper core; 80 times transmission of twisted pair; television and computer networks
Fiber optic – 26,000 times capacity of twisted pair cable; more secure and reliable; best over limited distances; lighter, more reliable, and less expensive than coaxial cable

## Slide 10: Wireless Connections
Radio frequency (RF)
  Wi-Fi (wireless fidelity) 802.11
  Bluetooth
Microwave
  Line of sight
Satellite
  GPS
Infrared
  Short distances
  Line of sight
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>
Wireless connections do not use a solid substance to connect; uses the air itself
Types of wireless connections are:
  Infrared
    Light waves used over short distances
    Sometimes called line of sight communications
    Sending and receiving devices must be in clear view of one another
  Broadcast radio
    Uses towers called transceivers (key term)
    Web-enabled devices follow a standard known as Wi-Fi (wireless fidelity)
  Microwave
    Uses high-frequency radio waves
    Also line of sight
    Used for short distances
  Satellite uses satellites orbiting about 22,000 miles above the earth as microwave relay stations; many of these offered by Intelsat, the International Telecommunications Satellite Consortium which is owned by 114 governments and forms a worldwide communications system
  Satellites can be used to send and receive data; Uplink
  is sending data to satellite and Downlink refers to receiving data from a Satellite
  GPS (Global Positioning system) use a network of 24 satellites owned and managed by the Defense Department which continuously sends location information to earth

## Slide 11: Communication Channels Summary
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>

## Slide 12: Connection Device Signals
Types of signals
  Analog
  Digital
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>
Signals
  Sent analog – telephone signals; continuous electronic wave
  Sent digital – computer signals; presence or absence of an electronic pulse; on/off

## Slide 13: Connection Devices
Types of modems
  Telephone
  DSL
  Cable
  Wireless
1-<number>
Transfer Speeds
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>
Modem – modulator-demodulator
  Modulation (key term) is the name of the process for converting from digital to analog
  Demodulation (key term) is the name of the process for converting from analog to digital
  Telephone – can be either internal or external; connects computer directly to a telephone line
  DSL – uses standard phone lines; external and uses either USB or Ethernet
  Cable – coaxial cable – same as your television; uses either USB or Ethernet
  Wireless modem
    Does not use cables
    Also known as WWAN (wireless wide are network modem) (key term)
    Signals are sent through the air
    Transfer Speed or transfer rate (key term)-measured in bits per second (key term); the higher the speed the faster the transfer rate

## Slide 14: Connection Services
Dial-Up services
Leased lines – T1
  T3 and DS3 have higher capacity
Digital subscriber line (DSL)
  Uses existing phone lines
  One type widely used is ADSL
Cable
  Uses existing TV cable
  Provides speeds as fast as DSL at a lower cost
Satellite/air connection services
  Seven times faster than dial-up
  Slower than DSL & cable modem
Cellular Services - use 3G cellular network
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>
Standard telephone lines and conventional modems use a dial-up service
  Slow
  Still popular, but many are using other types of connections
T1, T2, T3, and T4 leased lines – do not require conventional modems and provide very high capacity and is expensive—mainly used by corporations not typical end user; T1 lines provide a speed of 1.5 mbps (mega bits per second)(key term) which is over 26 times as fast as a conventional modem
DSL – uses existing telephone lines to provide high-speed connections; uses DSL modems
Cable – Cable connections reach 90% of homes in America but not all cable companies support cable modems presently
Satellite/air connection services – Uses just what it says—satellite and air connections; older satellites couldn’t upload and dial up was still used for the process; but newer satellites are two-way satellites capable of handling both uploading and downloading; available almost anywhere but slower than DSL
Cellular services – option for mobile devices and laptops using 3G cellular networks (key term) – current access is limited but growing – download speed 400 – 700 Kpbs and upload at 50 Kbps – future service to have speeds equal to DSL

## Slide 15: Typical User Connection Costs & Speeds
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>
This is a good time to discuss the various connection services available to the public
  Verizon
  Time Warner
  Comcast
  Others

## Slide 16: Bandwidth
Measurement of the capacity of the channel
Categories
  Voice band also known as low bandwidth
  Medium band
  Broadband
  Baseband
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>
Several technical matters affect data communications
One is bandwidth – bits-per-second (bps) transmission capability of a channel
Three types:
  Voiceband – also known as low bandwidth; standard phone line; too slow for many types of transmissions – especially high-quality video; typical speeds are 56 to 96 kbps
  Medium band – with special leased lines to connect minicomputers and mainframes as well as to transmit data over long distances (for larger computer systems); not typically used by individuals
  Broadband – used for high-capacity transmissions (DSL, cable, satellite connections); specialized high-speed devices; effectively transmits high-quality video and other communication needs; typically 1.5 mbps; higher speeds possible
  Baseband – widely used to connect individual computers that are located close to one another

## Slide 17: Protocols
Set of communication rules
Standard for Internet: TCP/IP (Transmission control protocol/Internet protocol)
  Identification
  Packetization
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>
Rules for exchanging data between computers
Essential features of protocol
  Identification - Identifying sending and receiving devices (IP address); (key term) Internet unique number address; domain name server (DNS) (key term) converts text-based addresses to IP addresses
  Packetization – allows message to be broken into so easier to transmit over Internet through various interconnected networks; allows message to be reassembled at destination

## Slide 18: Careers In IT
Network Administrator
  Manage a company’s LAN and WAN networks
  Maintain hardware and software
  Diagnose and repair problems
  Candidates usually have a bachelor’s degree in computer science and practical experience
  Annual salary is typically between $48,500 and $79,000
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>

## Slide 19: A Look to the Future
Telepresence Lets You Be There
  Seeks to create the illusion that you are actually at a remote location
  Early implementations mainly focus on an extension of video- conferencing
  Someday could beyond simple voice
1-<number>
Copyright © 2011 by The McGraw-Hill Companies, Inc. All rights reserved.
Notes: <number>