## Slide 1: Direct Time Study
Sections:
Direct Time Study Procedure – part 1
Number of Work Cycles to be Timed – part 2
Performance Rating – part 2
Time Study Equipment – part 2

## Slide 2: Direct Time Study - Defined
Direct Time Study:
  aka stopwatch time study
  direct & continuous observation of task
  using stopwatch or other timekeeping device
  to record time taken to accomplish task
ANSI definition:
  careful time measurement of task
  using time measuring instrument
  allows adequate time (foreign elements, delays, fatigue, and personal needs)
  task usu. broken down into work elements
Notes: ANSI Z94.11-1989

## Slide 3: Direct Time Study - Defined
While observing & recording time
  appraisal of worker’s performance level is made
  data then used to compute standard time for task (after adding )

## Slide 4: Direct Time Study - Defined
Background:
  first work measurement technique (1883)
  connected with origins of IE
  computerized techniques improved DTS i.t.o
    accuracy
    application speed of DTS
    database management functions that support it

## Slide 5: Direct Time Study - Defined
Applications:
  tasks that involve repetitive work cycle
  at least a portion of which is manual
  common in batch & mass manufacturing
Limitations:
  time-consuming  justified when,
    job has relatively long production run
    will be repeated in the future
  cannot be used to set prior to start of production
Notes: * i.e. production must be first completed in order to set Tstd

## Slide 6: Direct Time Study
Direct Time Study Procedure

## Slide 7: Direct Time Study Procedure
Define & document standard method
Divide task into work elements
  Note 1 & 2: before actual timing begins
Time work elements to get observed time,
Evaluate worker’s pace relative to standard performance to obtain normal time
  Called performance rating (PR):
  Note steps 3 & 4: done at same time; for several work cycles; values: averaged*
Apply allowance factor to compute standard time
Notes: * aka normalized time

## Slide 8: 1. Document the Standard Method
Methods engineering study and documentation:
  Determine the “one best method”
  Then document:
    all steps in method,
    hand & body motions
    special tools, gauges, equipment, equipment settings (e.g., feeds, speeds),
    irregular elements & their frequency
    workplace layout, working conditions
    all included in,
      “methods description form”
      videotape: for complex tasks

## Slide 9: 1. Document the Standard Method
Seek worker’s advice if possible
Once standard method is defined,
  it should not be possible for operator to make further improvements

## Slide 10: 13.1
Form to document the standard method
Notes: Operation is used here to mean task; note how you must determine the work elements for the operation (i.e. task)

## Slide 11: Why Documentation is Important
Batch production
  repeat orders after a significant time lapse
Methods improvements by operator*
  to restudy task, must be able to prove a change has occurred
Disputes about method
  operator complains that standard is too tight
  is operator using standard method?
Data for standard data system
  good documentation is essential for developing a standard data system
Notes: * worker may be able to figure out some motion shortcut or hand tool or other gimmick that reduces the time for the work cycle

## Slide 12: 2. Divide Task into Work Elements
Guidelines:
Each work element should consist of a logical group of motion elements with unified purpose
Beginning point of one element should be end point of preceding element
Each element should have a readily identifiable end point
Work elements should not be
  too long
  nor too short
Separate irregular elements, machine elements, internal elements
Notes: irregular elements, machine elements, internal elements?

## Slide 13: 2. Divide Task into Work Elements
Notes: irregular elements, machine elements, internal elements?

## Slide 14: 2. Divide Task into Work Elements
Notes: irregular elements, machine elements, internal elements?

## Slide 15: 3. Time the Work Elements
Time data usu. recorded on DTS form
Each element should be timed
  over several work cycles
  to obtain a reliable average
  number of cycles determined using statistical techniques (later)

## Slide 16: 13.2
Direct time study form
Notes: How to calculate Tn for irregular elements?

## Slide 17: 3. Time the Work Elements
Stopwatch timing methods:
  Snapback timing method
    stopwatch is reset to zero at the start of each work element
    reader must record final time for element just as watch is being zeroed
  Continuous timing method
    stopwatch: allowed to run continuously throughout duration of work cycle
    analyst records running time on stopwatch at end of each element
    may zero at beginning of each work cycle  starting time of any cycle always

## Slide 18: Advantages of Each Timing Method
Advantages of snapback method:
  Analyst can readily see how element times vary from cycle to cycle
  No subtraction necessary to obtain individual element times
Advantages of continuous method:
  Elements cannot be omitted by mistake
  Regular and irregular elements can be more readily distinguished
  Manipulation and resetting of the stopwatch is reduced
Notes:   Regular and irregular elements can be more readily distinguished?

## Slide 19: 4. Performance Rating
Analyst simultaneously
  observe performance of worker
  AND judge performance/pace of worker
    relative to definition of standard performance used by organization
Standard performance:
  Slower pace than standard:  longer (for work cycle)
  Faster pace than standard  shorter
Normal time for element/cycle:
Notes: Other names for normal time: include normalized time and base time
See slides from 5-A for more details on this equation

## Slide 20: 4. Performance Rating
Notes regarding performance rating:
  most difficult & controversial step in DTS
    since requires judgment of analyst to assess value of PR
  It is in worker’s interest & advantage to receive high PR during study
     and for task will be longer
     looser standard
     easier for worker to achieve a higher efficiency level as job continues
    this’s important to worker if s/he paid on wage incentive plan

## Slide 21: 5. Apply Allowances
A PFD allowance is added to the normal time to compute standard time
  where = allowance factor
    Personal time
    Fatigue
    Delays
The function of allowance factor:
  inflate value of standard time
  accounts for various reasons why worker loses time during shift

## Slide 22: Example 1
A direct time study was taken on a manual work element using the snapback method. The regular cycle consisted of three elements, a, b, and c. Element d is an irregular element performed every 5 cycles.
Work element a b c d
Observed time (min) 0.56 0.25 0.50 1.10
Performance rating 100% 80% 110% 100%
Determine (a) normal time and (b) standard time for the cycle using an allowance factor of 15%.*
Notes: * If not included, can be considered as default value (15%)

## Slide 23: Solution
(a) Normal time:
(b) Standard time:

## Slide 24: 5. Apply Allowances
  : normal time of worker during the worker-controlled portion of the cycle, min
  : PFD allowance
  : machine cycle time, min
  : machine allowance
    If company policy does not recognize separate machine allowance 
      , or
      set equal to value of
Notes: This is repeat from slides 5 - A

## Slide 25: Example 2

## Slide 26: Solution