## Slide 1
<number>
5. WEIGHT VOLUME RELATIONSHIPS

## Slide 2
<number>
Soil deposits comprise the accumulated solid particles plus the void space between the particles
The void spaces are partially or completely filled with water or other liquid.
Voids space not occupied by fluid are filled with air or other gas.
Hence soil deposits are referred to as three-phase system, i.e. Solid + Liquid (water) + Gas (air)
GENERAL

## Slide 3
<number>
Properties such as strength, compressibility, permeability are directly related to the ratio and interaction of these three phases.
GENERAL (continued)
Therefore, an understanding of the terminology and definitions relating to soil composition is fundamental to the study of soil mechanics and geotechnical engineering as a whole.
Bulk soil as it exists in nature is a more or less random accumulation of soil particles, water, and air as shown above.

## Slide 4
<number>
Volumes
Weights
For purpose of study and analysis it is convenient to represent the soil mass by a PHASE DIAGRAM, with part of the diagram representing the solid particles, part representing water or liquid, and another part air or other gas.
PHASE DIAGRAM

## Slide 5
<number>
Phase diagram in terms of mass

## Slide 6
<number>
Possible Cases:

## Slide 7
<number>
The total volume of a given soil sample can be expressed as:
Where
V = Total volume
Vs = Volume of soil solids
Vv = Volume of voids
Vw = Volume of water
Va = Volume of air
Assuming that the weight of the air is negligible, we can give the total weight of the sample as
Where Ws = weight of solids
Ww = weight of water
In engineering practice we usually measure the total volume, V, the mass of water, Mw, and the mass of dry solid Ms.

## Slide 8
<number>
Volume Relationships
There are three volumetric ratios that are very useful in geotechnical engineering , and these can be determined directly from the phase diagram
1. Void Ratio
2. Porosity
3. Degree of Saturation
Porosity and degree of saturation are commonly expressed as a percentage.

## Slide 9
<number>
water
air
soil
In this illustration,
e = 1
n = 50%
S = 50%

## Slide 10
<number>
Weight or Mass Relationships
The common term used for weight relationships are:
Moisture content (w) is also referred to as water content and is defined as the ratio of weight of water to the weight of solids in a given volume of soil:
Moisture content

## Slide 11
<number>
1. Unit weight (total, wet or moist unit weight) () is the weight of soil per unit volume.
Weight-Volume, Mass-Volume Relationships
2. Solid unit weight
3. Unit weight of water
I. Unit Weights (N/m3 or kN/m3)

## Slide 12
<number>
Weight-Volume, Mass-Volume Relationship
4. Dry unit weight
5. Saturated unit weight
6. Submerged unit weight

## Slide 13
<number>
II. Densities (g/cm3 or kg/m3)
Because the Newton is a derived unit, working with mass densities of soil may sometimes be convenient.
The SI unit of mass density is kilograms per cubic meter (kg/m3). We can write the density equations by replacing weight with mass in all equations in the preceding slides.
The density of water w varies slightly, depending on the temperature. At 4Co when water is at its densest, exactly equal 1000 kg/m3 or 1g/cm3)
Relationship between unit weight and density
The unit weights of soil in N/m3 can be obtained from densities in kg/m3 as

## Slide 14
<number>
Density and Unit Weight
Mass is a measure of a body's inertia, or its "quantity of matter". Mass does not changed at different places.
Weight is force, the force of gravity acting on a body. The value is different at various places.
The unit weight is more frequently used than the density is (e.g. in calculating the overburden pressure).
Note: The density/or unit weight are ratios which connects the volumetric side of the PHASE DIAGRAM with the mass/or weight side.

## Slide 15
<number>
Relationships Between Various Physical Properties
All the weight - volume relationships needed in soil mechanics can be derived from appropriate combinations of six fundamental definitions. They are:
Void ratio
Porosity
Degree of saturation
Water content
Unit weight
Specific gravity

## Slide 16
<number>
1. Relationship between void ratio and porosity
2. Relationship among Void ratio, Degree of Saturation, Water content, and Specific Gravity
Dividing the denominator and numerator of the R.H.S. by Vv yields:
This is a very useful relation for solving THREE-PHASE RELATIONSHIPS.

## Slide 17
<number>
Textbook derivation

## Slide 18
<number>
3. Relationship among Unit Weight, Void Ratio, Degree of Saturation and Specific Gravity
Notes:
Unit weights for dry, fully saturated and submerged cases can be derived from the upper equation
Water content can be used instead of degree of saturation.
Submerged unit weight can be approximated as

## Slide 19
<number>
Various Unit Weight Relationships

## Slide 20
<number>
Example 1
Instead think of

## Slide 21
<number>
Field density testing (i.e., sand replacement method) has shown bulk density of a compacted road base to be 2.06 t/m3 with a water content of 11.6%. Specific gravity of the soil grains is 2.69. Calculate the dry density, porosity, void ratio and degree of saturation.
Example 2
The rest is vey simple

## Slide 22
<number>
Example 3

## Slide 23
<number>

## Slide 24
<number>
Our Solution
S = 1
w =25.7
e = 0.668

## Slide 25
<number>
Example 4
V= 0.0282 m3
S = 56%
w = 18.5%
Gs = 2.529
Required:
e

d

## Slide 26
<number>

## Slide 27
<number>

## Slide 28
<number>
Our Solution
S = 56%
w = 18.5%
Gs = 2.529

## Slide 29
<number>
Relative Density
The relative density Dr, also called density index is commonly used to indicate the IN SITU denseness or looseness of granular soils.
The relative density is the parameter that compare the volume reduction achieved from compaction to the maximum possible volume reduction.
Volume reduction from compaction of granular soil

## Slide 30
<number>
Dr can be expressed either in terms of void ratios or dry densities.
Why e not n?

## Slide 31
<number>
Remarks
The relative density of a natural soil very strongly affects its engineering behavior.
The range of values of Dr may vary from a minimum of zero for very LOOSE soil to a maximum of 100% for a very DENSE soil.
Because of the irregular size and shape of granular particles, it is not possible to obtain a ZERO volume of voids. (Do you remember well-graded vs. poorly-graded!!)
ASTM test designations D-4253 and D-4254 (2007) provide procedure for determining maximum and minimum dry unit weights of granular soils.

## Slide 32
<number>
Granular soils are qualitatively described according to their relative densities as shown below
The use of relative density has been restricted to granular soils because of the difficulty of determining emax in clayey soils. Liquidity Index in fine-grained soils is of similar use as Dr in granular soils.