## Slide 1: Manufacturing Engineering Technology in SI Units, 6th Edition Chapter 25: Machining Centers, Machine Tool Structures and Machining Economics
Copyright © 2010 Pearson Education South Asia Pte Ltd
Manufacturing Processes (2), IE-352
Ahmed M El-Sherbeeny, PhD
Spring 2017
Notes: Presentation slide for courses, classes, lectures et al.

## Slide 2: Chapter Outline
Introduction
Machining Centers
Machine-tool Structures
Vibration and Chatter in Machining Operations
High-speed Machining
Hard Machining
Ultraprecision Machining
Machining Economics
Copyright © 2010 Pearson Education South Asia Pte Ltd

## Slide 3: Machining Economics
Limitations of machining/material removal operations:
Wasted material (although may be small)
Longer time (vs. forming/shaping): cutting/non-cutting
Require more energy (vs. forming/shaping)
Adverse effects on surface quality / properties of product
Importance of machining (despite above):
Producing complex workpiece shapes (e.g. internal features)
High dimensional accuracy / surface finish

## Slide 4: Machining Economics
Costs/factors involved with machining:
Machine tools, work-holding devices, fixtures and cutting tools
Labor and overhead
Setting up time (machine for operation)
Material handling and movement (e.g. loading blank, unloading machine part)
Gaging for dimensional accuracy and surface finish
Cutting times and non-cutting time

## Slide 5: Machining Economics
Minimizing Machining Cost per Piece
Important in all manufacturing processes to minimize:
  Machining cost per piece,
  Machining time per piece,
Various approaches exist (using software)
Important: input data must be accurate and up to date to be reliable
We show here simple/popular method of analyzing machining cost in turning operation

## Slide 6: Machining Economics
Cont. Minimizing Machining Cost per Piece
Total machining cost per piece, , in turning is
Following slides: discuss each of these costs in more detail

## Slide 7: Machining Economics
Cont. Minimizing Machining Cost per Piece
Machining cost per piece, , is given by:
  : machining time per piece
  : labor cost of production personnel per hour
  : burden rate (aka overhead charge), including:
    Depreciation
    Maintenance
    Indirect labor, etc.
The setup cost, ,is fixed amount (in $) per piece

## Slide 8: Machining Economics
Cont. Minimizing Machining Cost per Piece
Loading/unloading, machine-handling cost, , per piece:
  : time required to,
    load/unload part
    change speeds
    change feed rates, etc.
  and : see last slide

## Slide 9: Machining Economics
Cont. Minimizing Machining Cost per Piece
The tooling cost, , per piece:
  : numbered of parts machined per insert
  : numbered of parts that can produced per insert face
  : time required to change the insert
  : time required to index the insert
  : depreciation of insert (in $)

## Slide 10: Machining Economics
Cont. Minimizing Machining Cost per Piece
The time required to produce one part is
  : calculated for each particular operation
Example: for turning:
  : length of cut
  : feed
  : angular speed () of the workpiece
  : workpiece diameter
  : cutting speed (note, appropriate units must be used)

## Slide 11: Machining Economics
Cont. Minimizing Machining Cost per Piece
From the Taylor tool-life equation,
  : time () to reach a certain flank wear (before regrinding/changing insert)
The number of pieces per insert face:
Number of pieces per insert:
  : number of faces actually used
    Note, : not necessarily number of faces per insert
    Reason: not all faces are used before insert is discarded
Combining and in :

## Slide 12: Machining Economics
Cont. Minimizing Machining Cost per Piece
We now seek to determine optimum () and ()
First we find and for min. cost,
We differentiate with respect to and set it to zero,


## Slide 13: Machining Economics
Cont. Minimizing Machining Cost per Piece
Again we seek to determine optimum () and ()
Now we find and for max. prodon, i.e. min.
We differentiate with respect to and set it to zero,


## Slide 14: Machining Economics
Cont. Minimizing per Piece
Qualitative plot of /piece
  Note, also depends on req. surface finish: better S.F.  higher
  Note,
Qualitative plot of /piece (i.e. production rate)
  Note,
  Range bet. Two ’s is: “high-efficiency machining range”

## Slide 15: Machining Economics
Cont. Minimizing Machining Cost per Piece
Final notes
  Important to have accurate data, since small changes in greatly affect and (see last slide)
  Previous analysis can be done for all manufacturing processes:
    E.g. Cost/part in sand casting uses
    E.g. Cost/part in powder metallurgy, etc.