## Slide 1: VII- Flow Manufacturing Systems نظام التصنيع المستمر
<number>
1- Flow System Technology تقنية النظام المستمر
IE 469 Manufacturing Systems
469 صنع نظم التصنيع
Notes: Manufacturing systems - Flow line - Technology
July 31, 2026
<number>

## Slide 2: 1a- definition تعريف: نظام التصنيع الكبير
<number>
It is a line of connected number of specialized machines/workstation by suitable handling system based on a sequence of operations to produce a product.
هو خط إنتاج مكون من عدد من الماكينات او محطات العمل المتخصصة لأسلوب صناعي (تجميع- تحويل- فحص- تعبئة- فصل--) , وترتبط مع بعضها بمعدات مناولة مناسبة بناءا على تتابع العمليات لإنتاج منتج .
1
4
2
3
5
6
Finished
Part
Raw
Matl.
A- Flow system without Buffer
Buffer
1
4
2
3
5
6
Finished
Part
Raw
Matl.
B- Flow system with Buffer

## Slide 3: 1b- definition تعريف: نظام التصنيع الكبير
<number>
  The line is used for the following cases: يستخدم خط الإنتاج المستمر في حالة
  High demand طلب عالي للمنتج
  Stable product design تصميم مستقر للمنتج
  Long product life cycle دورة عمر طويلة للمنتج
  Several sequenced operation تعدد العمليات للإنتاج
The line achieve the following ويحقق الخط التالي
  Low labour cost خفض في تكلفة العمالة
  Low product cost خفض في تكلفة المنتج
  Reduce WIP خفض التخزين بين العمليات
  High production rate معدلات إنتاج عالية
  Specialized & standardized operations التخصص والقياس للعمليات الصناعية
  Integrated operations التكامل بين العمليات
  Factory layout Area reduction خفض في مساحات المصنع

## Slide 4: 2a- flow line types أنواع نظام خطوط أساليب التصنيع الكبير
<number>
نظام بخط In-Line Type
1
4
2
3
5
6
Finished
Part
Raw
Matl.
Preferable for Larger work-pieces
Larger number of work stations
Buffer Storage to smooth out irregularities

## Slide 5: 2b- flow line types أنواع نظام خطوط أساليب التصنيع الكبير
<number>
نظام دائري Rotary Type
Finished
Part
Raw
Matl.
4
2
3
5
6
1
Limited to smaller work- pieces
Limited to fewer stations
Do not lend to provide buffer storage
Low cost equipment
Less Factory space floor

## Slide 6: 2c- flow line types أنواع نظام خطوط أساليب التصنيع الكبير
<number>

## Slide 7: 2d- flow line types أنواع نظام خطوط أساليب التصنيع الكبير
<number>

## Slide 8: 2e- flow line types أنواع نظام خطوط أساليب التصنيع الكبير
<number>

## Slide 9: 2f- flow line types أنواع نظام خطوط أساليب التصنيع الكبير
<number>

## Slide 10: 3a- Work-part Transport methods طرق انتقال المشغولة بين المحطات
<number>
Factors affecting selection of transfer method
العوامل المؤثرة في اختيار طريقة الانتقال
The types of operation
The number of stations
The weight and size of the work-parts
including manual stations
Production rate requirement
Balancing the various process time

## Slide 11: 3b- Work-part Transport methods طرق انتقال المشغولة بين المحطات
<number>
1- Continuous Transfer الانتقال المستمرة
Work-piece moves continuously. This Requires continuous Work head move; (Beverage bottling Operation-Manual assembly). But not always possible
2- Intermittent/Synchronous Transfer الانتقال المتقطعة/المتزامنة
Discontinuous transport motion of Work-piece.
Work stations are fixed and work piece moves to proper locations at work head for processing.
All parts are moved and processed at same time in synchronous motion.

## Slide 12: 3c- Work-part Transport methods طرق انتقال المشغولة بين المحطات
<number>
3- Asynchronous Transfer الانتقال الغير المتزامنة
Work-piece moves independently after processing at current station to next station. Some parts are being moved and other parts are being processed at same time.
Greater flexibility is offered for processing time variation and line balance, by allowing In-process storage and parallel stations in the line. But the cycle time is increased.

## Slide 13: 3d- Work-part Transport methods طرق انتقال المشغولة بين المحطات
<number>
4- Pallet Fixture منصات تحميل المشغولات
Work-piece is attached to pallet fixture to carry work-piece through sequence of operations. It transfer the work-piece and helps Positioning and locating at the machine.

## Slide 14: 4a- Transfer Mechanisms آليات الانتقال
<number>
2- conveyer System
1- Linear Transfer Mechanisms آليات الانتقال الخطي
1- Walking Beam

## Slide 15: 4b- Transfer Mechanisms آليات الانتقال
<number>
معادلة آلية الانتقال الخطي Walking Beam Geometry
hs = Lifting Height
ds = Distance between work-stations
b = Walking beam size (10 hs)
Smin = Minimum piston stroke
Smax = Maximum piston stroke

## Slide 16: 4c- Transfer Mechanisms آليات الانتقال
<number>
2- Mechanisms Rotary Transfer آليات الانتقال الدائري
1-Rack and Pinion
2-Ratchet and Pawl
3-Geneva
4- Cam

## Slide 17: 4d- Transfer Mechanisms آليات الانتقال
<number>
wi
wd
rd
Driver
Driven wheel
Pin to index driven wheel
Qi
معادلة آلية جينيفا Mechanisms Geneva

## Slide 18: 4e- Transfer Mechanisms آليات الانتقال
<number>
Qi
wi
Qd
wd
ri
rd
qi
qd
معادلة آلية جينيفا Mechanisms Geneva

## Slide 19: 4f- Transfer Mechanisms آليات الانتقال
<number>
Qd
wd
Qi
wi
ri
rd
qi
qd
معادلة آلية جينيفا Mechanisms Geneva

## Slide 20: 4g- Transfer Mechanisms آليات الانتقال
<number>
rd
ri
Qi/2
Qd/2
C
d
a
معادلة آلية جينيفا Mechanisms Geneva

## Slide 21: 4h- Transfer Mechanisms آليات الانتقال
<number>
Find motor speed, if a rotary system requires three work-station with cycle time of 0.5 min. Assume, the indexer wheel diameter equal to 12 in.
Indexing angle,
Distance between drive and index centers,
Drive diameter,
Since the non-drive must correspond to cycle time, the rotation of drive motor can be:
Drive angle,
In this case, the drive motor rotate every 36 sec. For constant speed motor the ratio of time spend in processing to time spent indexing = 300:60.
Example for Geneva mechanism مثال لمعادلة آلية جينيفا

## Slide 22: 5-1a- Assembly system أنواع نظام خطوط التجميع
<number>
Assembly line resemble the process line and the difference lie in the nature of work activity as follow.
Assembly station is designed according Line Balancing to carry assembly process (s) such that:
  parts are fed to each station by feeder mechanisms
  A base part is fixed on pallet and transported through the stations to carry assembly operation of parts.
نظام بخط In-Line Type
1
4
2
3
5
6
Base
Part
Finish
Prod.
تتماثل أنواع محطات خط التجميع والانتقال بينها مع خطوط أساليب التصنيع , والاختلاف بينها يكمن في طبيعة العمل
وتصمم كل محطة تجميع للقيام بمهمة أو مهام لأساليب تجميعية باتزان الخطوط حيث الأجزاء تقدم للمحطة لعملية التجميع بحيث:
  تستقبل المحطة الأجزاء إلى المحطة بواسطة آليات تقديم لإتمام عمليات التجميع
  تثبت قاعدة أساسية على منصة تحميل تتحرك بين المحطات ليتم عليه التجميع

## Slide 23: 5-1b- Assembly system أنواع نظام خطوط التجميع
<number>
Labor intensive conveyer assembly
Robot assisted assembly

## Slide 24: 5-1c- Assembly system أنواع نظام خطوط التجميع
<number>
Gillette safety razor
(A) Half cap sub-assembly
(B) Final assembly
Sequence of Half cap sub-assembly
Load
Feed
Snap
Unload
Feed
Snap

## Slide 25: 5-1d- Assembly system أنواع نظام خطوط التجميع
<number>
نظام دائري Dial Type
2
3
1
Base
Part
Finish
Prod.
4
نظام دائري Carousel Type
4
2
3
1
6
5
1
نظام محطة تجميع واحدة Single station assembly
Base
Part
Finish
Prod.

## Slide 26: 5-2a – work transfer system أنظمة الانتقال بين المحطات
<number>
System configuration | Stationary base part | Work transfer system |  | 
 |  | Continuous | Synchronous | Asynchronous
Dial | No | Yes | Yes | No
In-line | No | Yes | Yes | Yes
Carousel | No | Yes | Yes | Yes
Single-station | Yes | No | No | No

## Slide 27: 5-3a- Part feeder to base part انتقال القطع لقاعدة التجميع
<number>
1
2
3
4

## Slide 28: 5-3b- Part feeder to base part انتقال القطع لقاعدة التجميع
<number>
1- Hopper: Bulk container for a type of component and initially oriented.
1a- Part feeder: A mechanism that removes the parts from the hopper one a time for delivery.
Vibratory Bowl Feeder
Center-board Bowl Feeder

## Slide 29: 5-3c- Part feeder to base part انتقال القطع لقاعدة التجميع
<number>
2- Selector and Orientor: They establish the proper orientation of the component.
Use of light source for part orientation
(a) Selector
(b) Orientor

## Slide 30: 5-3d- Part feeder to base part انتقال القطع لقاعدة التجميع
<number>
Placement onto index Table
3- Feeder track: It transfers the component from the Hopper and selector to the escapement and location on work-station head. Two types are used: gravity and powered.
4- Escapement and placement device: It removes a component from the track at time intervals that are consistent with the cycle time of the assembly head.
Escapement of riveted shaped parts
Pick And Place Mechanism
(a)
(b)

## Slide 31: 5-3e- Part feeder to base part انتقال القطع لقاعدة التجميع
<number>
O
1-
O
Feed rate f
Stop Sensor
Start Sensor
Lf2
Lf1
RC
Cycle Rate
LC
O
Delivery Rate
f

## Slide 32: 5-3e- Part feeder to base part انتقال القطع لقاعدة التجميع
<number>
Solution:
The time taken for the supply parts to from nf2 to nf1 = (nf2 - nf2)/RC =(18-6) x 0.2 = 2.4 min
O
The time taken for the supply parts to from nf1 to nf2 = (nf2 - nf2)/(f -RC ) =(18-6)/(20 x 0.3 – 5)=12 min.
Given:
Cycle time; TC = 0.2 min,
Feed rate: f = 20 components/min,
Passing part to feed track: = 0.3,
Number of parts in feed track at low level nf1=6,
Number of parts in feed track at high level nf2=18.
O
Determine:
a) What is the time it will be taken for the supply parts to from nf2 to nf1
b) What is the time it will be taken for the supply parts to from nf1 to nf2