## Slide 1: Boolean Algebra and Digital Logic

## Slide 2: Combinational Circuits – Basic concepts
Combinational Circuits
Combinational logic is used to build circuits that contain basic Boolean operators, inputs, and outputs.
The output of a combinational circuit is a function of its inputs at any given moment.
Combinational logic has no memory.
A combinational circuit may have several outputs. If so, each output represents a different Boolean function.

## Slide 3: Combinational Circuits – Basic concepts
Combinational Circuits
Combinational logic is used to build circuits that contain basic Boolean operators, inputs, and outputs.
The output of a combinational circuit is a function of its inputs at any given moment.
Combinational logic has no memory.
A combinational circuit may have several outputs. If so, each output represents a different Boolean function.

## Slide 4: Typical Combinational Circuits – A Half Adder (1/2)
Combinational Circuits
A half-adder is a simple combinational circuit.
Consider the problem of adding two binary digits together, three cases are possible:
  0 + 0 = 0
  1 + 0 = 0 + 1 = 1
  1 + 1 = 1 0 (the result is “0” with a carry of “1”)
We have two inputs (the bits to add) and two outputs (the “sum” and the “carry”).
Drawing the truth table leads us to the Boolean function of a half-adder.
  Note that each output has a Boolean function.

## Slide 5: Typical Combinational Circuits – A Half Adder (2/2)
Combinational Circuits
The sum is “1” when only one of the inputs (x, y) is equal to “1”
  This is the job of an XOR
  Sum =
The carry is “1” when only both inputs (x and y) are “1”
  This is the job of an AND
  Carry = xy

## Slide 6: Typical Combinational Circuits – A Full Adder (1/2)
Combinational Circuits
A half adder could be extended to a circuit that allows the addition of larger binary numbers: Full adder
Remember how we added binary numbers?
  We add each column without forgetting the carry from the nearest right column
A full adder has three inputs:
  The two bits to add (x and y)
  The carry from the nearest right column (carry-in)
A full adder has two outputs (the “sum” and the “carry”)

## Slide 7: Typical Combinational Circuits – A Full Adder (2/2)
Combinational Circuits
Think of how this logic diagram is obtained.
Note that a full-adder is composed of two half-adders and an OR gate.

## Slide 8: Typical Combinational Circuits – A Decoder (1/3)
Combinational Circuits
A decoder decodes binary information of a set of n inputs to a maximum of 2n outputs.
A decoder uses the inputs and their respective values to select one specific output line
  For a given input combination, only one output is set to “1” and all others are set to “0”

## Slide 9: Typical Combinational Circuits – A Decoder (2/3)
Combinational Circuits

## Slide 10: Typical Combinational Circuits – A Decoder (3/3)
Combinational Circuits
Memory Chip 4
Memory Chip 5
Memory Chip 6
Memory Chip 7
Memory Chip 0
Memory Chip 1
Memory Chip 2
Memory Chip 3
Decoder
0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1
13
0
1
2
3
4
5
6
7
CS
CS
CS
CS
CS
CS
CS
CS
0
0
1
0
0
0
0
0
0
0
1
Notes: For tutors only:
  We have 16 bits for address: The memory size is 216 = 64 Kwords = 64 Kbytes (supposing a word size of 1byte)
  Each memory chip has a size of : 64Kbytes/8 = 8Kbytes
  All memory 1 addresses begin with: 000xxxxxxxxxxxxx
  All memory 2 Addresses begin with: 001xxxxxxxxxxxxx
  All memory 3 Addresses begin with: 011xxxxxxxxxxxxx
  And so on until memory 7, its addresses begin with: 111xxxxxxxxxxxxx

## Slide 11: Decoder Examples
1-to-2-Line Decoder
2-to-4-Line Decoder
Note that the 2-4-line made up of 2 1-to-2- line decoders and 4 AND gates.

## Slide 12: Decoder Expansion - Example 1
3-to-8-line decoder
  Number of output ANDs = 8
  Number of inputs to decoders driving output ANDs = 3
  Closest possible split to equal
    2-to-4-line decoder
    1-to-2-line decoder
  2-to-4-line decoder
    Number of output ANDs = 4
    Number of inputs to decoders driving output ANDs = 2
    Closest possible split to equal
      Two 1-to-2-line decoders
See next slide for result

## Slide 13: Decoder Expansion - Example 1
Result

## Slide 14: Decoder Expansion - Example 2
7-to-128-line decoder
  Number of output ANDs = 128
  Number of inputs to decoders driving output ANDs = 7
  Closest possible split to equal
    4-to-16-line decoder
    3-to-8-line decoder
  4-to-16-line decoder
    Number of output ANDs = 16
    Number of inputs to decoders driving output ANDs = 2
    Closest possible split to equal
      2 2-to-4-line decoders
  Complete using known 3-8 and 2-to-4 line decoders

## Slide 15: Decoder with Enable
In general, attach m-enabling circuits to the outputs
See truth table below for function
  Note use of X’s to denote both 0 and 1
  Combination containing two X’s represent four binary combinations
Alternatively, can be viewed as distributing value of signal EN to 1 of 4 outputs
In this case, called a demultiplexer

## Slide 16: Encoding
Encoding - the opposite of decoding - the conversion of an m-bit input code to a n-bit output code with n £ m £ 2n such that each valid code word produces a unique output code
Circuits that perform encoding are called encoders
An encoder has 2n (or fewer) input lines and n output lines which generate the binary code corresponding to the input values
Typically, an encoder converts a code containing exactly one bit that is 1 to a binary code corres-ponding to the position in which the 1 appears.

## Slide 17: Encoder Example
A decimal-to-BCD encoder
  Inputs: 10 bits corresponding to decimal digits 0 through 9, (D0, …, D9)
  Outputs: 4 bits with BCD codes
  Function: If input bit Di is a 1, then the output (A3, A2, A1, A0) is the BCD code for i,
The truth table could be formed, but alternatively, the equations for each of the four outputs can be obtained directly.

## Slide 18: Encoder Example (continued)
Input Di is a term in equation Aj if bit Aj is 1 in the binary value for i.
Equations:
  A3 = D8 + D9
  A2 = D4 + D5 + D6 + D7
  A1 = D2 + D3 + D6 + D7
  A0 = D1 + D3 + D5 + D7 + D9
F1 = D6 + D7 can be extracted from A2 and A1 Is there any cost saving?
Notes: No. The total gate input cost remains the same.