## Slide 1: Direct Time Study
Sections:
Direct Time Study Procedure
Number of Work Cycles to be Timed
Performance Rating
Time Study Equipment

## Slide 2: Direct Time Study - Defined
Direct and continuous observation of a task using a stopwatch or other timekeeping device to record the time taken to accomplish the task
While observing and recording the time, an appraisal of the worker’s performance level is made to obtain the normal time for the task
The data are then used to compute a standard time for the task

## Slide 3: Direct Time Study Procedure
Define and document the standard method
Divide the task into work elements
Time the work elements to obtain the observed time Tobs
Evaluate worker’s pace relative to standard performance to obtain normal time Tn
  Called performance rating (PR)
Tn = Tobs(PR)
Apply allowance factor to compute standard time
Tstd = Tn(1 + Apfd)

## Slide 4: Document the Standard Method
Determine the “one best method”
  Seek worker’s advice if possible
Documentation should include:
  All of the steps in the method
  Special tools, gauges, equipment and equipment settings (e.g., feeds and speeds) if applicable
  Irregular elements and their frequency
Once the standard method is defined, it should not be possible for the operator to make further improvements

## Slide 5: 13.1
Form to document the standard method

## Slide 6: Why Documentation is Important
Batch production – repeat orders after a significant time lapse
Methods improvements by operator – to restudy task, must be able to prove a change has occurred
Disputes about method – operator complains that standard is too tight
  Is operator using the standard method?
Data for standard data system – good documentation is essential for developing a standard data system

## Slide 7: Divide Task into Work Elements
Guidelines:
Each work element should consist of a logical group of motion elements
Beginning point of one element should be the end point of the preceding element
Each element should have a readily identifiable end point
Work elements should not be too long nor too short
Separate irregular elements, machine elements, internal elements

## Slide 8: Time the Work Elements
Each element should be timed over several work cycles to obtain a reliable average
Stopwatch timing methods:
  Snapback timing method – stopwatch is reset to zero at the start of each work element
  Continuous timing method – stopwatch is allowed to run continuously throughout the duration of the work cycle

## Slide 9: Advantages of Each Timing Method
Advantages of snapback method:
  Analyst can readily see how element times vary from cycle to cycle
  No subtraction necessary to obtain individual element times
Advantages of continuous method:
  Elements cannot be omitted by mistake
  Regular and irregular elements can be more readily distinguished
  Manipulation and resetting of the stopwatch is reduced

## Slide 10: Performance Rating
Analyst judges the performance or pace of the worker relative to the definition of standard performance used by the organization
Standard performance PR = 100%
  Slower pace than standard PR < 100%
  Faster pace than standard PR > 100%
Normal time Tn = Tobs(PR)

## Slide 11: 13.2
Direct time study form

## Slide 12: Apply Allowances
A PFD allowance is added to the normal time to compute the standard time
Tstd = Tn(1 + Apfd)
where Apfd = allowance factor for personal time, fatigue, and delays
The function of the allowance factor is to inflate the value of standard time in order to account for the various reasons why the worker loses time during the shift

## Slide 13: Example
A direct time study was taken on a manual work element using the snapback method. The regular cycle consisted of three elements, a, b, and c. Element d is an irregular element performed every five cycles.
Work element a b c d
Observed time (min) 0.56 0.25 0.50 1.10
Performance rating 100% 80% 110% 100%
Determine (a) normal time and (b) standard time for the cycle

## Slide 14: Solution
(a) Normal time:
Tn = 0.56(1.00) + 0.25(0.80) + 0.50(1.0)
+ 1.10(1.0)/5 = 1.53 min
(b) Standard time:
Tstd = 1.53(1 + 0.15) = 1.76 min

## Slide 15: Machine Cycle in the Task
If the work cycle includes machine-paced elements, then standard time may include a machine allowance applied to the machine time
Tstd = Tnw(1 + Apfd) + Tm(1 + Am)
where Tnw = normal time for worker (external) elements, Tm = machine cycle time (assumed constant), and Am = machine allowance

## Slide 16: Cycle-to-Cycle Time Variations
Result from the following:
Variations in hand and body motions
Variation in the placement of parts and tools
Variations in the quality of the starting work units
Operator mistakes
Variations in worker pace
Timing errors by analyst

## Slide 17: Number of Cycles to be Timed
After several cycles, calculate sample standard deviation s
s =
Using the Student t distribution,
n =

## Slide 18: Performance Rating
Analyst observes and rates the worker’s performance relative to the definition of standard performance
The most difficult and controversial step in direct time study
  Potential conflict of interest between the worker and the analyst
Most common performance rating method is based on speed or pace

## Slide 19: Traits of a Good Rating System
Consistency among tasks
  A worker who can perform at 125% on one task should be able to do the same on other tasks
Consistency among analysts
Easy to explain and easy to understand
Based on a well-defined concept of standard performance
Rate performance during the observation
Worker notification

## Slide 20: Time Study Equipment
Stopwatch
  Mechanical stopwatches
  Electronic stopwatches
Video cameras
  Provides visual and audio record of method used by worker
Computerized techniques in direct time study
  Use of PCs and PDAs

## Slide 21: Mechanical Stopwatch
Calibrated in decimal minutes

## Slide 22: Electronic Stopwatch
LED read-out