## Slide 1: 5.8 Disinfection
Objective
In this lesson we will answer the following questions:
What disinfection requirements must be met in treating drinking water?
How does chlorination fit into the water treatment process?
What other methods can be used to disinfect water?

## Slide 2
Before water treatment became common, waterborne diseases could spread quickly through a population, killing or harming hundreds of people. The table below shows some common, water-transmitted diseases as well as the organisms (pathogens) which cause each disease

## Slide 3: Type of disinfection

## Slide 4
Chlorination Chemistry
When chlorine is added to water, a variety of chemical processes take place. The chlorine reacts with compounds in the water and with the water itself. Some of the results of these reactions (known as the chlorine residual) are able to kill microorganisms in the water.

## Slide 5
Chlorine Demand
When chlorine enters water, it immediately begins to react with compounds found in the water. The chlorine will react with organic compounds and form trihalomethanes. It will also react with reducing agents such as hydrogen sulfide, ferrous ions, manganous ions, and nitrite ions.

## Slide 6
In the first reaction, hydrogen sulfide reacts with chlorine and oxygen to create elemental sulfur, water, and chloride ions. The elemental sulfur precipitates out of the water and can cause odor problems.

## Slide 7
In the second reaction, hydrogen sulfide reactions with chlorine and water to create sulfuric acid and hydrochloric acid.

## Slide 8
Each of these reactions uses up the chlorine in the water, producing chloride ions or hydrochloric acid which have no disinfecting properties.
The total amount of chlorine which is used up in reactions with compounds in the water is known as the chlorine demand.
A sufficient quantity of chlorine must be added to the water so that, after the chlorine demand is met, there is still some chlorine left to kill microorganisms in the water

## Slide 9
Reactions of Chlorine Gas With Water
At the same time that chlorine is being used up by compounds in the water, some of the chlorine reacts with the water itself. The reaction depends on what type of chlorine is added to the water as well as on the the pH of the water itself.

## Slide 10
The chlorine reacts with water and breaks down into hypochlorous acid and hydrochloric acid.

## Slide 11
Hypochlorous acid may further brea Hypochlorous acid is the most effective form of free chlorine residual, meaning that it is chlorine available to kill microorganisms in the water.
Hypochlorite ions are much less efficient disinfectants.
k down, depending on pH.

## Slide 13: Breakpoint Chlorination

## Slide 14
between points 1 and 2
the water reacts with reducing compounds in the water, such as hydrogen sulfide. These compounds use up the chlorine, producing no chlorine residual.
between points 2 and 3
the chlorine reacts with organics and ammonia naturally found in the water. Some combined chlorine residual is formed - chloramines. Note that if chloramines were to be used as the disinfecting agent, more ammonia would be added to the water to react with the chlorine. The process would be stopped at point 3. Using chloramine as the disinfecting agent results in little trihalomethane production but causes taste and odor problems since chloramines typically give a "swimming pool" odor to water.

## Slide 15
Between points 3 and 4
the chlorine will break down most of the chloramines in the water, actually lowering the chlorine residual.
Finally, the water reaches the breakpoint, shown at point 4. The breakpoint is the point at which the chlorine demand has been totally satisfied - the chlorine has reacted with all reducing agents, organics, and ammonia in the water. When more chlorine is added past the breakpoint, the chlorine reacts with water and forms hypochlorous acid in direct proportion to the amount of chlorine added. This process, known as breakpoint chlorination, is the most common form of chlorination, in which enough chlorine is added to the water to bring it past the breakpoint and to create some free chlorine residual.

## Slide 16
Example:
For disinfecting water supply, it is required to treat 500,000 litres of daily supply with 0.5 ppm of chlorine. If the disinfectant is available in the form of bleaching powder containing 30% of available chlorine, calculate the amount of bleaching powder required to treat the daily flow of water.

## Slide 17
Solution:
0.5 ppm = 0.5 mg/L
Dosage of chlorine = 500,000 L x 0.5 mg/L x 1 kg/106 mg = 0.25 kg
For the bleaching powder with available chlorine of 30%, amount of bleaching power required = 0.25 kg x 100/30 = 0.833 kg