## Slide 1: King Saud University College of Engineering IE – 341: “Human Factors Engineering” Fall – 2017 (1st Sem. 1438-9H)
Visual Displays of Dynamic Information
(Chapter 5) – part 1: Quantitative Visual Displays
Prepared by: Ahmed M. El-Sherbeeny, PhD

## Slide 2: Lesson Overview
Uses of Dynamic Information
Quantitative Visual Displays (part 1)
Qualitative Visual Displays (part 2)

## Slide 3: Uses of Dynamic Information
Dynamic information: i.e. changing info; e.g:
  Natural phenomena (e.g. temperature, pressure)
  Vehicle speed
  Traffic lights
  Frequency, intensity of sounds, etc.
Dynamic displays:
  Displays used to display dynamic information
  Types of dynamic displays, type of info. presented:
    Quantitative: precise numeric value of some variable (e.g. “pressure is 125 psi”)
    Qualitative: approximate value/rate of change/change in direction (e.g. “pressure is increasing”)
    Status/check: determines if readings are normal (e.g. “pressure is normal”)
    Representational: situation awareness; e.g. radar display predicts where plane will be in 5 or 10 minutes

## Slide 4
Quantitative Visual Displays

## Slide 5: Quantitative Visual Displays
Types of variables in QVD’s:
  Changing/dynamic variables (e.g. temp., pressure)
  Static variables (rare): length, weight of objects
Basic Design of Quantitative Displays
  Mechanical displays (see next slide)
    Fixed scale with moving pointer (analog): a-e
    Moving scale with fixed pointer (analog): f-i
    Digital display: j
  Electronic displays (see slide 6)
    Analog scales: k,l
    Digital scale: m

## Slide 6: Mechanical Displays
Analog Displays
2. Digital Display

## Slide 7: Electronic Displays
Analog Displays
2. Digital Display

## Slide 8: Cont. Quantitative Visual Displays
Comparison of Different Designs (Studies)
Digital displays preferred vs. analog when:
  a precise numeric (quantitative) value is required
  values shown remain visible long enough to be read (i.e. not continuously changing)
Analog displays preferred vs. digital when:
  fixed-scale moving-pointer displays: useful when the values change frequently/continuously ⇒ limited time in reading values if digital displays were used
  when important to know direction or rate of value change (qualitative reading)

## Slide 9: Cont. Quantitative Visual Displays
Cont. Comparison of Different Designs
Fixed scale w/ moving pointer vs. moving scale w/ fixed pointer
  Generally: fixed scale is preferred vs. moving scale
  If numerical increase is related to another natural interpretation (e.g. more or less, up and down):
    easier to interpret straight line (horizontal or vertical scales) or thermometer scale with a moving pointer
    pointer position relative to zero/null adds value
  Don’t mix different types of pointer-scale indicators when used for related functions
    this avoids reversal errors in reading
  Direction of motion of moving element is clearer if manual control moves pointer (rather than scale)
  For slight variable movements/changes in quantity ⇒ more clear if a moving pointer is used

## Slide 10: Cont. Quantitative Visual Displays
Cont. Comparison of Different Designs
Moving scale w/ fixed pointer vs. fixed scale w/ moving pointer
  Moving scale preferred (due to small panel space) when range of values: too great to show on small scale; e.g.:
    moving rectangular open-window scales
    moving horizontal and vertical scales
  Also when a numerical value is needed to be readily available, a moving scale appearing in an open window can be read more quickly (which ?)
Circular/Semicirc. scales vs. vertical/horizontal
  Circular/Semicirc. Scales generally preferred (a,b,c)
  Vertical/horizontal preferred (d,e) when relating to null or viewing more/less, up/down (see slide 8)

## Slide 11: Cont. Quantitative Visual Displays:
Basic Features of Quantitative Displays
Scale range:
  Numerical difference bet. highest & lowest values on scale
Numbered interval:
  Numerical difference bet. adjacent #’s on scale
Graduation interval:
  Numerical difference bet. smallest scale markers
Scale unit
  Smallest unit to which scale is to be read (note, not necessarily = graduation interval)

## Slide 12: Cont. Quantitative Visual Displays
Specific Features of Conventional Quant. Displays
Ability of people to make visual discriminations in QVD’s is influenced by the following specific features:
  Numeric Progressions of Scales
  Length of Scale Unit
  Design of Scale Markers
  Scale Markers and Interpolation
  Design of Pointers
  Combining Scale Features
  Scale Size and Viewing Distance
Note, above features discussed here for mechanical scales, yet much of this applies also to electronic displays

## Slide 13: Cont. Quantitative Visual Displays
Specific Features of Conventional Quant. Displays
  Numeric Progressions of Scales
Every quantitative scale has numeric progression system, including
  Graduation interval: bet. adjacent markers
  Numbered interval: major scale markers
Number progressions:
  Progression by 1s (0,1,2,3,…) is easiest to use (see figure on next slide):
    Major markers: 0,10,20,30,….,
    with intermediate markers: 5,15,25,35,….,
    with minor markers at individual numbers
  Progression by 5 is also satisfactory
  Progression by 25 is moderate.
Decimals make scales more difficult to use:
  If used, zero before decimal should be omitted
Unusual progressions (3s, 8s etc): avoid

## Slide 15: Cont. Quantitative Visual Displays
Specific Features of Conventional Quant. Displays
  Length of Scale Unit
Defn: length on scale representing smallest numeric value to which the scale is to be read
  e.g. force is to be measured to nearest 10 Newtons,
  On scale: 10 N is to correspond to 1.3 mm
  ⇒ length of scale unit = 1.3 mm
length of scale unit should allow distinctions between values with optimum reliability in terms of human sensory & perceptual skills:
  research suggests values between: 1.3 - 1.8 mm
  Larger values are needed when instruments are used in non-ideal conditions
    e.g. low vision, poor illumination, limited time, etc

## Slide 16: Cont. Quantitative Visual Displays
Specific Features of Conventional Quant. Displays
  Cont. Length of Scale Unit
recom. format for quantitative scale given length of scale unit (?), graduation markers

## Slide 17: Cont. Quantitative Visual Displays
Specific Features of Conventional Quant. Displays
  Design of Scale Markers
recommended to include a scale marker for each scale unit to be read
Conventional progression scheme (last slide), based on:
  Major markers: 1, 10, 100, etc.
  minor markers: 0.1, 1, 10, etc. (example?)
  Scale Markers and Interpolation
If scales: much compressed (>last slide) ⇒ scale markers: crowded ⇒ reading accuracy ↓
  Such case: use a scale requiring interpolation
  Interpolation: estimation of values between markers
For high accuracy reading of scale:
  marker should be placed at every scale unit
  Requires: a larger scale or a closer viewing distance

## Slide 18: Cont. Quantitative Visual Displays
Specific Features of Conventional Quant. Displays
  Design of Pointers
Recommendations for pointer design:
  pointed pointers (tip angle of about 20°)
  have the pointer tip meet, but not overlap, the smallest scale markers
  have the color of the pointer extend from the tip to the center of the scale
  have the pointer close to the surface of the scale to avoid parallax (see below)

## Slide 19: Cont. Quantitative Visual Displays
Specific Features of Conventional Quant. Displays
  Combining Scale Features
mentioned features of quantitative scales: are integrated into relatively standard formats
  e.g. slide 14: used for circular, semi-circular scales
Note, above features: only general (non-rigid) guidelines
e.g.’s of poor scale designs:
  Ampere scale:
    Shortness of scale units
    Inadequate inter- mediate markers
  Kilowatt scale (left):
    Name 5 corrections?

## Slide 20: Cont. Quantitative Visual Displays
Specific Features of Conventional Quant. Displays
  Scale Size and Viewing Distance
previous guidelines: for normal viewing distance: 28 in. (71cm)
If display viewed from farther distances ⇒
  features have to be enlarged to maintain the same visual angle (VA) at the eye
To maintain same VA for any viewing distance x: use this formula to find proper dimension :
  Dimension at x [in] = Dimension @ 28 in * (x [in] / 28)
  Example: find @ 100 cm from scale (viewed in normal viewing conditions):
    Minimum length of scale unit
    VA
    Minimum Snellen acuity required to read scale

## Slide 21: References
  Human Factors in Engineering and Design. Mark S. Sanders, Ernest J. McCormick. 7th Ed. McGraw: New York, 1993. ISBN: 0-07-112826-3.