## Slide 1: Digital imaging
By : Alanoud Al Saleh

## Slide 2: History:
It started in 1960 by the National Aeronautics and Space Administration (NASA).
The technology of digital processing continues to expand rapidly and its application extends into fields such as astronomy, geology, forestry, agriculture, military science and medicine.

## Slide 3: In medicine
In medicine the technology has found widespread in particularly in diagnostic imaging: ultrasound, digital radiography, nuclear medicine, CT and magnetic resonance imaging.
Digital image processing is a multidisciplinary subject that includes physics, mathematics, engineering and computer science.

## Slide 4: Image types: 1. Analog images
They are continuous image.
In photography: images are formed when light is focused on film.
In radiography: X-ray pass through the patient and projected onto x-ray film.
In both cases, films are processed in chemical solutions to make them visible and the images are formed by a photochemical process.

## Slide 5: 2. Digital images:
They are numeric representations or images of objects which require a computer to be formed.
The information enters the computer is converted into a digital form or numbers using the analog-to-digital converter.

## Slide 6: Definitions:
Image processing: necessary to convert an input image to an output image.
Analog processing: Both the input and output images are analog
Digital processing: Both the input and output images are discrete.

## Slide 7: Processing:
A series of actions or operations leading to a desired result, thus, a series of actions or operations are performed upon an object to alter its form in a desired manner.
Therefore digital processing can be defined as:
A subject numerical representation of objects to a series of operations in order to obtain a desired result.

## Slide 8: Image digitization:
It is to convert an analog image into numeric data for processing by the computer.
It consists of three distinct steps:
Scanning
Sampling
quantization

## Slide 9: Scanning:
It is the division of the picture into small regions. Each small region of the picture is a picture element or Pixel
This will result in a grid characterized by rows and columns.
The size of the grid usually depends on the number of pixel on each side of the grid.

## Slide 10: Image grid

## Slide 11: Scanning:
Example: a 9X9 grid results in 81 pixels
The rows and columns comprise a matrix in our the matrix is 9X9.
As the number of pixel in the image matrix increases, the image become more recognizable and facilitates better perception of image details.

## Slide 12: Sampling:
The measurement of the brightness of each pixel in the entire image.
A small spot of light is projected onto the transparency and the transmitted light is detected by a photomultiplier tube positioned behind the picture. The output of the photomultiplier tube is an electrical (analog) signal.

## Slide 13: Quantization:
The brightness value of each sampled pixel is assigned an integer (0, or a positive or negative number) called a grey level.
The result is a range of numbers or grey levels each of which has a precise location on the rectangular grid of pixels.

## Slide 14: Quantization:
The total number of grey levels is called the grey scale, which is composed of any number of grey levels.
The result is an array of numbers representing the analog image that was scanned, sampled and quantized.
The array of numbers is then sent to the computer for further processing.

## Slide 15: Analog-to-digital conversion:
The ADC samples the analog signal at various times to measure its strength at different points. The more points sampled, the better the representation of the signal. The quantization is followed.
The two most important characteristics of the ADC are speed and accuracy

## Slide 16: ADC
Accuracy:
Refers to the sampling of the signal.
The more samples taken, the more accurate the representation of the digital image. If not enough samples are taken, the representation of the original signal will be inaccurate after computer processing.
This is referred to as aliasing which is a type of artefact on the image.

## Slide 17: Accuracy
It also determines the number of levels or shades of grey represented in the image. A 1-bit ADC result in two integers (0 and 1), which are represented as black and white.
A 2-bit ADC results in four numbers producing a 4 shade grey scale.
An8-bit ADC results in 256 integers ranging from 0 to 255 with 256 shades.

## Slide 18: Image with different gray shades

## Slide 19: Speed
The time taken to digitize the analog signal.
Speed and accuracy are inversely related, that is the greater the accuracy the longer it takes to digitize the signal.

## Slide 20: Why digitize images?
The major goal is that digital images can be processed by a computer resulting in the following advantages:
Image enhancement: The image can be made to look moor pleasing to the observer by improving the overall quality of the image.

## Slide 21: Why digitize images?
Image restoration: Poor images can be filtered to remove unwanted “noise” and also unnecessary fine detail in the image-a technique known as smoothing.
Image analysis
Image detection: Allows the observer to look for specific shapes, contours, or textures while disregarding the other features in the image.

## Slide 22: Digital image
Image analysis
Image restoration

## Slide 23: Why digitize images?
Pattern recognition: The computer can see structures and identify patterns.
Geometric transformation: Image can be rotated or scaled by changing the position of the pixel.
Data compression: The compression of digital images reduces the amount of data that comprise the image, which is important in data storage and transmission.

## Slide 24
Pattern recognition
Geometric transformation

## Slide 25
Thank
you