## Slide 1: Work Sampling
Sections:
How Work Sampling Works – part 1
Statistical Basis of Work Sampling – part 2
Application Issues in Work Sampling – part 3

## Slide 2: Work Sampling Defined
Statistical technique for determining the proportions of time spent by subjects in various defined categories of activity
Subjects = workers, machines
Categories of activity = setting up a machine, producing parts, idle, etc.
Work sampling study involves:
  large number of observations for subjects
  extended period of time
  finding proportion of time in each activity category based on proportion of observations in that category
Notes: ANSI Definition: “An application of random sampling techniques to the study of work activities so that the proportions of time devoted to different elements of work can be estimated with a given degree of statistical validity.”

## Slide 3: Work Sampling Defined
For statistical accuracy:
  Observations must be taken at random times
  Period of the study must be representative of types of activities performed by subjects
Work situations well-suited for work sampling:
  Sufficient time available to perform study (usually several weeks)
  Multiple subjects
  Long cycle times
  Non-repetitive work cycles
    i.e. various tasks (not just one task)
    work activities divided into categories

## Slide 4: Work Sampling Defined
When not to use Work Sampling
  highly repetitive jobs
    with short cycle times
    performed by one worker
  jobs requiring immediate measurement of task
  in such cases use other techniques (DTS, SDS, PMTS)
Other names used for work sampling:
  activity sampling
  occurrence sampling
  ratio delay study
  snap reading method* (reading assignment 1)
Notes: snap reading method*: by originator of method L. H. C. Tippett, since individual observations of the subjects are made quickly and without prior warning

## Slide 5: Work Sampling
How Work Sampling Works

## Slide 6: Work Sampling Applications
Machine utilization
  how much time is spent by machines in various categories of activity (e.g. 1)
  e.g. setup, production, downtime, etc.
Worker utilization
  how workers spend their time in various activities
Allowances for time standards
  assessment of delay components in PFD allowance factor
  e.g. delay components*: machine malfunctions, downtime, other interruptions
Notes: In fact, the name “ratio delay study” was used by Morrow for the technique because he saw this as the principal application

## Slide 7: Work Sampling Applications
Average unit time
  determining the average time on each work unit
  given: number of units produced during work sampling study
Time standards
  used in certain work situations (e.g. office work)
  note, work sampling provides limited statistical accuracy
     standards set by WS should not be used for incentive pay work

## Slide 8: Example 1: How Work Sampling Works
A total of 500 observations were taken at random times during a one-week period (40 hours) on 10 machines with results shown below.
Category No. of observations
(1) Being set up 75
(2) Running production 300
(3) Machine idle 125
500
How many hours per week did an average machine spend in each category?

## Slide 9: Example 1: Solution
Proportions of time determined as number of observations in each category divided by 500
Time in each category determined by multiplying proportion by total hours (40 hr)
Category Proportion Hrs per category
(1) Being set up 75/500 = 0.15 0.15 x 40 = 6
(2) Running production 300/500 = 0.60 0.60 x 40 = 24
(3) Machine idle 125/500 = 0.25 0.25 x 40 = 10
1.00 40